## Slide 1
Fiberhome Telecommunications Technology Experiences with
IBIS Models
Zheng Qi
Qzheng@fiberhome.com.cn

## Slide 2: Overview
IBIS Models have played an important role in signal integrity analysis
Access Buffer Characteristics
Waveform Quality Check
Timing Analysis

## Slide 3: Buffer Characteristics
What Information can we get ?
Use V-I Curves to calculate the driver output impedance
V-t Curve provides the Buffer’s transition time
C_comp provides intuitional info of the load

## Slide 4: Waveform Quality Check
Critical Net check
Edge Trigged Signals
Clocks
Check Contents
Incident Voltage
Edge Monotonic
High /Low noise margin
Source/sink currents

## Slide 5: Timing Analysis
Flight Time Calculating
Flight Time provides more reasonable descriptions than T.L Propagation Delay in Timing Budgets calculation
T.L Delay ,loads and topology effects are taken into consideration

## Slide 6: Mostly used model parameters
IBIS 1.0 V-I Curves
IBIS 1.0 C_comp
IBIS 2.1 rise/fall waveforms
IBIS 2.1 Pin mapping
IBIS 3.2 seldom
IBIS 4.0 seldom

## Slide 7: Model check
Typical Problems
Non-monotonic data in PU/PD table
DC point does not match I-V load line
V-t tables End slope not flat
…
Always tools will filter these points,but good
Understanding of these warning is necessary

## Slide 8: Successful stories
Multi-Drop bus Analysis
When debugging we found data was improperly strobed .Post analysis shows there is non-Monotonic Clock Edge. Using high bandwidth probe check again and got it
Timing Analysis
Strong Driver results in Hold time conflict
Occurs at “Low Speed” situation

## Slide 9: Behind these stories
IBIS models provides some clues in Waveform
Quality check. But
How Simulator processes the model is a black box
Simulated result sometimes are tools relevant

## Slide 10: Behind these stories
Timing Analysis
Different Driver strength results in great different Delay
Under low speed situation Timing analysis was proven and the IBIS model works well
IBIS model can’t describe the internal delay of the buffer . when doing timing analysis we always puzzle about the “Zero” reference point . especially when timing budgets is tight
Closing the Timing loop requires Core-to-core timing

## Slide 11: Problems
High Speed Serial Interconnect have widely used . But effective analysis was lagged
Find Bugs of Serial Interconnect is more difficult than old designs . Maybe it is an impossible task

## Slide 12: We are expecting
Model Maker
End User
Tools Vendor
Third Tools