## Slide 1: Adding On-Chip Capacitance in IBIS Format for SSO Simulation
Raymond Y. Chen
SIGRITY, Inc.

## Slide 2: Agenda
Is IBIS good for SSO simulation
SSO simulation flow using IBIS
Improve SSO simulation accuracy by adding Cdie for on-chip power/ground parasitics
Further discussion

## Slide 3: Can IBIS Model SSO (From Official IBIS FAQ)

## Slide 4: Examine IBIS Model of Device, IC Package and PCB for SSO Simulation
Lumped IC package model and PCB model (EBD) in an IBIS file are for rough SSO estimation since semiconductor company usually will not give out details on their package and modules. For real world high speed system design, geometry based EM field solvers are must for package + PCB system level simulation including SSO.
IBIS is developed for device modeling, as a behavioral model, it can be used for, and actually is good for SSO simulation, provided if a few IBIS parameters can correlate well with original SPICE transistor model (next slide).
SSO simulation must include many non-linear devices in one simulation run. IBIS has the natural speed advantage over SPICE transistor level model, therefore, SSO is a very good Signal Integrity (SI) application for IBIS.

## Slide 5: Examine IBIS for Device Model in SSO Simulation
Ipwr
Ignd
Isig
+
Vout
_
The pull-up and pull-down currents of an IBIS model must have the accuracy close to the transistor level model for proper SSO simulation, because most system level noise voltage are due to these currents flowing through the signal and power distribution system.
Ignd
Isig
Blue line: IBIS Green line: Transistor

## Slide 6: A Sample SSO Simulation Flow Using IBIS – DDR + Motherboard
Prepare DDR model in PowerSI
  Define ports depending on nets of interest
  Extract S paramter of the DDR module
  Convert S parameter data to SPICE subcircuit with Broadband Spice
Prepare Motherboard model in Speed2000
  Connect voltage sources for +2.5V and Vtt rails; verify capacitor models
  Connect Northbridge driver models and termination resistors for DDR nets
Connect the DDR module subcircuit, chip loads, and connector models in Speed2000
Use Speed2000 to analyze the complete system

## Slide 7: Circuit Linkage Block Diagram
DIMM 1
DDR Model Definition
DDR Module
SPICE Deck
Subcircuit
Connector
Model
Subcircuit
(ex. IBIS)
DDR
Device
Subcircuit
(ex. IBIS)
DIMM 2
DDR
Device
Subcircuit
(ex. IBIS)
M
O
T
H
E
R
B
O
A
R
D

## Slide 8: Prepare DDR Module for Extraction in PowerSI
Read in DDR layout.
Define power / ground ports on the top and bottom of the edge connector and at the active devices. Define ports for signals for SSO. For example, DQ16, DQ17, DQ18, DQ19, DQS2, DQ24, DQ25, DQ26, and DQS3. Ports are defined at the edge connector and at the device pins for these signal nets (two ports per signal net).
Set the appropriate frequency sweep parameters and extract the S parameter information for the module. Then covert S parameters to SPICE circuit using Broadband SPICE.
.SUBCKT DDR_module_model
+ n1 n2 n3 n4 n5 n6 n7 n8
+ n9 n10 n11 n12 n13 n14 n15
+ n16 n17 n18 n19 n20 n21 n22 ref
Rd1_1 n23 ref 50.000000
Rd1_2 n24 ref 1
Vd1 n1 n23 0
F1 ref n24 Vd1 1.0
G1 ref n24 n1 ref 0.02
Rd2_1 n25 ref 50.000000
....

## Slide 9: Prepare Motherboard in Speed2000
Connect Northbridge driver and package
model for write cycle analysis.
(IBIS model for the drivers are used in this example.)
Verify decoupling capacitors and
termination resistor linkages.
Connect voltage sources for +2.5V (yellow)
and Vtt (orange) rails.

## Slide 10: Connect the Subcircuits
The automatic IBIS linkage feature was used to connect the Northbridge IBIS drivers.
Pin mapping section must be complete before using automatic IBIS connection feature.
A few IBIS driver definitions are shown here.
With the automatic IBIS feature, numerous SSO simulations are possible: even / odd mode, stuck high, stuck low, and variable number of drivers / aggressors.
After the Northbridge driver is defined, add circuit voltage views for all waveforms of interest (receiver waveforms, power / ground bounce, etc.).

## Slide 11: SSO Simulation Results
Local Power Ground Noise at Die-Pad
Victim Signal Stuck Low
At Receiver End
Victim Signal Stuck High
At Receiver End
One of the Active SSO Signals at Receiver End
Digital Trigger with Certain Bit Pattern

## Slide 12: Why We Need Cdie
We have C_comp in IBIS, but we don’t have the parasitics between pull-up and pull-down for the on-chip power distribution.
Cdie will affect SSO noise at die pad and at system level.
Without Cdie, IBIS based SSO results sometimes are more pessimistic than SPICE model.
nd_pu
nd_pd
nd_pc
nd_gc
nd_out
gnd
Package
R_pkg
L_pkg
C_pkg
gnd
C_comp
nd_in
nd_pc
nd_gc
gnd
Package
R_pkg
L_pkg
C_pkg
gnd
C_comp
INPUT BUFFER
OUTPUT BUFFER

## Slide 13: After Adding Cdie
Driver end waveform will be more accurate.
Noise simulation will be more accurate, for example, power and ground noises at die pad.
System includes signals, power and ground for package and PCB
nd_pu
nd_pd
nd_pc
nd_gc
Cdie
gnd
C_comp
OUTPUT BUFFER
VRM, DC/DC
Termination
Receiving end device

## Slide 14: After Adding Cdie
With a few nF Cdie, driver end waveform at die pad shows less ripple.

## Slide 15: After Adding Cdie
With a few nF Cdie, victim line (stuck low) at the board receiver end shows less noise.

## Slide 16: Further Discussion
Lumped Cdie model is good for improving IBIS based system level SSO simulation.
Adding lumped Rdie in series with Cdie can further improve simulation accuracy.
For very accurate simulation of die pad noises, distributed on-chip power ground model is necessary, plus broadband EM models for IC package and PCB.
G
P
Power
Distributed model for on-chip power and ground system is important to predict noises at each die pad, whereas lumped Cdie will fail. Adding good on-chip power ground model in system level simulation requires new tools.