## Slide 1
IBIS QUALITY
DESIGNCON IBIS SUMMIT Feb 2, 2004
Robert Haller
rhaller@sisoft.com
Signal Integrity Software, Inc.
6 Clock Tower Place – Suite 250
Maynard MA. 01754
978-461-0449 X 15

## Slide 2: IBIS Quality (IQ) Subcommittee
Goals
  Rating system that is easy to understand and adopt
  Communicate to vendors/users.
  Cover overall file, component, and model sections
  Check for completeness, correctness, accuracy
  Leverage of prior work Meet every 2 weeks (Tuesdays 9:00 EDT for 1 hour)
Mailing list
  Ibis-quality@freelists.org
  http://www.freelists.org/archives/ibis-quality
Web Site
  http://www.sisoft.com/ibis-quality

## Slide 3: IQ Document Available
http://www.sisoft.com/ibis-quality/docs
IQ_Document.txt
Notes: Why are we here today

## Slide 4: IQ Document Index
1.0 IBIS Quality Summary
1.1 IBIS Quality level definitions
1.2 IBIS Quality summary as comments in file
2.0 General Header Section Requirements
3.0 Component Section
3.1 Component Package Requirements
3.2 Component Pin Requirements
3.3 Component Diff Pin Requirements
3.4 Component Model Selector Requirements
Notes: Why are we here today

## Slide 5: IQ Document Index
4.0 Model Section
4.1 Model General Requirements
4.2 Model Waveform Processing Requirements
4.3 Model I-V Table Requirements
4.4 Model V-T Table Requirements
4.5 Model Ramp Data Requirements
5.0 Possible Errors that should be checked
6.0 Correlation
6.1 SPICE correlation
6.2 Lab correlation
7.0 Model Limitations
Notes: Why are we here today

## Slide 6: IQ Document Sample
3.1 Component Package Requirements
Requirements for the [Package] and [Package Model] sections:
3.1.1 {LEVEL 0} [Package] must have typical values
Typical values must be defined on a component. Min/Max optional but must be defined as NA if not available.
3.1.2 {LEVEL 0} [Package] Parasitics must be reasonable
Reasonable values are: L < 10nH, C < 20pF, R < 1 ohm
Min must be less than typ and typ less than max
Notes: Why are we here today

## Slide 7: IQ Document Levels
Level 0 requirements
Level 0 requirements can be checked by ibischk3 version 3.2.9 or later software. Use of ibischk3 is highly recommended, to avoid performing level 0 checks manually…
Level 1 requirements
Level 1 includes all items in level 0, plus checks for correctness and completeness, and basic simulation tests…
Level 2a requirements
Level 2a includes all items in level 1, plus simulation correlation:
- Spice Correlation.
- Cross reference IBIS Accuracy figure of merit (FOM)
…
Notes: Why are we here today

## Slide 8: Summary
IBIS Quality Subcommittee Goals
IBIS Quality Documentation Available !
  http://www.sisoft.com/ibis-quality/docs
IQ Index
IQ Sample Documentation presented
IQ Levels