## Slide 1: Creating IBIS Models for Stacked-Die Packages
Steve Peterson
Intel Corporation
steve.peterson@intel.com
02-Feb-04

## Slide 2: Problem Statement
Intel sells memory with several devices stacked inside a single package
We receive bare die from several vendors
  We receive IBIS models but no schematics
Customers require IBIS models for new stacked-die package

## Slide 3: Solution
Use internal schematics plus vendor IBIS models to create a new netlist
Simulate to generate IV and VT curves for new IBIS model
IBIS Model
Data
EnableA
EnableB

## Slide 4: Methodology
Generate two sets of IV and VT curves
  Device A is active while device B is tri-stated
  Repeat with device B active and A tri-stated
Build new IBIS model using both curves
  Assign D[0] to A active (with B tri-stated)
  Assign D[7:1] to B active (with A tri-stated)
Edit IBIS model to add model_selector
  Change D[7:0] to use model_selector
  Requires IBIS version 3.2 or higher

## Slide 5: Data Bus Example
BEFORE
[IBIS Ver] 2.1
...
[Pin] signal_name model_name
B1 DQ0 Ab_output
B2 DQ1 Ba_output
B3 DQ2 Ba_output
B4 DQ3 Ba_output
AFTER
[IBIS Ver] 3.2
...
[Pin] signal_name model_name
B1 DQ0 DQ
B2 DQ1 DQ
B3 DQ2 DQ
B4 DQ3 DQ
...
[Model Selector] DQ
Ab_output Device A DQ
Ba_output Device B DQ
At least one instance of each buffer
Manually add
Model Selector

## Slide 6: Ground Clamp Comparison
New IBIS model reflects behavior of both die
Device A ground clamp (-130mA)
Device B ground clamp (-195mA)
Combined ground clamp (-325mA)

## Slide 7: AC Timing Comparison
Original (single-die) pullup_on for device A
Combined curve showing additional loading from device B
Original device B
Combined device B

## Slide 8: Conclusion
This document describes a methodology of generating a multi-die IBIS model from transistor netlists plus IBIS models
Effects of multiple loads are accounted for
  Power clamps for all devices are combined
  Vt behavior accounts for additional loading
Package parasitics can be handled using worst case loading or EBD format