## Slide 1: [Driver Schedule] Model Initialization
Bob Ross
DesignCon IBIS Summit Meeting
Santa Clara, California
February 2, 2004

## Slide 2: My (stated/unstated) Driver Schedule Assumptions (in BIRD35.3)
Under [Model], the model assumptions must prevail
  Works for single transition and one cycle (Rising and Falling)
  FULL CYCLE for [Driver Schedule]
    Rise_on_dly Rise_off_dly Fall_on_dly Fall_off_dly
    x1 or NA x2 or NA x3 or NA x4 or NA
    Full cycle => down-up (d-u), (u-d), (d-u-d-u), (u-d-u-d) sequencing for “slow” clock (no over-clocking considered or allowed)
    16 possibilities, but 5 [x || NA] table variations with 8 total variations considering numerical ordering, finite durations
  Follows top-level [Model] “Polarity” Non-Inverting and Inverting modes (“phasing”) in transparent manner
  Everything is relative to Rise or Fall edges of “Master Clock”
Therefore known initial state (High or Low) allowing single switch and one cycle simulation

## Slide 3: Initial States (should be implemented for full capability)
R_on R_off F_on F_off Non-Invert Inverting
xr NA xf NA Low High
NA xr NA xf High Low
x1 x2 NA NA Low Low
x2 x1 NA NA High High
NA NA x1 x2 High High
NA NA x2 x1 Low Low
xr1 xr2 xf2 xf1 Low Low
xr2 xr1 xf1 xf2 High High

## Slide 4: Illegal Cases
R_on R_off F_on F_off Reason
NA NA NA NA unknown initial state
xr NA NA xf u-u sequencing
NA xr xf NA d-d sequencing
xr1 xr2 xf1 xf2 u-d-d-u sequencing
xr2 xr1 xf2 xf1 d-u-u-d sequencing
And just 1 or 3 numerical entries (sequencing)