## Slide 1: Verification of IBIS models
Hans Klos
Hans.Klos@Sintecs.nl
Sintecs BV
Lansinkesweg 4
7553 AE Hengelo
The Netherlands

## Slide 2: Agenda
Introduction
Where to get IBIS models
How to verify IBIS models
Adding additional information
Roadmap IBIS Development Studio

## Slide 3: Where to get IBIS models
Download from internet
  Not always latest version on internet
Contact component vendor(s)
Create models from spice data
Create models by measurement

## Slide 4: How to verify IBIS models
IBIS golden parser
Visual verification
Test IBIS model in simulator
Compare IBIS model with measurement data

## Slide 5: IBIS Golden parser
IBISCHK
  Is a program that parses the model file to verify that the file conforms to the IBIS specification. It is free, publically available executable code developed by contractors for the IBIS Open Forum.
  The official ibischk4 checks Version 1.1, 2.1, 3.2 and 4.0 level IBIS files. (Use -ebd and -pkg flags for .ebd and .pkg files.)

## Slide 6: Visual verification
To verify an IBIS model, a graphical view of the waveform(s) makes it easier
In a graphical viewer of the IBIS models, the potential problems can be found easier.
Free tools are available for visual verification of an IBIS model.
    IBIS Development Studio
    Visual IBIS editor

## Slide 7: Graphical Viewer

## Slide 8: Graphical view of I/V tables

## Slide 9: Combine waveforms

## Slide 10: Modify waveform
Modify waveform in the ASCII file is difficult.
It is easier to move points graphically
Graphical editing functionality needed

## Slide 11: Test IBIS model in simulator
After graphical verification, the IBIS model must be tested in the simulator where you are going to use the IBIS model.
Run the model with the standard test loads.
Comparing the results against a transistor-level reference simulation using the same loads.

## Slide 12: Compare IBIS model with measurement data
The last step in the modeling process is to correlate the simulation results with actual silicon measurements.
Correlation involves measuring the I-V curves and rise/fall times of an actual IC and verifying that they fall within the maximum and minimum values used in the IBIS model. (In addition, for ICs in a motherboard or other test setup driving a known load, compare the oscilloscope waveforms with simulation waveforms using the same load.)

## Slide 13: Adding additional info
A IBIS model is the best place to define constraints needed for the SI simulator :
  S_overshoot_high Static overshoot high voltage
  S_overshoot_low Static overshoot low voltage
  D_overshoot_high Dynamic overshoot high voltage
  D_overshoot_low Dynamic overshoot low voltage
  D_overshoot_time Dynamic overshoot time
  Vmeas Measurement voltage for timing

## Slide 14: Constraints in IBIS
Most SI simulators uses a constraint spreadsheet for defining constraints.
Constraints for under-/over-shoot should come from the IBIS model.
Most IBIS models does not contain this information.
This information can be found in the datasheet, or contact the component vendor.

## Slide 15: Roadmap IBIS Development Studio
Test model in simulator (ICX / ePlanner / Hyperlynx / simulators) within IBISDS
Enhanced features for model wizard
XML output of IBIS model
Other improvements suggested by IBISDS users (ibisds@edality.com)
For more info, visit us at http://www.edality.com