## Slide 1: IBIS, current status (4.1) and some notes on IBIS4.0 parameters
Eckhard Lenski

## Slide 2: Overview
IBIS, current status (4.1) and some notes on IBIS4.0 parameters
current status
questions
new tools
parameters
statements

## Slide 3: IBIS 4.1
Current status
IBIS 4.1
Includes now external models:
VHDL AMS
Verilog AMS
SPICE ( 3F5 )

## Slide 4: New Keywords
Current status
Keywords
Uses connectivity and IBIS-Parameters
like VinH, VinL from [Model] Keyword
Connectivity and
measurement parameters are
defined inside ‚external circuit‘
( e.g. Inputs with 4 Thresholds )
[External Circuit]
[End External Circuit]
[Node Declarations]
[End Node Declarations]
[Circuit Call]
[End Circuit Call]
[External Model]
[End External Model]

## Slide 5: New model types
Current status
4 new model types
I/O_diff
Output_diff
3-state_diff
Input_diff
2 new sub parameters
Rref_diff
Cref_diff
clarifications of many keyword descriptions

## Slide 6: A living standard
Current status

## Slide 7: ICM
Current status
Not frequency dependent, -> next version
ICM v1.0 IBIS InterConnect Modeling Specification
Conductance added as a parameter
S-Parameters
Touchstone Format
Coupling per section possible

## Slide 8: New free tools on the IBIS homepage
New tools
s2ibis3
Ibischeck 4.0
Java
series MOSFETs
better convergence with HSPICE
Check the file depending on the version in the keyword
[IBIS Ver] 4.0
Monotonicity of V-I-tables
ver 4.0 : with summation of V-I-tables
ver 3.2 : without summation (each table alone )

## Slide 9: IBIS4.0 parameters explained
parameters
Vth, Vth-min, Vth-max
Sub-Params: Vth, Vth_min, Vth_max,
Keyword: [Receiver Thresholds]
Receiver thresholds differential
Vcross_low, Vcross_high, Vdiff_ac, Vdiff_dc,
Tslew_ac, Tdiffslew_ac
Receiver thresholds single ended
Threshold_sensitivity, Reference_supply,
Vinh_ac, Vinh_dc, Vinl_ac, Vinl_dc,

## Slide 10: New Receiver thresholds
VinL_ac, VinL_dc is offset to Vth , no min max values
parameters
Vcross_low, vcross_high is referenced to gnd,
no min max values
Vth has got reference supply, with min max values
Vdiff_ac, Vdiff_dc , no min max values
VinH_ac, VinH_dc is offset to Vth , no min max values
Reference_supply for Vth
Threshold_sensitivity dependent on reference supply

## Slide 11: Single ended parameters
parameters
VinH_dc
Vth
VinH_ac
Vcc
time
Voltage
VinH_ac : during a transition from L -> H,
input will state change,
when crossing Vinh_ac
VinH_dc : after a transition from L -> H,
input will not change the new state,
if above Vinh_dc

## Slide 12: differential parameters
parameters
Vcross_low
Vcross_high
Vddq/2
Vddq/2 + 0.175V
Vddq/2 - 0.175V
t
u
t
u
0.25V
0.5V
0V
Differential signal:
Vdiff_dc
Vdiff_ac
t
u
In-pos
In-neg
0V

## Slide 13: Threshold voltage Vth
Vth is for typical values only
parameters
These will be calculated using the equation
No explicit values for min-max-condition Models
Vth_min, Vth_max are values for typical conditions
Vth(min/max) =
Vth + ( Threshold sensitivity X change in supply voltage )

## Slide 14: Threshold example part 1
Vcc 3.3V 3.0V 3.6V
Vth 1.65V 1.5V 1.8V
Threshold sense = ( VthMAX-VthMIN ) / ( VsupplyMAX-VsupplyMIN )
= ( 1.8V – 1.5V ) / ( 3.6V –3.0V ) = ( 0.3V ) / ( 0.6V )
= 0.5
Vth and threshold sense must come
from the IC-Manufacturer
parameters

## Slide 15: Threshold example part 2
parameters
Typ Min Max
Vth 1.5v VthMIN xxx VthMAX yyy
Vthmin 1.45v VthMINmin xx VthMAXmin yy
Vthmax 1.53v VthMINmax x VthMAXmax y
Threshold sensitivity 0.45
Ref. Supply Power clamp reference
Powerclamp 3.3V 3.15V 3.45V

## Slide 16: Threshold example part 3 calculation
parameters
typ
min
max
Vth
1,5
VthMIN
1,35
VthMAX
1,65
Vthmin
1,45
VthMINmin
1,3
VthMAXmin
1,6
Vthmax
1,53
VthMINmax
1,38
VthMAXmax
1,68
Thres sense
1
Ref. Supply
Power clamp reference
Powerclamp
3,3
3,15
3,45
VthMINtyp
= Vthtyp +
1 *
( 3.15V -3.3V )
1.35V
VthMAXtyp
= Vthtyp +
1 *
(3.45V - 3.3V )
1.65V
VthMINmin
= Vthmin +
1 *
( 3.15V -3.3V )
1.30V
VthMINmax
= Vthmax +
1 *
(3.15V - 3.3V )
1.38V
VthMAXmin
= Vthmin +
1 *
( 3.45V -3.3V )
1.60V
Vthmaxmax
= Vthmax +
1 *
(3.45V - 3.3V )
1.68V
typ
min
max
Vth
1,5
VthMIN
1,4325
VthMAX
1,5675
Vthmin
1,45
VthMINmin
1,3825
VthMAXmin
1,5175
Vthmax
1,53
VthMINmax
1,4625
VthMAXmax
1,5975
Thres sense
0,45
Ref. Supply
Power clamp reference
Powerclamp
3,3
3,15
3,45
VthMINtyp
= Vthtyp +
0.45 *
( 3.15V -3.3V )
1.4325V
VthMAXtyp
= Vthtyp +
0.45 *
(3.45V - 3.3V )
1.5675V
VthMINmin
= Vthmin +
0.45 *
( 3.15V -3.3V )
1.3925V
VthMINmax
= Vthmax +
0.45 *
(3.15V - 3.3V )
1.4625V
VthMAXmin
= Vthmin +
0.45 *
( 3.45V -3.3V )
1.5175V
Vthmaxmax
= Vthmax +
0.45 *
(3.45V - 3.3V )
1.5975V

## Slide 17: Threshold example part 4 graph
parameters
Threshold
sensitivity
0.45
1
VthMAXtyp
VthMAXmax
VthMAXmin
VthMINtyp
VthMINmax
VthMINmin
VthTYPtyp
VthTYPmax
VthTYPmin

## Slide 18: Questions and statements
Few new members in IBIS
statements
Gurus and beginners
IBIS 4.1 contains now 140 pages
ICM contains 50 pages
E-roadshows for training & interactions

## Slide 19: Increasing issues
Number of IO-models per file
statements
Gap between current version of IBIS and models you get
Number of parameters
Information needed, which tool uses which parameters

## Slide 20: IBIS is a standard ANSI/EIA 656-A
Model availabilty
Model quality
Good accuracy with short simulation time
Tool independent
Past Today Future
statements

## Slide 21: PVT : Process, Voltage, Temperature
question
Model class δVcc Tj Process
1 ± 5% 0 – 110 ± 2σ
2 ± 5% 0 – 110 ± 3σ
3 ± 5% m40 – 125 ± 2σ
4 ± 5% m40 – 125 ± 3σ
5 ± 10% 0 – 110 ± 2σ
6 ± 10% 0 – 110 ± 3σ
7 ± 10% m40 – 125 ± 2σ
8 ± 10% m40 – 125 ± 3σ
± 2σ means 95,5% of all shipped parts fulfill these limits
± 3σ means 99,7% of all shipped parts fulfill these limits
δVcc ± 5% means e.g. 3P3V -- 3P15V -- 3P45V
δVcc ± 10% means e.g. 3P3V -- 3P00V -- 3P60V

## Slide 22: Questions to IBIS4.1
VHDL-AMS model support
SPICE 3F5
How to check ?
- visual
- syntax
- ???
- How to translate to other SPICE-tools ?
- encrypted SPICE ?
question

## Slide 23: Final
E-roadshows sounds good
IC vendors must support new parameters faster
Acceptance of new IBIS-versions must be higher
More graphical explanations of parameters
Tool vendors must support new parameters faster