## Slide 1: The Benefits of Multi-Lingual Extensions to IBIS
Stéphane Rousseau
PCB European Product Specialist

## Slide 2: Agenda
Simulation Limitations
Advanced Modeling Capabilities
Modeling Alternatives:
  Altera Stratix GX High-Speed Serial Interface (HSSI)
Conclusions

## Slide 3: Simulation Limitations
Model availability remains an issue
  Proprietary models and languages limit industry mass adoption
IBIS has major limitations; customers can’t use it exclusively
  Non-extensible syntax
  Unable to model today’s buffer technology
    Adaptive drivers and receivers
  Limitations in modeling power supply dynamics
SPICE has issues as well
  Too slow for analyzing entire design!!
  Models often encrypted to proprietary formats
  Vendors reluctant to provide the IP often found in SPICE models
Additional engine limitations exist

## Slide 4: Advanced Modeling Capability
Allow customers to use models in any possible industry standard format
  There are different model formats and languages in use today for high-speed design
    IBIS
    SPICE
      HSPICE, Eldo, PSpice, …
    VHDL-AMS (IC level)
By providing support for more than one, improve probability of finding a model
Use the right model for the job at hand

## Slide 5: Extensions to IBIS
Allow IBIS models to reference external models through keywords
  Standard language extensions
    SPICE
    VHDL-AMS
  IBIS extensions
      [External Model]
      [External Circuit]
      [Circuit Call]
      [Node Declaration]

## Slide 6: I/O Buffer Examples
IBIS only
IBIS Parasitics with SPICE Buffer
SPICE Parasitics with VHDL-AMS buffer
IBIS Model
PIN
Component
Pin
Composite Model
SPICE
Buffer
Model
PIN
Component
Pin
Composite Model
SPICE Package
Model
VHDL-AMS
Buffer
Model
PIN
Component
Pin

## Slide 7: Multi-Lingual Simulation
Mix and match driver model formats on a single net
entity ibis_tx_cmos is
generic (
c_comp:real:=7.0e-12;
vpudata:real_vector:=( -5.250000e+00, … ,7.500000e+00);
ipudata:real_vector:=( 3.555770e-01, … ,-1.356870e-01);
… same for vpd, ipd, vpc,ipc, vgc, igc
VHDL-AMS
R_I$277 VCC out1 1.55K
C_I$272 ibias N$238 28.3P
M_I$46 N$240 ibias 0 0 NFET L=1.52U W=7.85U M=40
M_I$283 out2 out2b VCC VCC PFET L=0.5U W=4U M=1
.MODEL NFET NMOS (RSH=17 KP=1.34M
+ GAMMA=0.919 PHI=0.707 LAMBDA=0.1M RD=52.88
+ RS=52.55 CBD=4.79P CBS=5.73P PB=1
+ CGSO=3.17P CGDO=2.04P CGBO=4.01P MJ=0.189 )
...
SPICE
[IBIS Ver] 3.2 [File name] sample.ibs [File Rev] 0.0 [Date] August 31, 2002 [Source] Data Book [Notes] Default model for source. [Disclaimer] This information is modeling only
|***************************************
[Component] Driver [Manufacturer] Generic [Package] | typ min max R_pkg 0 NA NA L_pkg 5.0nH NA NA C_pkg 2.0pF NA NA
IBIS

## Slide 8: Modeling Alternatives: Starting Point
<number>
The Benefits of Multi-Lingual Extensions to IBIS
DATE IBIS Summit 2004
Altera Stratix GX High-Speed Serial Interface (HSSI)
  SPICE transistor level model
  Single circuit for transceiver
  Selectable parameters for Driver pre-emphasis levels, Driver output voltage amplitude, Driver impedance, Receiver equalization level, Receiver impedance, Trace length and loss
3” lossy differential pair trace model from driver pins to receiver pins
Circuit as delivered took 21 minutes (real time) to simulate in Eldo (SPICE)

## Slide 9: Original Transceiver Model
<number>
The Benefits of Multi-Lingual Extensions to IBIS
DATE IBIS Summit 2004
Multi-page schematic created with SpiceVision PRO from Concept Engineering
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Issues with SPICE Models
Can’t simulate Driver separate from receiver
  Probably simulating extra nodes that are irrelevant
Subcircuits encrypted (Eldo)
Global nodes (.global in SPICE)
  Possible conflict with models from another source
Scale option = 1u
  Another possible conflict with other models
* These are common issues with SPICE models *

## Slide 11: Transceiver Model Reduction
Driver and Receiver sections separated
  Allows instantiation of driver and receiver IBIS 4.1 models on separate parts for design verification
Driver section reduced
  Data and pre-emphasis signal generation simplified with controlled-source logic
Simulation time reduced to 12 minutes real time – 57% of original time
Driver simplified

## Slide 12: Package Model
Complex package model
  3 differential pairs fully coupled
  3 cascaded sections
bump
BGA
trace
ball

## Slide 13: Package Model Reduction
Element elimination
Simple IBIS RLC parameters
S-parameter model

## Slide 14: Package Model Element Elimination
bump
BGA
trace
ball
Reduced simulation time by about 10%
Changed results beyond acceptable error
bump
BGA
trace
ball

## Slide 15: Simple IBIS RLC Parameters
Can’t be more accurate than reduced element model
Should provide much faster simulation time
Reduced simulation time by 25%
Reduced overshoot
  Assumed impedance of 50 Ohms was better than original SPICE model
L = Td * Z
C = Td / Z
Td measured from original simulation is 83ps (Tr ~ 200ps)
Assume Z0 is 50
L = 4.15nH
C = 1.66pF

## Slide 16: S-parameter Package Model
S-parameter set created by SPICE simulation of original package model
  Frequency steps of 100MHz from 100MHz up to 10GHz
Simulation time reduced by 25% from full package model simulation
S-parameters have other issues
  Usually no DC information
  Possible non-causal or non-passive results
S-param
SPICE

## Slide 17: Behavioral Modeling
Functionality and accuracy must be maintained!
Majority of simulation time is spent solving the 1000’s of nodes in the transistor level transmitter and receiver models
This time could be greatly reduced by using behavioral models such as VHDL-AMS

## Slide 18: VHDL-AMS Model Correlation
Parameterized model adjusted to match SPICE simulation of driver without pre-emphasis

## Slide 19: VHDL-AMS Model Functionality
Model adjusted to match voltage swing and pre-emphasis functions

## Slide 20: Signal Comparison at the Receiver
Simulation correlation is most important at the receiver. Eye diagrams show little difference caused by package models with the VHDL-AMS buffer models
SPICE
package
S-param
package

## Slide 21: Simulation Time Reduction

## Slide 22: Conclusions
The SPICE model can be reduced to save simulation time
The package model can be translated to other formats to save some simulation time, but doesn’t justify the change in results.
Using a behavioral model of the driver and receiver drastically decreases simulation time to less than 1/10 and maintains fidelity to the original results
Extensions to IBIS and Multi-Lingual Simulator provide flexibility and performance