## Slide 1: Parametric Models in IBIS Multilingual Framework
F.G.Canavero1, I.A.Maio1, B. Ross 2, I.S.Stievano1
1 Politecnico di Torino, Italy, 2 Teraspeed Consulting Group LLC (USA)
igor.stievano@polito.it
http://www.eln.polito.it/research/emc

## Slide 2: Introduction (i)
IBIS Implementation of I/O buffer Parametric Models for High-Performance SI and EMC simulations
Improved modeling of latest technologies and high-order effects
  LVDS drivers with pre-emphasis,
  DDR memories,
  Power supply ports, etc …

## Slide 3: Introduction (ii)
Available applications:
  Macromodels of I/O ports
  Inclusion of slowly-varying device parameters (eg, temperature)
  Inclusion of the power-supply voltage variation
  Models of the power supply port
  Models of tristate drivers
  Models of LVDS devices
Mlog - Macromodeling via parametric
identification () of LOgic Gates
T
vdd
enable
INPUT PORT (REC)
OUTPUT
PORT (DRV)
Single-ended
CMOS
[I.S.Stievano, I.A.Maio, F.G.Canavero, “Mlog, Macromodeling via Parametric Identification of Logic Gates,” Trans. Of Adv. Pack., 2003 (in press)]
[I.S.Stievano, C.Siviero, I.A.Maio, F.G.Canavero, “Modeling of the Static and Dynamic Behavior of Differential Drivers,” Proc. of EMC-Compo 2004]

## Slide 4: Mlog review (i)
A mathematical expression reproducing the electrical behavior of the device
What is it ?
IC
i(t)
v(t)
i(t)
v(t)
F
i=F(v, d/dt)
Nonlinear dynamic relationship
Mlog - Macromodeling via parametric
identification () of LOgic Gates

## Slide 5: Mlog review (ii)
Real Device (or its physical model)
is conveniently stimulated
Reaction (port transient responses)
is used to build the model
IC
stimulus
reaction
How does it work ?

## Slide 6: Mlog: what is the output ?
Model structure: F is a  nonlinear Basis Functions (various types)
i = -a1 tanh{c1 v + b1} + a2 tanh{c2 dv/dt + b2}
e.g.,
unknown parameters: amplitude, position, spreading
(1)
(2)
(1)
(2)

## Slide 7: Mlog: implementation
i = -a1 tanh{c1 v + b1} + a2 tanh{c2 dv/dt + b2}
F.cir
x
i1(v)
i2(x)
v
i
v
(a) CIRCUIT INTERPRETATION & SPICE IMPLEMENTATION
i1
i2
(b) DIRECT EQUATION DESCRIPTION/IMPLEMENTATION:
VHDL-AMS and IBIS Multilingual Extension
for ICX Ver. 3.2 simulator

## Slide 8: IBIS Multilingual Extension
[IBIS Ver] 4.0
[File name] driver_test.ibs
[File Rev] 0.0
[Date] 28/01/2004
|***************************************************************************
[Component] DRIVER
[Manufacturer] Polito
[Package] …
…
[Pin] signal_name model_name R_pin L_pin C_pin
1 vout MODEL_PAR
|***************************************************************************
|
[Model] MODEL_PAR
Model_type Output
Polarity Non-Inverting
…
[External Model]
Language VHDL-AMS
|
| corner_name file_name circuit_name
Corner Typ driverX.vhd driverX(bufferbehav)
|
| d_control a_signal
Ports D_control A_signal
|
[End External Model]
Driver_test.ibs
NOTE: some example syntax details differ slightly from the approved IBIS Version 4.1 specification
D_control
A_signal

## Slide 9: VHDL-AMS Model Implementation (i)
Digital
to analog conversion
entity driverX is
generic (
Ts: real := …
port(
d_control : in std_logic;
terminal a_signal : electrical);
end entity driverX;
architecture bufferbehav of driverX is
quantity Vu_ref across i through a_signal
to Electrical_ref;
…
--- w1_01 low to high transition
constant w1_01 : real_vector := …
InputBITSTR: process (d_control)
begin
if (d_control'event and d_control = '0') then
flag <= 10;
trans_inst <= now;
elsif (d_control'event and d_control = '1') then
flag <= 01;
trans_inst <= now;
end if;
end process InputBITSTR;
…
driverX.vhd
1

## Slide 10: VHDL-AMS Model Implementation (ii)
Analog parametric model
…
…
…
if (d_control = '0' and flag = 10) use
w1 == Lookup("Vt", now-trans_inst, w1_10, tw);
w2 == Lookup("Vt", now-trans_inst, w2_01, tw);
elsif (d_control = '1' and flag = 01) use
w1 == Lookup("Vt", now-trans_inst, w1_01, tw);
w2 == Lookup("Vt", now-trans_inst, w2_10, tw);
end use;
end architecture bufferbehav;
driverX.vhd
f1 == -a1*(2/(1+exp(-2*c1*Vu_ref +…) –1) + …
f2 == …
i == w1*f1 + w2*f2
2
i = w1(t)f1 (v,dv/dt) +
+ w2(t)f2 (v,dv/dt)
Example representation for
CMOS single ended drivers

## Slide 11
DEVICE
Example 1 (i)
PARAMETRIC
MODEL
TEST CIRCUIT
Z0=50.19 
TD=0.72 ns
1 (2) basis functions for f1 (f2) and and dynamic order 1
High-speed IBM CMOS Driver (Vdd=1.8V)
1
2
[I.S.Stievano et Al., “Parametric Macromodels of Drivers for SSN Simulations,” Proc. of IEEE International Symposium on EMC, Boston, MA, USA, Aug. 18-22, 2003]
1pF

## Slide 12
Example 1 (ii)
40 ns
2 V
1
2
simulation: ICX
1
2
Driver_test.ibs

## Slide 13
Example 1 (iii)
Comparison of
Driver_test.ibs
Driver_test.cir
&
(ICX)
(PSPICE)
Driver_test.ibs
Driver_test.cir

## Slide 14
Example 2 (i)
[I.S.Stievano, C.Siviero, I.A.Maio, F.G.Canavero, “Modeling of the Static and Dynamic Behavior of Differential Drivers,” Proc. of EMC-Compo 2004, Mar. 31 – Apr. 1, 2004]
Fairchild FIN1001 (Vdd=3.3V) LVDS
High Speed Differential Driver
DEVICE
PARAMETRIC
MODEL
TEST CIRCUIT
100  diff.
resistor
coupled line structure
stripline
3 ns delay
4 vias
128 bit stream
1 ns bit time
200 ps uniform
jitter
Macromodel details and validation in

## Slide 15
ICX Application: Eye diagram
Example 2 (ii)
600 mV
v
v
1ns

## Slide 16: Conclusions
Parametric models are well suited to IBIS
multilingual extension: easy implementation and
use in IBIS compliant simulators
  Math Foundations and Generality
  HIGH ACCURACY at LOW COMPLEXITY (like classical IBIS models)
  Good EFFICIENCY
  PROTECTION OF IP
advanced modeling techniques introduced via IBIS multilingual extension not affect IBIS standard and require no upgrades of IBIS ver. 4.1 compliant simulators
advantages

## Slide 17: Acknowledgements
for providing the ICX simulation environment
Thanks to
Sergio Perazza (Mentor, Italy) for the technical support on ICX and for the validation Example 2
Arpad Muranyi (Intel) for VHDL templates and code posted on http://www.eda.org/pub/ibis/summits/jun03a/ and http://www.eda.org/pub/ibis/summits/feb04a/