## Slide 1: IBIS: Addressing Challenges in Behavior and Measurement February 2006
Ian C Dodd
Architect, High Speed Tools
SDD Division

## Slide 2: Introduction
EDA Companies have established areas of excellence in their SI tools
  E.g. AMS modeling, macro-modeling, (encrypted) SPICE modeling, design templates, flexible measurements, scripting.
  Once these are established it is extremely unusual for a company to de-emphasis support for these features.
All EDA Companies also maintain a “lowest common denominator” for SI device behavior and measurement
  IBIS 3.2
  Allows IC vendors and independent modeling companies to create a single model for use with all major SI tools.
  Needs to accurately cover 99% of devices

## Slide 3: What is the current state of the art?
IBIS 3.2 still has lots of life in it for behavior, but there are examples where it is not adequate:
  Drivers with pre-compensation
  Equalizers
IBIS 3.2 has bigger problems with measurement. It is not adequate for:
  Receivers with slew rate sensitivity
  Self clocked data streams
IBIS 3.2 no longer meets the 99% criteria
  Still should be the first choice where it is sufficiently accurate
We need a new “lowest common denominator”

## Slide 4: Synchronous Timing Analysis
Static timing analysis: Input setup and
hold time
Static timing analysis: Clock edge to data out delay
Spreadsheet: Constraints, results
and violations
SI analysis: Driver, receiver,
package, trace
delays

## Slide 5: Analysis of Synchronous Nets
Predominant technology when IBIS 2.1 was developed.
  IBIS model describes behavior with IV and VT tables, Ccomp etc.
  IBIS supports measurement with Vinh, Vinl, Vmeas etc.
Typical Spreadsheet content (abbreviated):
  Min/max/actual trace length, max/actual number of vias, max/actual stub length
  Physical topology
  Min/max/min actual/max actual driver to load delays
  Max/actual overshoot voltage, max/actual ring-back voltage
  Non-monotonic events

## Slide 6: Source Synchronous Timing Analysis
Data book: Input setup and
hold time
Spreadsheet: Constraints, results
and violations
SI analysis (clock, data): Driver, receiver,
package, trace
delays

## Slide 7: Analysis of Source Synchronous Nets
Common technology when IBIS 3.2 was developed.
  Additions to IBIS behavior include series passives, driver scheduling, bus hold …
  Additions to IBIS measurement include dynamic overshoot, strength dependant thresholds ...
Additions to the Typical Spreadsheet
  Max/actual trace length difference between data and clock net
  Min/max/min actual/max actual driver to load delay difference match data and clock net (Derived from setup and hold requirement.)
  Max/actual dynamic overshoot voltage and time

## Slide 8: What Is New that Affects IBIS?
Source synchronous devices with input slew rate sensitivity.
Heavy inter-symbol interference
New definitions for threshold voltages and overshoot
Multi-gigabit, self clocked signaling
  Pre-compensation
  Equalizers
  Phase locked loop data and clock recovery
  Eye diagrams and masks
Multi-level signaling

## Slide 9: A look at one challenge: DDR2 (simplified)
The clock and data receivers have very significant sensitivity to input slew rate.
Dynamic overshoot is specified using a VT area.
We want to be able to include DDR2 nets in an automated scan of the whole PCB
We do not want to hard code DDR2 specific features into the waveform analysis or results spreadsheet.
  This will be a never ending job and delivered later than the customer wants it!

## Slide 10: Proposed General Approach
Enhanced behavior and measurement information in IBIS
  Create intelligent multi-lingual input models that delay their output signal based in slew rate
  Enhance the IBIS measurement facilities to support the new dynamic overshoot constraint
    Describe how to make the measurement
    Inform the spreadsheet to add new columns for the data

## Slide 11: Option 1: transistor level SPICE
Pros
  IC manufacturer can use the internal models that were developed from the Silicon.
Cons
  Encryption is required to hide the IP. Each EDA vendor has their own encryption package and proprietary foibles in their transistor primitives
  Simulation will be slow compared to IBIS or AMS
  Complicated models are prone to bugs.
  Implementing flexible measurements in the model (e.g. the new dynamic overshoot) is too difficult. To solve the overall problem we would have to add a comprehensive measurement language to IBIS

## Slide 12: Option 2: Macro-models
Pros
  Will work with any EDA vendor that has AMS, or is willing to add the (macro) building blocks into their SPICE like simulator.
  Faster simulation than transistor level models
Cons
  The current building blocks only have been proven in their support of IBIS 3.2. It is likely that new building blocks will soon be needed.
  Implementing flexible measurements in the model (e.g. the new dynamic overshoot) is too difficult. To solve the overall problem we would have to add a comprehensive measurement language to IBIS

## Slide 13: Option 3: Analog Only AMS*
Pros
  Most EDA vendors have access to analog only AMS
  Stepping stone to full AMS.
  Relatively easy for the model to do its own measurements
    Can be output as text messages ready for the spreadsheet
    Augment in IBIS with a simple list of column headings to add to the spreadsheet.
  Fast simulation
Cons
  The languages are complex and no vendor (to my knowledge) has every feature supported
    Could be alleviated by agreeing to a preferred language subset
  Implementing digital features e.g. extended history in an equalizer requires jumping through hoops.
* Analog “AMS” generally differs from “A” in its support for discontinuous functions

## Slide 14: Option 4: AMS
Pros
  Most flexible and technically elegant solution
  Easy for the model to do its own measurements
    Can be output as text messages ready for the spreadsheet
    Augment in IBIS with a simple list of column headings to add to the spreadsheet.
  Fast simulation
Cons
  Few EDA vendors have currently offered AMS in their SI tools.
  The languages are complex and no vendor (to my knowledge) has every feature supported
    Could be alleviated by agreeing to a preferred language subset

## Slide 15: Conclusion
We will not de-emphasize what we believe to the best long term solution i.e. multi-lingual IBIS with AMS.
We believe that in addition to the ultimate solution a short term a “lowest common denominator” modeling language is needed
IBIS 3.2, by itself, is no longer able to reliably meet this requirement
The solution should address both behavior and measurement
There are a number of competing methodologies that will meet many of the requirements
By definition we will only have a “lowest common denominator” if all the major EDA vendors agree on a single solution and add it to their SI tools.