## Slide 1: Differential System Design and Power Delivery
Vishram S. Pandit and Michael Mirmak
Intel Corp.
IBIS Summit at DesignCon
February 9, 2006
Acknowledgements:
Julius Delino, Sanjiv Soman, Woong Hwan Ryu, Arpad Muranyi, Henri Maramis
Copyright © 2006, Intel Corporation. All rights reserved.

## Slide 2: Motivation
  Common assumptions for differential system design…
    Currents in differential lines are equal and opposite
     Summation of currents in sig and sig# (differential lines) is zero
    Current in power equals current in ground at the driver
  These are not valid for all differential systems
  Understanding current behavior is key to proper differential power delivery design
  IBIS* community needs to address this behavior for system simulations

## Slide 3: Outline
  Driver and termination types used in differential current analysis
    “Differential” driver types
      Fully, Half and Pseudo
    Termination schemes and current profiles
      Power, Ground, Between Lines, PI
  Detailed analysis of the popular half differential driver design
    Currents in
      Power and ground at driver
      Differential lines
  Power Delivery (PD) design examples
    Normal operation vs. driver power on/off
    IBIS model usage

## Slide 4: Typical Differential Driver Types (1)
I
R
R
Gnd
Power
I
Gnd
I
Power
A
A
B
B
Fully Differential
Half Differential
Pseudo Differential
Gnd
Gnd
Power
(1) IBIS Modeling Cookbook for IBIS Ver. 4
May have
separate bias
circuit

## Slide 5: Differential Interface Characteristics
 | Fully Differential | Half Differential | Pseudo Differential
Driver Terminations | Between sig and sig# (if not at receiver) | Different combinations (e.g., sig and sig# to power, gnd) | Not terminated
Receiver Terminations | Between sig and sig# (If not at driver) | Different combinations (e.g., sig and sig# to power, gnd) | Different combinations (e.g., sig and sig# to power, gnd)
Driver Bias | May be separate bias circuit | Provided through termination | Usually not necessary
Industry Interfaces | LVDS | USB2.0, PCI Express*, SATA, etc. | USB1.1

## Slide 6: Typical Expectations for Differential Systems
Gnd
Power
A
I1
A
I1
A
A
Load
I2
I2
At driver…
Current in power = current in ground
Currents in sig + sig# = 0
    Equal and opposite currents in sig and sig#
Voltages in sig and sig# = Mirror image with respect to a common reference
DR
sig
sig#
Assumptions that may not be valid for all differential systems:
At driver, current in power = current in ground
Summation of currents in sig and sig# = 0

## Slide 7: Termination Schemes for Half Differential
  1) Power 2) Line to line
  3) Ground 4) 
DR
sig
sig#
Vterm
R1
R1
DR
sig
sig#
Vterm
R4
R4
DR
sig
sig#
DR
sig
sig#
R3
C
C
R3
Gnd
R2
R5

## Slide 8: Termination #1: Power
Io_in
Io_in#
Io_out
REF
Vterm
VR
55
55
Io_out#
Vcc
Gnd
I
55
55
Vreg
Box is an S-parameter-based model with
power, signal ports generated by PowerSI
Vreg model:
1.25 V, 5 nH, 7.8 mΩ
REF is a single,
arbitrary reference node
PDN+ IO

## Slide 9: Normal Operating Condition
Difference Current: Large DC, Small AC
Current (vssq)
≠
Current (vccq)
Currents in Tlines:
Summation ≠ 0 (1)
Voltages in Tlines
(1) Majority of return current is through ground, a net DC return current

## Slide 10: Driver Power On/off
Difference Current :
Large DC & AC
Current (vssq)
≠
Current (vccq)
Currents in Tlines:
Summation ≠ 0
Voltages in Tlines

## Slide 11: Termination #2: Line to Line
REF
Vterm
VR
91
Vcc
I
55
55
Vreg
Gnd
Io_in
Io_in#
Io_out
Io_out#
Vreg model:
1.25 V, 5 nH, 7.8 m

## Slide 12: Normal Operating Conditions
Difference Current: Small DC & AC
Current (vssq)
=
Current (vccq)
Currents in Tlines:
Equal and opposite;
Summation ≈ 0
Voltages in Tlines

## Slide 13: Driver Power On/off
Difference Current:
Large DC & AC
Current (vssq)
≠
Current (vccq)
Currents in Tlines:
Summation eventually ≈ 0
Voltages in Tlines with change in common reference

## Slide 14: Termination #3: Ground
Io_in
Io_in#
Io_out
REF
Vterm
VR
55 
Io_out#
Vcc
I
55 
55 
Vreg
Vterm
Gnd
55 
50 pF
50 pF
Vreg model:
1.25 V, 5 nH, 7.8 mΩ

## Slide 15: Normal Operating Conditions
Difference Current: Small DC & AC
Current (vssq)
=
Current (vccq)
Currents in Tlines:
Equal and opposite;
Summation ≈ 0
Voltages in Tlines

## Slide 16: Driver Power On/off
Difference Current:
Large DC & AC
Current (vssq)
≠
Current (vccq) (1)
Currents in Tlines:
Summation ≠ 0
Voltages in Tlines
(1) Currents will be equal depending on the cap charge up time, and cap value

## Slide 17: Termination #4: 
Io_in
Io_in#
Io_out
REF
Vterm
VR
64.5 
64.5

Io_out#
Vcc
Gnd
I
55 
55 
Vreg
309 
Vreg model:
1.25 V, 5 nH, 7.8 m

## Slide 18: Normal Operating Conditions
Difference Current: Large DC, Small AC
Current (vssq)
≠
Current (vccq)
Currents in Tlines:
Summation ≠ 0
Voltages in Tlines

## Slide 19: Driver Power On/Off
Difference Current:
Large DC & AC
Current (vssq)
≠
Current (vccq)
Currents in Tlines:
Summation ≠ 0
Voltages in Tlines

## Slide 20: Summary of Current Profiles
Comparison of termination schemes
Terminations | I(sig) and I(sig#) | I(Power) and I(Ground) at driver
Power | I(sig) + I(sig#) ≠ 0 | I(Power) ≠ I(Ground)
Between lines | I(sig) + I(sig#) = 0 | I(Power) = I(Ground)
Ground with AC coupling | I(sig) + I(sig#) ≠ 0 (0 after charge up of cap) | I(Power) ≠ I(Ground) (equal after charge-up of cap)
PI | I(sig) + I(sig#) ≠ 0 | I(Power) ≠ I(Ground)

## Slide 21: Significance of Current Profiles
  I(sig) and I(sig#) at driver
    For half differential driver, the currents in the lines may or may not be equal and opposite.
    In normal operation, when I(sig) ≠ I(sig#)
      AC amplitude may be equal but centered around some DC value
      Net non-zero DC return current
    In the driver on/off scenario, summation of I(sig) and (sig#) may result in net DC+AC current
  I(power) and I(ground) at driver
    In normal operation , when I(power) ≠ I(ground), some DC shift is present
      AC current may be equal
    Consider these currents in the driver on/off scenario
      di/dt will be different for power and ground in this case

## Slide 22: Observations re Energy in PDN and Noise
  Half differential driver designs utilize a current source
  High-frequency energy in Power Delivery Network (PDN) is small compared to that in driver power on/off scenario
  Power delivery solution space (die decoupling, package and board) depends on di/dt
  Noise produced in normal operating condition is smaller than that for driver power on/off condition
  Worst case occurs when driver power on/off cycles occur at resonant frequency of the PDN

## Slide 23: Modeling Differential Systems
  Different modeling approaches for half differential driver
    Transistor models
    Icc(t) method
    IBIS models
  In a differential system, each modeling approach needs to address
    Termination schemes’ dependence on system currents
      Currents in power and ground
      Currents in sig and sig#
    The solution space is dependent on the currents

## Slide 24: Transistor Model: SPEED2000* example
I
55 
55 
Power (B)
Power (A)
55 
55 
Z0=55 
Z0=55 
5 pairs
Power
Gnd
VR
Gnd
Box represents
a planar 3-D model;
Power and Gnd are
not single nodes
Transistor Model

## Slide 25: Sigrity SPEED2000* + Synopsys HSPICE* In Co-simulation
1.41v
1.145 v
1.1 v
0.94 v
1.52 v
Noise at driver (A)
Noise at termination (B)
Driver power on/off event

## Slide 26: Contemporary Icc(t) methods
Typical Icc(t) approach assumes equal currents in power and ground
Termination schemes MATTER when computing Icc(t)
Currents in power and ground may or may not be equal
  Monitoring Ivcc and Ivss a must
Vcc
PDN Model
Gnd
Icc

## Slide 27: Icc(t): Proposed Method
I
R
R
R
R
A
A
I2
Z0
Z0
I1
Gnd
V1
V2
Transistor
model
Driver
Termination

## Slide 28: Icc(t) for 5 Buffers
Current in power
Current in ground
Driver power on/off event

## Slide 29: Icc(t) Model: SPEED2000* example
Power (B)
55 
55 
Z0=55 
Z0=55 
5 pairs
Gnd
Power
Gnd
VR
Ivcc
Ivss
Power (A)
Box represents
a planar 3-D model;
Power and Gnd are
not single nodes

## Slide 30: Ivcc, Ivss under Sigrity SPEED2000*
0.85 v
1.6 v
0.78 v
1.65 v
Noise at source (A)
Noise at termination (B)
Driver power on/off event

## Slide 31: IBIS model: Sigrity SPEED2000* Example
Power (B)
55 
55 
Z0=55 
Z0=55 
1 pair
IBIS* Model
Power (A)
Gnd
gnd
gc
pc
pu
Power
Gnd
VR
out
Box represents
a planar 3-D model;
Power and Gnd are
not single nodes

## Slide 32: Normal Operation
Current in Power
≠
Current in Ground
Summation of currents in
transmission lines ≠ 0
Driver Currents

## Slide 33: Driver Power On/Off
  For optimum power delivery system design, driver power on/off behavior of the buffer must be analyzed
  For IBIS*, the output only model cannot be switched off
    Removing power from the buffer may not be accurate
  I/O model can be powered off through the Enable control
    Implementation is tool-dependent

## Slide 34: Conclusions
  For half differential system
    Currents in differential lines are not always equal and opposite
    Currents in power and ground are not always equal
    Termination schemes play an important role
  For differential systems, power delivery design must consider
    Normal operation vs. power on/off events
    Decoupling solutions to mitigate worst case operating conditions
  Different modeling approaches need to accommodate this behavior
  Key questions for industry
    Do today’s tools support driver power on/off event simulations?
    Can IBIS* be used reliably for driver power on/off analyses?
    Does BIRD95 include all the data needed for this kind of analysis?

## Slide 35: Backup

## Slide 36: Geometry and Stackup
Trace width: 5 mils
Trace spacing: 7 mils

## Slide 37: Icc verification with co-simulator
5 Diff Drivers are used
Co-simulator: Sigrity SPEED2000* + Synopsys HSPICE*
Current in power
Current in ground
Driver on/off
event
Current flow at drivers