## Slide 1: HDL and IBIS 4.1 Models in a Functional DDR Memory Interface Analysis
Randy Wolff, Micron Technology
©2005 Micron Technology, Inc. All rights reserved. Products are warranted only to meet Micron’s production data sheet specifications. Information, products and/or specifications are subject to change without notice. All information is provided on an “AS IS” basis without warranties of any kind. Dates are estimates only. Drawings not to scale. Micron and the Micron logo are trademarks of Micron Technology, Inc. All other trademarks are the property of their respective owners.

## Slide 2: Project Definition
Analyze a complete DDR memory interface in one simulation
Simulation should consider:
  Overshoot/Undershoot violations
  Setup and hold timing violations
  Include pattern dependant crosstalk between address, command, control, and data signals
  Slew dependant timing calculations

## Slide 3: Project Approach
Combine HDL functional models and IBIS I/O models
HDL code takes care of timing checks
IBIS model contains basic electrical checks
How does it all work?
IBIS 4.1!

## Slide 4: Simulation Diagram
Connection of HDL functional models and IBIS I/O models to the physical board layout
Chipset HDL
Chipset IBIS
PCB Traces, Vias, Passives, Connectors, etc
Memory IBIS
Memory HDL
Chipset IBIS 4.1 Model
Memory IBIS 4.1 Model
PCB SI Tool
43 signals/traces
(43)
(43)
Layout Database

## Slide 5: Analysis Details
Memory module (simulated traces highlighted in white)

## Slide 6: Analysis Details
Digital code from the chipset testbench generates the system stimulus
Random address and data pattern generators ensure realistic stimulus patterns for the Write cycle
Memory responds to chipset commands, thus automating Read cycle data patterns
Single simulation completes a Read and Write Cycle – multiple cycles can be run to simulate realistic bus utilization

## Slide 7: Functional SI Verification Results
HDL models contain timing checks
Timing violations caused by PCB effects are flagged

## Slide 8: Functional SI Verification Results
Analog Address, Clock, and Data signals at memory during a burst write from the chipset
Simulation easily changed to generate pseudo-random or fixed address and data patterns

## Slide 9: Functional SI Verification Results
Digital Address and Clock signals at the memory die during a burst write from the chipset

## Slide 10: Functional SI Verification Results
Combined analog and digital Address signals at the memory die during a burst write from the chipset
Provides a useful visualization of the logical analog equivalent

## Slide 11: Future Enhancements
Exercise all 64 DQ signals in the system (instead of 8)
Use AMS to analyze slew dependant timing – outputting results on separate signal
Model DDR2 system including ODT effects
Include S-parameter models to replace PCB physical information for enhanced crosstalk analysis
IBIS enhancements:
  Instantiating a [Model] in a [Circuit Call] statement
  Corner-specific Parameters passing

## Slide 12: Project Contributors
Gary Pratt, Mentor Graphics
Mark Kniep, Micron Technology
Pavani Jella, Micron Technology
Randy Wolff, Micron Technology