## Slide 1: IBIS Quality Committee Report
IBIS Summit, Feb 1, 2007
Kim Helliwell, LSI Logic

## Slide 2: Active Committee Members
Michael LaBonte, Cisco Systems (Chair)
Bob Ross, Teraspeed Consulting
Roy Leventhal, Leventhal Design and Communications
David Banas, Xilinx
Moshiul Haque, Micron Technology
Kim Helliwell, LSI
Eckhard Lenski, Siemens
Radovan Vuletic, Qimonda

## Slide 3: IBIS Quality Spec (Sample Pages)

## Slide 4: IBIS Quality Checklist

## Slide 5: OLD Quality Classification Scheme
Numbers indicate level:
  0: Passes IBISCHK and some basic automated checks
  1: Passes numerous “manual” checks for presence, completeness and correctness of data
  2: Correlation with simulated or measured data
    a. Correlates with simulation
    b. Correlates with measurements
  3: Both simulation and measurement correlation was done
    So: IQ2 a+b = IQ3, essentially.

## Slide 6: Problems With OLD Scheme
Provides no way to designate an unchecked model
  (-1?)
Meanings of various levels were hard to keep straight
The two letter designations were hard to keep straight
  Does “a” refer to simulation or measurement?
Having 2ab = 3 might be good algebra, but it’s not a good classification scheme.
Passing IBISCHK does not occupy its own level
  Taking this one step further: any “automated” check we can imagine should, in principle, be added to IBISCHK.
No “room” to add new levels for timing, power, etc.

## Slide 7: NEW Quality Classification Scheme
Numbers indicate level
  0: unchecked, unverified file.
  1: passes IBISCHK with no errors or warnings (explained warnings are allowed).
  2: Suitable for basic waveform simulation.
  3: Suitable for timing analysis.
  4: Suitable for power integrity analysis.
Appended letters indicate further qualifications
  “S”: has been correlated with simulation results.
  “M”: has been correlated with measured results.
  “X”: an exception exists in the file (must be documented).
Examples:
  IQ1: passes IBISCHK
  IQ2S: can be used for waveform simulation and has been correlated with simulation results.
  IQ3MS: Can be used for timing analysis, and has been correlated with both simulation and measured results.

## Slide 8: Advantages of NEW Scheme
Each level has a specific meaning.
There is a level that means “not checked.”
Letter designations have meaning (therefore can be remembered more easily).
Scheme is open ended: more “levels” can be added if necessary, and more letter designations can be added as required.
Letter designations can be appended to ANY level as appropriate.

## Slide 9: IBIS Quality Task Group Parser Bugs
Non-Monotonic Warnings for Combined Tables in All Versions
  Currently, only 4.0 and higher levels get checked for nonmonotonicity of the combined tables.
  This check is useful whatever the file version is.
  Proposes that this check be extended to all versions, and that nonmonotonic single tables be flagged as “Info” rather than “Warning”.
Parser Permits Vmeas not Between Vinh and Vinl
  Often indicates a problem with the model.
  Parser does not flag this in any way.
  Example of a new check that can be automated.
  Should only be a “Caution,” “Warning” is too strong, since there are cases where this legitimately will occur.

## Slide 10: Level 2 Checks (Note: this list is still under discussion) (Suitability for waveform analysis)
All pins must be defined and validated for correct logical/physical/model mapping.
[Model selector]s must be validated.
[Diff Pins] must be present if required.
C_comp values must be checked.
Component [Package] parasitic values reasonable
V-T tables must be defined for all output drivers.
All I-V and V-T tables must be inspected.
On-die termination must be properly modeled if present.
Typ/Min/Max values must be present and in correct order for all tables and parameters.
Ramp Data must be validated in accordance with IBIS spec.
Ramp data must be validated against appropriate V-T tables if available.

## Slide 11: Level 3 Checks (Note: this list is still under discussion) (Suitability for Timing Analysis)
Vinl/Vinh must be defined on receivers
Standard Load/Vmeas must be defined on drivers.
Must have at least signal pin RLC parasitics.
All package parasitics must be checked.
All model spec waveforms and standard load parameters must be defined and validated.
All output models must be simulated into standard load and switch through Vmeas.

## Slide 12: Level 4 Checks… (Note: this list is still under discussion) (Suitability for Power Integrity Analysis)
[Pin Mapping] must be present and correct
Power and Ground pin parasitics present
Need BIRD95 to be fully capable

## Slide 13: Meaning of “X”
Used to declare that a file is suitable for a particular analysis even if a required check is not passed by strict standards.
  Not intended as a “free pass” to distribute a substandard model.
Reason for the X designation must be documented in the file itself.
  Users should open the file and check the documentation for the reason for the “X”
Example: IBISCHK gives a warning for scrambled typ/min/max order on component curves even when combined curves are OK.
Example: For certain topologies, the pulldown table will not cross the 0-V, 0-current line for an output buffer, which is flagged as a warning, yet this is expected normal behavior for those topologies.
Example: Parser problems, as in Bug93 ([Model Selector] receiver thresholds for differential receivers result in errors and warnings)
Should be used only for warnings that are not possible to resolve, and errors that result from known parser bugs.

## Slide 14: Where to get more information…
http://www.vhdl.org/pub/ibis/quality_wip/