## Slide 1: Study of IBIS Waveform Time Offsets
How IBIS simulators handle offset and aligned IBIS waveform data
Mike LaBonte, Cisco Systems
IBIS Summit Meeting, 1 February 2007

## Slide 2: Background
To change states a buffer must turn off one transistor and turn on the other.
The turn-off usually precedes the turn-on, to avoid excessive “through current” while both are partially on.
Simulators must mimic this time offset controlling the pullup and pulldown I/V elements.
IBIS models do not directly convey this timing.
Simulators examine IBIS waveforms for 2 fixtures (pulled up and pulled down) to “guess” the turn-on/turn-off timing.
When waveforms have no offset, simulators must revert to some fallback mode, which is proprietary and likely to vary.

## Slide 3: Offset IBIS Waveforms (normal)
Pulldown turns off, resistor pulls up
Pullup turns on, pulls against resistor
Pullup turns off, resistor pulls down
Pulldown turns on, pulls against resistor

## Slide 4: Aligned IBIS Waveform (abnormal)
Pulldown turns off
Pullup turns on
Pulldown turns on
Pullup turns off
Changes voltage at same time, regardless of fixture voltage!
Note: waveform manually shifted

## Slide 5: Simulation Test Circuit
2.5V 167MHz buffer
  Vendor IBIS model, 0 ERRORs, 0 WARNINGs
  Vendor silicon SPICE model
Package R=70.4m L=5.3e-9 C=1.08e-12
50 ohm T-line terminated to mid-voltage VTT
Tested with 3 IBIS simulators + Silicon SPICE
Voltage measured at buffer pad
Power/ground currents measured in 2 simulators
Test cases:
  Buffer with normal waveforms
  Falling waveforms aligned
  No waveforms at all

## Slide 6: Baseline: Vendor IBIS, S2IBIS, and Silicon
C_comp calculated for s2ibis is about double the vendor value

## Slide 7: Vendor IBIS Fall Waves Offset (Normal)

## Slide 8: Vendor IBIS Waveform Case - 3 Simulators
Differences in trigger time and waveform trimming

## Slide 9: Vendor IBIS Waveform Case – Lined Up
Shifted in time to line up at 1.25V on falling edge

## Slide 10: IBIS Fall Waves Manually Aligned
Some IBIS models look like this

## Slide 11: Aligned IBIS Waveform Case – Lined Up
Agreement slightly worse than normal IBIS case

## Slide 12: No IBIS Waveform Case – Lined Up
Waveforms deleted from IBIS file

## Slide 13: Normal IBIS Waveform Case - Currents
VCCQ currents should match
VSSQ currents should match
Volts/mA

## Slide 14: Normal IBIS Waveforms - 2 IBIS Simulators
Volts/mA

## Slide 15: Aligned IBIS Waveform Case - Currents
Volts/mA

## Slide 16: Aligned IBIS Waveform Case - Currents
Volts/mA
IBIS currents are 3X silicon!

## Slide 17: Aligned IBIS Waveforms – 2 IBIS Simulators
Volts/mA

## Slide 18: Conclusions
IBIS simulators differ slightly in voltage simulation (at least for one off-the-shelf IBIS model).
IBIS simulators differ in how they handle pullup/pulldown turn-on/turn-off timing, and therefore power/ground currents, even with correctly timed IBIS waveform data.
  BIRD 95 has been accepted to address this.
  Kumar was right.
IBIS simulators differ even more in how they handle pullup/pulldown turn-on/turn-off timing when IBIS waveforms have incorrect time offset.
In the latter case the voltage waveform difference between simulators becomes only slightly worse.