## Slide 1: X
Bob Ross
IBIS Summit Meeting
DesignCon 2007
Santa Clara, California
February 1, 2007

## Slide 2: X for Exception Designation
Kim Helliwell, “IBIS Quality Committee Report” http://www.eda.org/pub/ibis/summits/feb07/helliwell.pdf
Real exceptions exist
“X” means exception is noted (DOCUMENTED)
Real examples
  I-V Glitch
  I-V tables not crossing 0 V, 0 A
  DDRII (BUG93) – Error in ibischk4 parser
Still discussing best approaches

## Slide 3
[Power Clamp] extraction (2Vdd to Vdd) with real shutdown protection circuit “glitch” of about 110 uA in clamp region

## Slide 4
Full [Power Clamp] internal pullup from 2Vdd to -Vdd with “glitch”
ibischk4 gives Warning
Could use “X”
Will some tools reject model?

## Slide 5
One choice: remove “glitch” to maximize tool portability
ibischk4 Warning gone
Should we still mark with “X” because overshoot simulations might be distorted?

## Slide 6
CML Stearing Logic [Pulldown] Tables Produce Quality Document Exception
Top-level
  ODT [Power Clamp]
  MAIN [Pulldown]
  [Driver Schedule]
MAIN [Pulldown]
  Scaled waveforms
BOOST [Pulldown]
  Scaled waveforms

## Slide 7
4.3.10 {LEVEL 3} [Pulldown] I-V tables pass through zero/zero
Typ, Min, and Max Pulldown table currents should all pass through zero at zero volts from ground (cmos). These three pull down tables should pass through zero/zero except in special cases (i.e. Differential, PECL, LVDS, or SERDES driver).
0 ibischk4 Warnings, but should exceptions be documented with “X”?
Or should this be left without comment?
(Could become a future Caution check)

## Slide 8: Parser Error for DDRII Models
[Model Selector] DDRII_DIFFCLKIO_BI
|
DDRII_DIFFCLKIO_75 75 Ohm On Die Termination | Default
DDRII_DIFFCLKIO_150 150 Ohm On Die Termination
DDRII_DIFFCLKIO_NO No On Die Termination
----------
[Model] DDRII_DIFFCLKIO_75
[Receiver Thresholds]
|
Vth = 0.90V
Vth_min = 0.882V
Vth_max = 0.918V
Threshold_sensitivity = 0.50
Reference_supply Power_clamp_ref
Vinh_ac = +250mV
Vinh_dc = +50mV
Vinl_ac = -250mV
Vinl_dc = -50mV
Tslew_ac = 300ps | Based on JEDEC STANDARD JESD8-15A
|
| Differential parameters (generates Warning message when added)
|
| Vdiff_ac = +500mV
| Vdiff_dc = +100mV
|
Bad Warning for differential specifications with [Diff Pin], [Receiver Thresholds], and [Model Selector] (for setting on-die terminator) – BUG93
Comment the model?

## Slide 9: X Dilemma – Parser Gives Wrong Warning/Error
Correct model with Warning/Error NOW, but in future, no Error or Warning (E.g., BUG93)
Correct model and “X”
  Yes for covering lag in EDA tool parser update
  No because model is correct even though ibischk4 flags problem today (but then user is confused)
Comment model parameters and “X”
  Yes to document modification and suggest future change
  No, should not depend on user changes
Under discussion

## Slide 10: X Closure
Several types of exception cases shown
Vendors might handle cases differently
  Real characterization with “X”
  Modify model with or without “X”
  Several models covering several cases
  Ignore
Main point is that “X” means the exceptions are known, and some resolutions might be suggested