## Slide 1: IBIS Modeling of USB Buffers
Sudarshan H N
NXP Semiconductors
February 1, 2007

## Slide 2: Agenda
Introduction
Modes of USB
Block Diagram
Skeleton of USB IBIS Model
Driver Operation.
Receiver Operation.
Application view of USB IBIS Models.
Summary.
Questions/Suggestions.

## Slide 3: Introduction
What’s special in USB ?
  Single ended and Differential Receivers connected to the same node.
What’s the problem ?

## Slide 4: Modes of USB

## Slide 5: Block Diagram
Tx-
Rx-
Rx
Tx+
Rx+
D+
D-
Driver is essentially two parallel single ended buffers (D+ & D-)
Receiver has 2 parts
  2 parallel single ended buffers carrying complementary signals (Rx+ & Rx-)
  Differential receiver (Rx)
Signals at both the driver and receiver side are full swing signals.

## Slide 6: Skeleton of USB IBIS model
[IBIS Ver] 3.2
.
.
.
[Manufacturer] NXP Semiconductors
[Pin] signal_name model_name R_pin L_pin C_pin
1 D+ two_speed_buffer_D+ 0.2 5.0n 2.0p
2 D- two_speed_buffer_D- 0.2 5.0n 2.0p
[Diff Pin] inv_pin vdiff tdelay_typ tdelay_min tdelay_max
1 2 200mv NA NA NA
[Model Selector] two_speed_buffer_D+
USB_FS Full speed operation of USB
USB_LS Low speed operation of USB
[Model] USB_FS | of usb
Model_type I/O
Polarity Non-Inverting
Enable Active-Low
| Reciever Thresholds
Vinl = 0.8V | USB Specification
Vinh = 2.0V | USB Specification

## Slide 7: Driver Operation
Driver is essentially 2 parallel single ended drivers.
Extraction of I-V and V-t data can be done individually.
All the four I-V curves [Gnd Clamp] [Power Clamp] [Pullup] & [Pulldown] are extracted for each pin by considering each one as a separate buffer.
Similarly V-t curves [Rising Waveform] & [Falling Waveform] can be done. R_fixture has to be 45 ohm as the USB line will be terminated with 45 ohm Single ended .
Also C_comp can be calculated separately for each pin.

## Slide 8: Receiver Operation Part 1 : Single Ended Receivers
Rx-
Rx+
D+
D-
Signal at Rx+ (Rx-) will be low only when signal at D+ (D-) is below 0.8 V
Signal at Rx+ (Rx-) will be high only when signal at D+ (D-) is above 2.0 V
Hysteresis parameters.

## Slide 9: Part 2 : Differential Receiver
CMVR=((D+)+(D-))/2 | Diff = (D+)-(D-) | Rx
0.8V≤CMVR≤2.5V | Diff ≥200mV | H (core logic HIGH)
0.8V≤CMVR≤2.5V | Diff ≤-200mV | L (core logic LOW)
- | ¦Diff¦<200mV | Undefined
0.8V>CMVR>2.5 | - | Undefined
CMVR = Common Mode Voltage Range
Diff = Input Sensitivity
Rx
D+
D-

## Slide 10: Receiver description in IBIS
USB Differential receiver can be correctly modeled only if the values of
Common Mode Voltage Range (CMVR)
Input sensitivity (Diff)
are specified (Section 7.1.4.1 of USB 2.0 Spec document)
In addition Single ended receivers has to be described with
VIL, VIH values.
Hystersis parameters.

## Slide 11: [Receiver Thresholds]
[Receiver Thresholds] | for a differential receiver (Rx)
Vcross_low = 0.8V | USB Spec
Vcross_high = 2.5V | USB Spec
Vdiff_ac = +200mV
Vdiff_dc = NA
Tdiffslew_ac = NA
[Receiver Thresholds] | for a single ended receiver (Rx+, Rx-)
Vth = 1.4V
Vinh_ac = +0.6V
Vinh_dc = +100mV
Vinl_ac = -0.6V
Vinl_dc = -100mV
Tslew_ac = 1.2ns
Not Possible to define [Receiver Thresholds] for both Single ended and differential receivers in a single model!!!
CMVR

## Slide 12: Issue !!!!
IBIS has to support both Single ended and differential modes for correct modeling of USB.
For Single ended operation : Vinl, Vinh
For Differential mode : Vdiff for Input Sensitivity
Vcross_low and Vcross_high for CMVR
But from the Cookbook…
For differential Input or I/O model types, the differential input threshold (vdiff) overrides and supersedes the need for Vinh and Vinl.
Solution
New [Model Type] has to be created in IBIS specification which can handle both single ended and differential ended operation for USB kind of buffers.

## Slide 13: Model Contd..
[Model] USB_FS
.
.
.
[GND Clamp]
[Power Clamp]
[Pulldown]
[Pullup]
[Ramp]
[Rising Waveform]
[Falling Waveform]
[Model] USB_LS
.
.
.
[GND Clamp]
[Power Clamp]
[Pulldown]
[Pullup]
[Ramp]
[Rising Waveform]
[Falling Waveform]
All these 4 tables are same as that of [Model] USB_IOP_FS. Can we avoid this duplication?

## Slide 14: Necessity to avoid this duplication
[GND Clamp], [Power Clamp] , [Pulldown] , [Pullup] - each has 3 tables corresponding to typ, min and max corners.
So totally 4*3 = 12 simulations required to generate these 4 tables.
Each simulation may take 1-2 min(approx).
So if we avoid these simulations it will effectively reduce ~ 30 mins for one model generation.
2 ways to do this..
Modify IBIS generating tools to intelligently put the same data for the two [Model] ‘s by simulating only once.
Introduce new IBIS specification which avoids tables in the duplicated model.
2nd method is preferable as it reduces the redundancy of data and thereby the file size.

## Slide 15: Proposal to reduce this duplication
By putting model names in front of the curve names.
[Model] USB_FS
.
.
[GND Clamp]
[Power Clamp]
[Pulldown]
[Pullup]
[Ramp]
[Rising Waveform]
[Falling Waveform]
[Model] USB_LS
.
.
[GND Clamp] USB_FS
[Power Clamp] USB_FS
[Pulldown] USB_FS
[Pullup] USB_FS
[Ramp]
[Rising Waveform]
[Falling Waveform]

## Slide 16: Application of USB USB Topology
Upstream Mode
Downstream Mode

## Slide 17: Low Speed USB Model in Upstream Mode.
AC Test Load Conditions.
Rref = 15k
Vref = 0
Cref = 100p
Vmeas = 1.65V

## Slide 18: Low Speed USB Model in Downstream Mode.
AC Test Load Conditions.
Rref = 1.5k
Vref = 3.6
Cref = 400p
Vmeas = 1.65V

## Slide 19: Same Model should work in 2 applications ?
As the cell is in low speed mode, there will be no difference in I-V or V-t curves between upstream and downstream modes and hence there is only one model defined.
But the same model has to cater to 2 kinds of applications with varying Vref, Rref and Cref.
Not possible with the single [Model] !!!
Copy of same model with different names for upstream and downstream, with models varying in their Vref, Cref, & Rref can be done. But it will result in redundancy of data.
IBIS community can look into this issue.

## Slide 20: Summary
USB has 2 complementary single ended drivers , 2 complementary single ended receivers and a differential receiver with full swing signaling.
Not possible to model both single ended and differential receiver in IBIS in a single model.
  Proposal : IBIS has to provide new specification to support this type of buffer.
As Full speed model and low speed models both have same driver characteristics, simulating the model for these curves twice is not required.
  Proposal : IBIS can support new specifications as suggested to reduce the time required in model generation.
As the same model should cater to 2 kinds of applications with varying Vref, Cref & Rref it is not possible with single IBIS model.
  Proposal : There should be an option to override the default values of Rref, Cref and Vref when using IBIS model.

## Slide 21: References
Universal Serial Bus Revision 2.0 specification http://www.usb.org/developers/docs
Switching in USB Consumer Applications by Eva Murphy & Padraig Fitzgerald , Analog Devices http://www.analog.com/library/analogDialogue/archives/40-01/usb_switch.html
IBIS 4.2 Specification Document http://vhdl.org/pub/ibis/ver4.2/ver4_2.pdf
IBIS Cookbook http://www.vhdl.org/pub/ibis/cookbook/cookbook-v4.pdf
Introduction to IBIS models and IBIS model making by Arpad Muranyi at Intel Corp. Nov. 3 & 4, 2003
IBIS Modeling for High Speed Designs by Dr. Lynne Green - JEDEX 2004 IBIS Workshop, April 16, 2004
IBIS Models @ 1.25GHz and Beyond by Bob Haller, Barry Katz, Kevin M. Fisher - DESIGNCON EAST June 23, 2003

## Slide 22
Questions ?
Comments?
Suggestions?