## Slide 1: New Interconnect Models Removes Simulation Uncertainty
Fangyi Rao, Agilent Technologies
Chad Morgan, Tyco Electronics
Vuk Borich, Agilent Technologies
Sanjeev Gupta, Agilent Technologies
New Interconnect Models Removes Simulation Uncertainty
Notes: <number>

## Slide 2: Presentation Outline
<number>
Tyco Electronics:
  Passive Component Model Review
  Simulation Tools and Methods Review
  Simulation Advantages from Using Impulse Responses
  Getting Impulse Responses Directly
  Converting Band-Limited S-parameters to Impulse Responses
  Practical Implementation Needs for Impulse Response Models
Agilent Technologies:
  A New Method to Convert Band-Limited Spectrum to Impulse Responses
  Method Validation Data
  Proposed Time Domain Impulse Response Model Methodology
  EDA Support for Exporting/Importing Impulse Response Data File
Notes: <number>

## Slide 3: Passive Component Models: Traditional
<number>
Quasi-Static 2D & 3D solvers used to derive inductance (L), mutual inductance (k), and capacitance (C) for component cross sections. Models typically lossless with the exception of series DC resistance (R)
Advantages: Sub-circuit models use generic SPICE elements
  Can be run in transient simulations with non-linear active device models
  Can be run in AC-sweep simulations to compute linear S-parameters
  Models are inherently causal and passive
Disadvantages: At high data rates, models become complex and inaccurate
  Model complexity and run-time increase with shorter cross-section lengths
  Frequency-dependant loss & dispersion not adequately modeled
  Longitudinal modes and transverse currents not adequately modeled

## Slide 4: Passive Component Models: Modern
<number>
Scattering parameters (S-parameters):
  Measurable by modern vector network analyzers (VNAs) with or without device under test (DUT) fixturing
  Generated by parametric equations, 2D field solvers (frequency-dependant RLGC tables), 2.5D field solvers, and 3D full-wave field solvers
Advantage: Frequency-domain simulations
  Flexible…can be directly used with linear simulations and deembedding
  Accurate…frequency-dependant losses and higher-order modes included
  Portable…can be transferred between simulators using Touchstone format
Disadvantage: Time-domain simulations
  Must be converted to pole/residue macro-models or impulses for SI analysis
  Conversion to impulse data requires significant expertise (more than iDFT)
  Many SI engineers struggling to use S-parameters efficiently in simulations

## Slide 5: Simulation Tools: Traditional SPICE
<number>
Generic SPICE (i.e. Berkeley SPICE v3): Can only solve transient simulations through time-stepping of differential equations from ‘traditional’ elements – must convert S-parameters into lumped element circuits:
  Genetic algorithms: Given a structure, can determine lumped element values that will fit given S-parameters…difficult to know structure ahead of time
  Macro-modeling: ‘Vectfit’ procedure fits S-parameters to a pole/residue function, passivity is enforced, and a lumped element circuit is produced
Laplace domain simulation
  Uses recursive convolution (usually faster than time integration of the lumped element approximation) to evaluate the model in
    Pole/residue (1), pole/zero (2) or rational polynomial (3) form
(1)
(2)
(3)

## Slide 6: Simulation Tools: Custom & Commercial
<number>
Math programming languages:
  Frequency-domain multiplication
    Take DFT of source waveform
    Multiply by system S-parameters
    Take iDFT of result to get output*
  Time-domain convolution
    Take iDFT of system S-parameters*
    Convolve with source waveform
Commercial tools:
  Advanced algorithms to complete S-parameter-to-impulse response conversion, along with convolution
    Passivity and causality are enforced
    Data validity maintained to Fmax
*Completing a valid iDFT of band-limited S-parameters is not a trivial task (will be shown)

## Slide 7: Simulation Tools: Method Summary
<number>
Macro-modeling:
  Pole-residue curve fit and passification for all frequencies
  Produces strictly causal and passive models for SPICE usage
  Difficulties:
    Consistent passification
    Time-domain data validity
Transient convolution:
  Must have accurate impulse responses to complete procedure
  One must overcome iDFT difficulties to compute impulse responses
The focus of this paper will be on transient convolution
  Converting band-limited S-parameters to causal, passive impulses
  Discussing a standard impulse response file format

## Slide 8: Impulse Response Advantages: Convolution
<number>
If one has the impulse response, convolution is simple to accomplish:
  Consistent impulse response time steps make convolution easier
  Separated ‘base delay’ makes convolution more efficient
Convolution can then be easily coded by doing the following:
  Reduce the impulse response to its shortest length:
    Remove all zero points before the impulse ‘base delay’
    Remove all zero points after the impulse has settled
  Mirror the shortened impulse response
  Generate the input waveform (same time steps as impulse)
  Complete transient convolution:
    Step the impulse through the input waveform
    Multiply all overlapping points
    Add the multiplication results to get the output at each time
  Shift the output waveform forward in time by the ‘base delay’

## Slide 9: Impulse Response Advantages: Conversion
<number>
Impulses can be easily converted to S-parameters using a DFT
  If impulse has settled (starts/ends at 0 volts), there are few transform issues
  S-parameters can be determined up to Fmax=1 / (2*Tstep)
  Impulse can be zero-padded to get any desired frequency resolution
Impulse can be used to generate SPICE macro-models
  Sum of exponentials approximation can be used to get models directly
  Pole/residue approximation of S-parameters can be used to get models
Impulse Response
S-parameters
SPICE Macro-modeling
Transient Convolution
DFT
Pole/Residue Fit
Exponential Sum Fit
Impulse response models represent ‘golden source’ for model distribution
  Impulse response model can be directly used in math tool convolution
  EDA tools should easily be able to handle an impulse response model

## Slide 10: Getting Impulse Responses Directly
<number>
If one has impulse responses, they can be used directly in transient convolution without inverse transform issues
Impulse response sources:
  Several time-domain modeling tools (FIM, FDTD, TLM)
  Component manufacturers (let experts deal with the iDFT issues)
Problem: No standard file format for model distribution
Solution: Create a new time-domain impulse file format
  File format allows multiple tools to exchange information
  A specific file format is proposed later in the paper

## Slide 11: Converting S-parameters to Impulses: Difficulties
<number>
If one only has band-limited S-parameters, one must use the inverse discrete Fourier transform (iDFT or iFFT) to get time-domain impulse responses:
x(n) is the discrete time-domain sequence
X(m) is the discrete frequency-domain sequence
N is the total number of samples in x(n) and X(m)*
The major source of error in calculating time-domain impulse responses from band-limited S-parameters is termed iDFT LEAKAGE
  The iDFT has ZERO leakage only if a structure is lossless/dispersionless such that its delay is constant at all frequencies and a multiple of 1/2Fmax
  (i.e. Delay(f) = Constant = m/2Fmax  Fmax can be tuned to eliminate leakage)
  Real physical structures have loss & reflections, so delay varies across frequency – iDFT leakage CANNOT BE AVOIDED entirely
    Time-domain energy existing between discrete iDFT time steps will manifest error on ALL available discrete time points as a sync function
    Frequency-domain windowing can greatly minimize iDFT leakage error, but there are issues with this (discussed later)
*Given band-limited s-parameters with N/2 points (Ranging from 0 to Fmax in steps of Fstep), X(m) is usually created with N points by mirroring the initial spectrum. The iDFT of X(m) then yields a real-valued time-domain signal, x(n), where the time step is defined as 1/2Fmax and the stop time is defined as 1/Fstep.

## Slide 12: Converting S-parameters to Impulses: Difficulties
<number>
Lossless
Constant Delay
Lossless, constant delay example of iDFT LEAKAGE:
  In this case, leakage can be avoided by selecting (Fmax = m / 2*Delay, m = integer)
  Green waveform shows no leakage when data falls on a discrete time point
  Red waveform shows sync leakage when data falls between discrete time points
iDFT
iDFT
Lossy, varying delay example of iDFT LEAKAGE:
Eliminating LEAKAGE at all time points is IMPOSSIBLE, because energy is coming out of the system at different times for different frequencies

## Slide 13: Converting S-parameters to Impulses: Difficulties
<number>
Frequency-domain windowing: S-parameters are multiplied by common window shapes to decrease output magnitude with increasing frequency
  Advantage: iDFT sinusoid ‘pulsation’ is minimized (less time leakage)
  Disadvantages:
    Many window functions are non-causal
    High-frequency data is not preserved (time-domain signal is damped)
‘Natural windows’ have helped many SI engineers get good simulation data:
  Step, pulse, and bit pattern responses all have spectra that roll-off with increasing frequency (defined by edge rate)
  System simulations typically examine highly lossy insertion loss responses, which roll off dramatically with increasing frequency

## Slide 14: Converting S-parameters to Impulses: Difficulties
<number>
Causality enforcement is a good goal for any sophisticated iDFT conversion
‘Base delay’ causality enforcement better…must find structure’s ‘base delay’:
  Delay versus frequency can be plotted using the equation below
    For a reflectionless system, this is the true delay versus frequency
    If a system has reflections, delay is distorted above & below the true delay
  One can use the minimum value of delay vs. frequency as the ‘base delay’
Base Delay (2.54 ns)
Base Delay (2.54 ns)
Note: Group delay is NOT a true measure of delay…only of phase linearity!!!

## Slide 15: Converting S-parameters to Impulses: Difficulties
<number>
Note: Completing an accurate Hilbert transform can be difficult since it requires calculation of the iDFT, which has leakage for band-limited S-parameters.
‘Base delay’ causality can be enforced using phase shifting and the discrete Hilbert transform:
The Hilbert transform is usually calculated as follows:
  Take the iDFT of the real frequency data to get the time signal’s even component
  Since the signal is real/causal, one can calculate the time signal’s odd component
  Take the DFT of the time signal’s odd component to get imaginary frequency data

## Slide 16: Converting S-parameters to Impulses: Difficulties
<number>
Checking & enforcing passive component physical passivity
  At each frequency, an s-parameter matrix is passive only if the minimum eigenvalue of I-S’S* is greater than or equal to zero (semi-positive definite)
  A small ‘EigenBuffer > 0’ value can be used for over-passification
  One can multiply the entire [S] matrix by a scalar multiplier at each frequency to force passivity
EigenBuffer=0.01
Other frequency-domain model issues:
  Fmax must be large enough to ensure adequate time step (Ts = 1 / 2Fmax)
  DC extrapolation & frequency interpolation must be handled

## Slide 17: Converting S-parameters to Impulses: Difficulties
<number>
Bottom Line…it is easier to get valid frequency-domain data from time-domain data than it is to get valid time-domain data from band-limited frequency-domain data:
  DFT of settled impulse response yields accurate S-parameter data
  iDFT of band-limited S-parameter data yields impulse response with leakage
iDFT
Easy
Difficult!!
DFT
It is desirable to have a tool that can complete the iDFT properly:
  Tool must eliminate leakage with minimal change to initial S-parameters
  Tool must enforce ‘base-delay causality’ and passivity

## Slide 18: Impulse Response Model Implementation Needs
<number>
There are advantages to directly using impulse responses in time-domain simulations, and there is a need for a standardized file format
Given band-limited S-parameters, it is difficult to directly calculate accurate time-domain impulse responses, and there is a need for a tool to do so
Concludes Tyco Electronics portion of the presentation:
  chad.morgan@tycoelectronics.com
  www.tycoelectronics.com/documentation/spiceelectricalmodels/
  modeling@tycoelectronics.com
Agilent Technologies up next:
  Fangyi Rao, Vuk Borich, & Sanjeev Gupta
  New approach for calculating valid impulse responses
  Impulse response model methodology and Agilent support

## Slide 19: Time Domain Convolution Challenges
<number>
Causal condition: Kramers-Kronig (K-K) relations
Real and imaginary parts are not independent.
Hilbert integrals involve entire spectrum.
Truncation in band-limited spectrum breaks K-K relations. Direct iDFT is non-causal.
Causality

## Slide 20: Case Study: A Simple Response Function
<number>
IFT
Truncate H at 1 Hz ( = 1). Compute impulse response by iDFT. Result is non-causal.
Restore causality by adjusting response to 0 at t < 0. Spectrum is altered.
Original H
DFT adjusted causal response
Exact
iDFT truncated H
Impulse Response
Spectrum

## Slide 21: Problems with Windowing
<number>
Standard window functions are non-causal
Equivalent to convolving h(t) with LPF. Leads to non-causal response at t < 0.
Spectrum roll-off at truncation frequency
Example: apply Hanning window to H
Original H
Windowed H
Exact
iDFT windowed H
Impulse Response
Spectrum

## Slide 22: Delay Preservation
<number>
Delay causality: no response before system base delay time
Common sources of violation
- Substrate dielectric constant model
Does not satisfy K-K relations if tanis constant
- Skin loss model: sqrt(f) dependent loss is non-causal without imaginary part.
Measured
Waveform (mV)
Modeled

## Slide 23: Passivity
<number>
Measurement or numerical modeling error cause non-passive S-parameters
Passivity can be corrected frequency-by-frequency
Requirement for passivity correction
- minimum impact on original data, avoid over-damping
- preserve causality in corrected S-parameters

## Slide 24: Rigorous Approach for Impulse Response Calculation
<number>
Calculate impulse response from band-limited spectrum
Automatic causality enforcement with respect to time zero and delay
Correct passivity violation in S-parameters while maintaining causality
Impulse response matches original spectrum to highest possible accuracy

## Slide 25: Revisit Simple Response Function
<number>
Use new approach to compute impulse response from truncated H
Response is causal
FT of impulse response matches original H
No roll-off at high frequency
DFT impulse response
Original H
Exact
Impulse response
Impulse Response
Spectrum

## Slide 26: S-parameters of Low Impedance RLC Network
<number>
Extract S-parameters of RLC sub-network
Compare waveforms between lumped network and S-parameter convolution
Tough case for convolution: Ohm impedance network normalized to 50 Ohm
Narrow dynamic range in S-parameters. Requires highly accurate impulse response.

## Slide 27: Lumped vs S-parameter Convolution
Original S(1,1)
<number>
Direct iDFT Approach: poor agreement
New Approach: perfect agreement
Lumped
S-parameter
Waveform
Spectrum
DFT impulse response
Lumped
S-parameter
DFT impulse response
Original S(1,1)
Waveform
Spectrum

## Slide 28: S-parameters of 30 Meter Coaxial Cable
<number>
Data measured up to 6.4 GHz
Noisy data at high frequency
Impulse response accurately represent original spectrum even in noisy region
Spectrum
dB
Original S(2,1)
DFT impulse response

## Slide 29: S-parameters of 20 cm Multilayer Line
S(2,1)
FT impulse response
Original
<number>
8-layer transmission line
Complex structure in spectrum due to coupling between layers
Excellent match between impulse response and original spectrum

## Slide 30: Delay Modeling
<number>
Analytic transmission line model optimized to match measured S-parameter
Non-causal lossy substrate dielectric constant is used
Results in non-physical response before delay time
In new approach, delay causality violation is automatically corrected in impulse response
Waveform (mV)
Measured
Modeled
Zero output
before delay

## Slide 31: Impulse Response Model Methodology
<number>
It is not straightforward to calculate impulse response from band-limited S-parameter
Must consider not only accuracy, but also causality, passivity and delay preservation
Much easier to start with impulse response models for convolution. Spectrum can be easily recovered by DFT.
Impulse Response
S-parameters
SPICE Macro-modeling
Transient Convolution
DFT
Pole/Residue Fit
Exponential Sum Fit
Need standard time domain file format for impulse response
Allows interoperability and distribution of causal/passive impulse response obtained by our new approach or other methods
Eliminates EDA vendor-proprietary treatment of S-parameter convolution

## Slide 32: Interconnect Model Exchange
Current
  S-parameters
    No standard simulation methodology results in variation of simulation results between different EDA tools
  Lumped SPICE models
    Difficult to extract for long and complex channel
Future vision
    Multiport Impulse response
Connector Vendor
Package Vendor
Multiport ADS Impulse Format
SPICE A
SPICE B
SPICE …
Similar result
Reduced uncertainty
Vendor ensure the quality of the models

## Slide 33: ADS Time Domain Impulse Format
<number>
Easy to use: 2 simple steps
Create Impulse response from S-parameter ( connector and package vendors)
Use impulse response within ED Tools
S-parameter
EDA Tool
Impulse File
Step 1: input S-parameter
Step 2: run

## Slide 34: Proposed ADS Impulse Response Format
<number>
support S/Y/Z form
uniform time step and time unit
base delay of S(I,J)
number of time point for S11
impulse response of S11
number of time point for S12
impulse response of S12
Impulse data is real number.
Data starts from delay time (0 before delay)
Initial version. Format is opened to modification.

## Slide 35: S-parameter Simulation
Impulse Model
S-parameter simulation of impulse response can be compared with original measurements
35

## Slide 36: Cascaded Impulse Models
All reflections, crosstalk, insertion loss are accounted for.
Provides voltage and current at every node
Allow frequency, time and envelope domain simulations
36

## Slide 37: Summary
<number>
Fundamental difficulties due to causality and passivity in impulse response calculations and effects on time domain convolution
New approach for accurate and causal impulse calculation from band-limited spectrum
Validation in various SI applications
Propose a new impulse response model methodology
Need for time domain data format of impulse files