## Slide 1: Touchstone Syntax for Versions 1.0 and 2.0
Bob Ross
IBIS Summit Meeting
DesignCon 2008
Santa Clara, California
February 7, 2008

## Slide 2: Background
Touchstone issued in 1984 by EEsof (now part of Agilent Technologies)
Touchstone is an OPEN, defacto format supported by nearly all companies supplying or handling S-parameter data
Touchstone ® is a registered trademark January 7, 1984 to October 10, 2007 – but it may have an indefinite life
Touchstone “Version 1.0” uploaded as public reference for ICM reference
  http://www.eda.org/pub/ibis/connector/
Touchstone Version 2.0 extended to remove some limitations and add some resistance per port flexibility for PDS applications, but no mixed mode (differential) yet
  http://www.eda.org/pub/ibis/docs/

## Slide 3: Version 2.0 Document Overview (Document Still Under Review)
Contains Touchstone “Version 1.0” format
  “Version 1.0” is designation of compatible superset of original format, although “1.0” never entered
Touchstone Version 2.0 advances
  Selectable reference resistance by port
  Explicit [Number of Ports] and [Number of Frequencies] keywords yields more flexible data format
    Selectable 2-port ordering (12_21 or 21_12)
  Symmetrical matrix format efficiency
  Some reference normalization changes

## Slide 4: Comment and Options Lines Same for All Versions
Comment character: “!” at beginning or within line
Options Line with 4 arguments in any order:
  # frequency_unit parameter format R,n
  frequency_unit: {GHz | MHz | kHz | Hz}
  parameter: {S | Y | Z | H | G}
  format: {DB | MA | RI}
  R,n: R <value> ! (R and <value> pair)
Defaults (when arguments missing):
  GHz, S, MA, R 50
Examples
  # ! Use the defaults, but one # is required
  # GHz S DB R 25 ! Any order examples
  # R 25 S GHz DB
  # GHz MHz ! Error example – two frequency units

## Slide 5: Touchstone “Version 1.0” Format (SnP where n=number of ports)
Unique S2P ordering (21 before 12 retained)
  Natural order is 11 12 21 22
Unique n-port formatting of data rules (n => 1)
Ordering and number or entries per line formed indirect way of determining number of ports
  New line required for each new frequency
  Frequencies must be in increasing order
End of file or beginning of noise parameters terminates data
  Noise parameters indicated by out of sequence frequency entry less than last frequency (for 2-port data only)
G-, H- defined for 2-ports only – all versions

## Slide 6: “Version 1.0” Fixed Format Examples (f = frequency, s = data-pair)
S1P f s f s f s f …
S2P f s s s s f s s s s f s s s s f …
S3P f s s s s s s s s s f s s s s s s s s s f …
S4P f s s s s s s s s s s s s s s s s f s s s s s s s s s s s s s s s s f …
S5P f s s s s s s s s s s s s s s s s s s s s s s s s s f …
S6P f s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s f …
Formatting, frequency ordering, and end of file implies number of ports and frequencies values.
Etc …

## Slide 7: “Compatibility Notes” Advances Original Touchstone
Differences between original Touchstone and “Version 1.0”
  99 port limit removed (usually not enforced)
  dB (dB/angle) allowed for Y-, Z-, H-, and G- parameters (even though potential data at infinity problem when the magnitude is 0.0)
  Y- and Z- parameters allowed for n => 3
Touchstone Version 2.0 (versus “Version 1.0”)
  No normalization for Y-, Z-, H-, and G- parameters and effective noise resistance
  Data format restrictions relaxed

## Slide 8: Touchstone Noise Format for All Versions
For 2-port data only
Five entries per line:
  Frequency (starts with out of sequence frequency)
  Minimum noise figure in dB
  Source reflection coefficient always normalized with respect to R <value>
  Phase of source reflection coefficient in degrees
  Effective noise resistance
    Normalized with respect to R <value> for “Version 1.0” and below
    Not normalized for Version 2.0

## Slide 9: Version 2.0 Block Arrangement
Keywords and Option Line (first entry is [Version] <n>)
N-port Data Block (new line required only for each new ascending order frequency)
Optional Noise Data Block (n=2 only)

## Slide 10: Touchstone Version 2.0 Seven IBIS-like Keywords
Required keywords
  [Version] 2.0
    Only “2.0” is permitted
    Omitted [Version] implies “Version 1.0”
    Must be first keyword before or after comment lines
  [Number of Ports] <n>
    [Two-Port Data Order] {21_12 | 12_21} required for n=2 only
  [Number of Frequencies] <nf>
Optional keywords
  [Reference] <list of n reference resistances in port order>
  [Matrix Format] {Full | Lower | Upper}
    Defaults to Full if omitted
  [Number of Noise Frequencies] <nnf>
    Used ONLY for 2-port data (should require n=2)
    Required only if noise data follows 2-port data list

## Slide 11: Touchstone Version 2.0 Rules
[Version] 2.0 required as first entry in file or after ! lines
Keyword and option block before any n-port data
  All other keywords in any order
  Option line anywhere within block
  Parser uses count information to check data block (and noise block) data content from n and nf (and nnf if given) and [Matrix Format]
Each new frequency must be first entry in a row
  Number of entries per row is optional (n value determines when new frequency and port grouping occurs
  Ascending frequency still required
Noise parameter data format unchanged
  Still requires at least one line of 2-port data
  Still requires out of sequence frequency from last data set

## Slide 12: Touchstone Version 2.0 Data Normalization Changes
“Version 1.0” (and original Touchstone)
  Z, Y, G, H automatically normalized based on the R <value> or default
    So the Z11 = 1.0  (normalized) entry with R 50 documents the actual Z11 magnitude is 50.0 
  Effective noise resistance is normalized with respect to R <value>
Version 2.0
  Z, Y, G, H entries are direct and independent of <value> or [Reference] values (NOT normalized)
  Effective noise resistance is NOT normalized

## Slide 13: IBIS and Non-IBIS Conventions
New keywords follow IBIS rules exactly
  Bounded by “[“ and “]”
  Separated within by single space or under-bar
  Followed by data or data list of selected arguments
  Subparameters not defined in Touchstone Version 2.0
Touchstone comment character “!” similar to IBIS comment character (beginning or within line)
Everything is case insensitive (unlike IBIS)
Units are predefined – no multipliers allowed as in IBIS
Weak numerical typing like IBIS
  Numerical data can be fixed point, floating point or exponential (for example, 50 = 50.0 = 5e1)

## Slide 14: Version 2.0 Unique 2-port Features
Requires n=2
  [Two-Port Data Order] required
  G- H- Parameters Allowed
  Noise Parameters Allowed
Error if any of above exist for n < > 2

## Slide 15: Closure
Syntax rule and data interpretation summary for all Touchstone versions
Some legacy rules retained for compatibility
Touchstone parser
  Only Version 2.0 syntax?
  Pass all “Version 1.0” syntax?
Touchstone ® trademark - indefinite life
Specific examples in latest draft document (in temporary link)
  http://www.eda.org/pub/ibis/docs/
Thanks to Michael Mirmak for preparing document, to Radek Biernacki for some very detailed review, and all the other participants for their help

## Slide 16: Next Steps
Finish review and vote for IBIS release
Write request for parser quotes document
Get parser quotes and select developer
Raise money committments
Probably start project in 2009 or earlier
Submit as GEIA standard either as Version 2.0 or wait for a Version 2.1 based on parser developer review comments and changes