## Slide 1: Multi-Mode Modeling
Bob Ross
IBIS Summit Meeting
DesignCon 2008
Santa Clara, California
February 7, 2008

## Slide 2: Configurable Buffers in IBIS
Current methods in IBIS
  [Model Selector] (general usage – all voltages, modes, technologies, conditions)
  [Alternate Package Models]
  [Series Switch Groups] (and [On], [Off] models)
  [Add Submodel] (for specific state (e.g., Non-driving mode only)
Tool/user select based on ALL choices documented
  State selection (e.g., for I/O Driving or Non-driving operation)
  EBD format – multiple buffers on net
  Algorithmic Model Executable (Windows, Unix, Linux, etc.)
  Multi-lingual language selection (VHDL-AMS, SPICE, Verilog_A(MS), etc.)
  Syntax with levels of override for higher level functionality (technical and levels of specification)

## Slide 3: Missing Configurability
Examples
  Differential/single-ended reconfiguration
  3-state vs. I/O distinction if both exist in device (not really needed)
  3-state on/off toggle dynamic characterization when “enable” is switched (not really needed)
Can offer separate [Component]s for hard coded configurations
EDA tools can hard override the configuration
Example of one configurable buffer given

## Slide 4: Real Output Clock(s) Example
In Sync. Mode Selector MUXs
LVPECL, LVDS [Model Selector]s
CMOS (3.3V, 2.5V, 1.8V, 1.5V plus slew rates [Model Selector]s)
(Complimentary CMOS possible, but not in this device)

## Slide 5: Four [Component] Choices
[Component] CLOCKS_SS
[Component] CLOCKS_SD
[Component] CLOCKS_DS
[Component] CLOCKS_DD
8 Single-ended (S) pins (1-8) or 4 Differential (D) pin-pairs (1,2 3,4 5,6 7,8)
Model Selectors in Sync. with Differential Pin assignments (next two slides)

## Slide 6: [Model Selector] Choices for [Pin]s
[PIN] | S D
1 clk_1 { CMOS_A || Diff_A }
2 clk_2 { CMOS_A || Diff_A }
3 clk_3 { CMOS_A || Diff_A }
4 clk_4 { CMOS_A || Diff_A }
5 clk_5 { CMOS_B || Diff_B }
6 clk_6 { CMOS_B || Diff_B }
7 clk_7 { CMOS_B || Diff_B }
8 clk_8 { CMOS_B || Diff_B }

## Slide 7: Four Distinct [Diff Pin] Assignments
[Diff Pin]
1 2
3 4
5 6
7 8
[Model Selector] CMOS_A
….
[Model Selector] CMOS_B
….
[Model Selector] Diff_A
….
[Model Selector] Diff_B
….
Both or Neither for Bank A
Both or Neither for Bank B

## Slide 8: Issues Under Consideration
Differential Mode (vdiff location problem)
  “vdiff” – can be different for PECL and LVDS if these were Input models
  (Not a problem here for Output only clocks)
IBIS Limitation
  No selection mechanism for re-configuration of single-ended (matched pairs) to differential
  Originally an ECL option for early devices
  Must use different [Component]s for hard-coded choices

## Slide 9: Observations
Configurability makes a strong case for moving differential parameters into the [Model] scope directly along with single-ended parameters
  Already done for [Receiver Thresholds]
  Ugly but solves dual mode problem for some technologies (DDR, USB, ECL, Configurable)
Consider offering a single-ended/differential selection option
  Another mechanism for EDA tools to control
  Helps limit the choices
  But selectors and S/D modes must be in sync.