## Slide 1: Building advanced transmission line and via-hole models for serial channels with 10 Gbps and higher data rates DesignCon IBIS Summit, Santa Clara, February 7, 2008
Yuriy Shlepnev shlepnev@simberian.com
Copyright © 2008 by Simberian Inc. Reuse by written permission only. All rights reserved.
Notes: This presentation is about building advanced electromagnetic models for interconnects with data rates 10 Gbps and higher.
<number>

## Slide 2: Agenda
07/30/26
© 2008 Simberian Inc.
<number>
Introduction
  De-compositional analysis of multi-gigabit channels
Building models for transmission lines
  Proximity, edge and skin-effects
  Surface roughness
  Metal plating
  Dielectric polarization and high-frequency dispersion and loss
Building models for differential via-holes
  Localizability
  De-embedding
  Effective via-hole impedance and geometry optimization
Conclusion
Notes: I will start with an overview of the basics of the de-compositional analysis of interconnects, proceed with the detailed analysis of the signal degradation effects and parameters extraction techniques for transmission lines. After this we will discuss how to design and how to build models for localizable via-holes.
<number>

## Slide 3: Introduction
07/30/26
© 2008 Simberian Inc.
<number>
Faster data rates drive the need for accurate electromagnetic models for multi-gigabit data channels
Without the electromagnetic models, a channel design may require
  Test boards, experimental verification, …
  Multiple iterations to fix or improve performance…
No models or simplified static models may result in complete failure of the design
Notes: <number>
Faster data rates require advanced analysis and modeling. It is important at the interconnect budget exploration stage and at the verification stage as well. Without the modeling the results could be unpredictable and lead to complete design failure. The multi-gigabit serial standards require simulation both in time and in frequency domain. It means that your frequency-domain models have to be extremely broadband and causal because of the broadband spectral content of a serdes signal. Low, medium and high-frequency effects have to be accounted for in your RLGC models for t-lines and in multiport S-parameter models.

## Slide 4: Major signal degradation factors
07/30/26
© 2008 Simberian Inc.
<number>
Via-hole transitions and discontinuities: Reflection, radiation and impedance mismatch
Transmission lines: Attenuation and dispersion due to physical metal and dielectric properties High-frequency dispersion
Dispersion
Attenuation
Reflection
Notes: <number>
Signal degradation factors can be formally separated into two groups. First, degradation in the straight segment of transmission line caused by losses and dispersion due to dielectric and conductor properties and high-frequency dispersion. Two graphs on the right illustrate typical dependencies of attenuation and delays p.u.l. for a PCB line. Second, discontinuities or transitions such as via-holes reflect the signal and electrically couple signal to parallel-plane structures and space around the board. One way to simulate all those effects is to throw geometry of the whole network into a 3D full-wave field solver and wait for few hours for the result if simulation is possible.

## Slide 5: Electromagnetic models for interconnects
07/30/26
© 2008 Simberian Inc.
<number>
Decomposition
W-element models for t-line segments defined with RLGC(f) p.u.l. tables
Multiport S-parameter models for via-hole transitions and discontinuities
3D full-wave electromagnetic models are required for successful analysis of multi-gigabit channels!
Notes: Another more effective way is to decompose the net into transmission line segments and discontinuities, build models for them with an electromagnetic solver and use a system-level analysis tool to recompose them back, attach driver and receiver models to estimate the performance of the whole net. Transmission lines can be characterized with per unit length frequency-dependent RLGC parameters and arbitrary discontinuities can be characterized with the multiport scattering parameters. A 3D full-wave solver has to be used to extract the models.
<number>

## Slide 6: De-compositional system-level analysis
07/30/26
© 2008 Simberian Inc.
<number>
Both early system exploration and system verification can be done on the base of de-composition into elements with localizable electromagnetic models
System Exploration
Notes: The de-compositional analysis must use one or more electromagnetic solvers as in the process illustrated on this diagram. The decomposition can be done by either by a system-level analysis tool or manually for a system exploration for instance. An electromagnetic solver takes geometry of the network elements and produces p.u.l. RLGC and S-parameter models, that later are recomposed by a circuit simulator and time and frequency responses of the network are computed.
<number>

## Slide 7: Hybrid simulation technology is used to illustrate this presentation
07/30/26
© 2008 Simberian Inc.
<number>
Method of Lines (MoL)
  More accurate than finite element method (FEM) and finite integration technique (FIT) for problems with multiple thin dielectric and metal layers
  Provides conductor interior solution for metal planes
Trefftz Finite Elements (TFE) or Ultra-Week Discontinuous Galerkin’s Element (UWDG)
  Can be used for any material and easy to interface with MoL
  Used to model strip conductor interior with rough surface
Method of Simultaneous Diagonalization (MoSD)
  Extracts modal and per unit length parameters of lossy multi-conductor lines and periodic structures
  Allows precise non-reflective de-embedding
  Provides 3D observable definition of the characteristic impedance
Notes: To illustrate the signal degradation effects, I used regular version of Simbeor solver from Simberian Inc. The solver engine is based on a hybrid simulation technology. Method of Lines is used to build Green’s function for multilayered dielectrics of stackup with metal planes. Trefftz finite elements are used to simulate the interior of strip conductors. Method of Simultaneous Diagonalization is used to extract modal and per unit length parameters of the transmission lines and for precise de-embedding of S-parameters.
<number>

## Slide 8: Agenda
07/30/26
© 2008 Simberian Inc.
<number>
Introduction
  De-compositional analysis of multi-gigabit channels
Building models for transmission lines
  Proximity, edge and skin-effects
  Surface roughness
  Metal plating
  Dielectric polarization and high-frequency dispersion and loss
Building models for differential via-holes
  Localizability
  De-embedding
  Effective via-hole impedance and geometry optimization
Conclusion
Notes: Though, the conductor and dielectric dispersion and loss effects can not be separated and work together, conceptually the effects can be investigated separately.
<number>

## Slide 9: Conductor attenuation and dispersion effects
07/30/26
© 2008 Simberian Inc.
<number>
proximity effect in planes ~10 KHz
Inductance p.u.l. L(f) decreases
proximity and edge-effects or transition to skin-effect ~1 MHz or higher
well-developed skin-effect ~100 MHz or higher
Resistance p.u.l. R(f) increases
Roughness ~40 MHz
DC
uniform current distribution
dispersion and edge effects – further degradation
Low
Medium
High
R(f) and L(f) increase
Frequency
Hz
Z
X
Y
Skin-effect
Notes: <number>
Let’s take a closer look at the degradation effects related to the conductor properties. At low frequencies the current distribution is uniform across the traces and planes and at about 10 KHz current in plane concentrates below the strip. At the medium frequencies we observe a transition to skin-effect and current becomes larger near the conductor surface and near the corners. Finally, at high frequencies, current inside the conductors is almost zero and we can talk about well-developed skin-effect. Transition from low to high frequencies causes increase of R p.u.l. and decrease of L p.u.l. due to larger current near surface and smaller magnetic field energy inside the conductor. If skin depth becomes comparable with the surface roughness, the roughness causes increase of both R and L. Dispersion due to presence of dielectric and edge-effect at high frequencies can case further changes in R and L. Picture on the left illustrates the skin-effect as the energy absorption by a conductor. Energy flows inside the conductor and not along the wave propagation direction.

## Slide 10: Current distribution in rectangular conductor
07/30/26
© 2008 Simberian Inc.
<number>
1.7 MHz, t/s=0.5, Jc/Je=0.999
28 MHz, t/s=2.0, Jc/Je=0.76
170 MHz, t/s=5, Jc/Je=0.16
1 GHz, t/s=12.2, Jc/Je=0.005
Current density distribution in 10 mil wide and 1 mil thick copper at different frequencies
t/s is the strip thickness to the skin depth ratio
Jc/Je is the ratio of current density at the edge to the current in the middle.
Notes: <number>
To quantify the medium frequencies or transition to skin-effect we can use either thickness of strip or plane to skin depth ratio (t/s) or equality of the real and imaginary parts of the internal impedance p.u.l. This is example of current density and internal impedance for a 10 mil by 1 mil strip. At thickness to skin depth 0.5, the current distribution is uniform and the imaginary part of the internal impedance is less than 5% of the real part. When the strip thickness becomes 2 skin depth at 28 MHz, the ratio of current density in the center to the current density at the edge is still high – 0.76, and the real and imaginary parts are not close to each other. Only at 170 MHz, when strip is 5 skin-depth thick, current in the center is relatively low and the difference between the real and imaginary parts of the impedance is a few %.

## Slide 11: Transition to skin-effect and roughness
07/30/26
© 2008 Simberian Inc.
<number>
40 MHz
150 MHz
4 GHz
0.5 um
400 GHz
Account for roughness
No roughness effect
10 um
5 um
1 um
18 GHz
0.1 um
Transition from 0.5 skin depth to 2 skin depth for copper interconnects on PCB, Package, RFIC and IC
Interconnect or plane thickness in micrometers vs. Frequency in GHz
RFIC
Package
IC
No skin-effect
Well-developed skin-effect
PCB
Ratio of skin depth to r.m.s. surface roughness in micrometers vs. frequency in GHz
Roughness has to be accounted if rms value is comparable with the skin depth
Notes: <number>
Now we can defined the medium frequencies for different technologies on the base of the strip or plane thickness to skin depth ratio. The vertical axis on the left graph is conductor thickness in micrometers. The horizontal axis is frequency. Along the blue line the conductor thickness is half of skin depth and there no skin-effect below this line. Along red line, the conductor thickness is equal to five skin depth. Well-developed skin-effect area is above the red line. Transition to skin-effect occurs between those lines. We can see that different technologies may have transition at different frequencies. Conductor thickness for PCB technology may be from 50 um to 15 um. It means that transition frequencies may be as high as 500 MHz. With 5 um conductor thickness in packaging applications, the transition takes place from 40 MHz to 4 GHz – right in the middle of the multi-gigabit serdes spectrum. With 2 um thickness the transition takes place at 20 GHz. In addition, the conductor surface roughness can complicate the analysis. It must be accounted as soon as root mean square of the bumps is about one skin-depth. With 10 um roughness it means frequencies as low as 40 MHz, where the roughness can substantially change the attenuation. Typical PCBs or packaging applications may have roughness from 5 to 1 um, that is in the frequency band relevant to the serdes interconnects analysis.
Note that this classification is necessary only to understand the limitations of a particular solver. A static solver for instance always assumes well developed skin effect to estimate the resistance and internal inductance p.u.l

## Slide 12: Modeling roughness with the effective surface impedance
© 2008 Simberian Inc.
<number>
Rough surface may be characterized with two parameters and approximated as triangular bumps along the current flow
SR
RA
Roughness Factor: RF=L_rough/L_straight
L_rough
L_straight
RF=2 or RA=60 deg
RF=1.4 or RA=90 deg
SR (RMS value)
Roughness Angle: RA=2*arcsin(1/RF)
07/30/26
Strip-line, w=140 um, t=50 um, h=350 um, DK=3.4, copper, all surfaces are rough.
Zsurface
+100%
+40%
Notes: The roughness is a complicated subject and multiple papers have been written recently about it. A possible approach is to measure two parameters of the rough surface – rms value of the peak to valley distance and rms value of the path increase along the rough surface comparing to a straight line (roughness factor) and construct surface with the equivalent triangular profile. The impedance of such surface can be computed with the Trefftz finite elements similar to the original technique of Morgan developed in 40-s, that was later used by Hammerstad and Bekkadal to construct roughness model widely used in microwave engineering. These two graphs illustrate the dependencies of attenuation in a strip-line from the rms roughness at different frequencies. With the roughness factor 2, the attenuation can double at high frequencies, with the roughness factor 1.4 the attenuation can grow just 40%. The effect is just the increase of the surface area that absorbs the energy of electromagnetic wave travelling along the line. Note that this model is causal – it means that not only attenuation is changing, but also the propagation constant and complex characteristic impedance too.
<number>

## Slide 13: Effect of surface roughness on a PCB micro-strip line parameters
07/30/26
© 2008 Simberian Inc.
<number>
Rough
Flat
Rough
Flat
Lossless
Lossy
Transition to skin-effect
7 mil wide and 1.6 mil thick strip, 4 mil substrate, Dk=4 (lossless), 2-mil thick plane. Strip and plane are copper.
Metal surface RMS roughness 1 um (plane and bottom surface of strip), rms roughness factor 2,
  25 % loss increase at 1 GHz and 65% at 10 GHz
+65%
Notes: To illustrate the conductor effect I generated few examples with the ideal dielectric. Here parameters of a typical PCB microstrip line with flat conductors and with rough bottom of the strip and plane. The model predicts 65% increase in attenuation at 10 GHz.
<number>

## Slide 14: Transition to skin-effect and roughness in a package strip-line
07/30/26
© 2008 Simberian Inc.
<number>
Rough
Flat
Transition to skin-effect
Rough
Flat
Lossless
Lossy
79 um wide and 5 um thick strip in dielectric with Dk=3.4.
Distance from strip to the top plane 60 um, to the bottom plane 138 um. Top plane thickness is 10 um, bottom 15 um.
RMS roughness is 1 um on bottom surface and almost flat on top surface of strip, RMS roughness factor is 2.
Transition is up to 2 GHz, 33% loss increase at 10 GHz
+33%
Notes: Another example for a flip-chip packaging application. Top surface of the strip is flat. The roughness effect is smaller comparing to the previous example and gives only 33% increase of the attenuation. Though the small thickness of the strip shift the transition to skin-effect up to 2 GHz. It means that the models constructed with a static solver and based on the assumption that the skin-effect is well developed at 1 GHz will be not accurate in this case.
<number>

## Slide 15: Effect of RoHS metal surface finish on a PCB micro-strip line parameters
07/30/26
© 2008 Simberian Inc.
<number>
NoFinish – 8 mil microstrip on 4.5 mil dielectric with Dk=4.2, LT=0.02 at 1 GHz.
ENIG2 - microstrip surface is finished with 6 um layer of Nickel and 0.1 um layer of gold on top
Nickel resistivity is 4.5 of copper, mu is 10
~50% loss increase from 0.1 to 10 GHz
No Finish
ENIG2
No Finish
ENIG2
Gold
Nickel
Copper
Strip
No Finish
+50%
Notes: A micro-strip line conductor may contain multiple layers of different conductors as in the electroless nickel immersion gold process (ENIG). Considering the recent increase in gold prices and green technologies you may wonder what is the effect of thinner gold layer on top of nickel. The effect of attenuation increase can be observed over relatively wide frequency band as illustrated here and at 1 GHz the attenuation may grow as much as 50% in addition to changes in the impedance and inductance per unit length.
<number>

## Slide 16: Dielectric attenuation and dispersion effects
07/30/26
© 2008 Simberian Inc.
<number>
Dispersion of complex dielectric constant
  Polarization changes with frequency
  High frequency harmonics propagate faster
  Almost constant loss tangent in broad frequency range – loss ~ frequency
High-frequency dispersion due to non-homogeneous dielectrics
  TEM mode becomes non-TEM at high frequencies
  Fields concentrate in dielectric with high Dk or lower LT
  High-frequency harmonics propagate slower
  Interacts with the conductor-related losses
Dk vs. Frequency
Loss Tangent vs. Frequency
At higher frequency
Notes: <number>
Dielectric effects can formally be separated into two parts. The first one is related to the frequency-dependent polarization or dielectric property itself. Typical dependency of dielectric constant for FR4-type dielectrics is shown here (I explain it later). Dielectric constant decrease with the frequency and loss tangent is zero a DC, grows to some value, slightly grows over a wide frequency band and drops to zero at extremely high frequencies. Such causal wideband Debye model can be constructed from just one frequency measurement. Higher frequency harmonics propagate faster due to the dielectric constant decrease. Another phenomenon related to non-homogeneous dielectric is concentration of electromagnetic field in the dielectric with higher dielectric constant as illustrated here. TEM modes become non-TEM due to the longitudinal components of electromagnetic field. It can cause non-classical growth of attenuation and increase in the p.u.l. inductance. Full-wave analysis is required to simulate this effect. Higher frequency harmonics propagate slower and L p.u.l. increases. Technically the high-frequency dispersion is not separable from the conductor effects.

## Slide 17: Broadband causal dielectric models with dispersion are required
07/30/26
© 2008 Simberian Inc.
<number>
Dielectric Constant
Dk=4.2 at 1 GHz
Frequency, Hz
LT=0.02 at 1 GHz
Loss Tangent
Djordjevic, R.M. Biljic, V.D. Likar-Smiljanic, T.K.Sarkar, IEEE Trans. on EMC, vol. 43, N4, 2001, p. 662-667.
Loss Tangent
LT=0.02 at 1 GHz
Dk=4.2 at 1 GHz
Dielectric Constant
Frequency, Hz
2) One-pole Debye (1PD) model
3) Wideband Debye (WD) model
With one measurement of Dk and LT for PCBs the possibilities are 1) Flat non causal (FlatNC) model
Notes: To capture the dispersion and loss due to the polarization properties of dielectric, a frequency-dependent causal models of dielectric have to be used. For dielectrics used in PCBs, it is often to have measurement of dielectric constant and loss tangent at just one frequency point. The first choice is to assume them frequency-independent – it produces the flat non-causal model. One-pole Debye is the simplest case of causal model and wideband Debye is the model that is the closest to behavior of PCB-type dielectrics. Note that with multiple frequency measurement points the multi-pole Debye model may be the best choice.
<number>

## Slide 18: Effect of dielectric models on a PCB micro-strip line parameters
07/30/26
© 2008 Simberian Inc.
<number>
FlatNC – 7 mil microstrip on 4.0 mil dielectric with Dk=4.2, LT=0.02 and without dispersion
1PD – same line with Dk=4.2, LT=0.02 at 1 GHz and 1-pole Debye dispersion model
WD – same line with Dk=4.2, LT=0.02 at 1 GHz and wideband Debye dispersion model
No metal losses to highlight the effect
FlatNC
1PD
FlatNC
1PD
WD
WD
Notes: This slide illustrates how the choice of the dielectric model affect the complex propagation constant and characteristic impedance of a micro-strip line. Attenuation with the wideband Debye and flat non-causal models are almost the same (metal losses are neglected in this example). Though their effective dielectric constants that characterize the imaginary part of the propagation constant are dramatically different. The real part of the characteristic impedance with the wideband model slowly grow with the frequency and imaginary part changing accordingly to maintain causality. Both parts of the impedance with the flat model are not changing with the frequency at all. One-pole Debye model parameters are close to the wideband over just one decade in frequency band around the measurement point.
<number>

## Slide 19: Building transmission line models with a field solver
07/30/26
© 2008 Simberian Inc.
<number>
Effect or Feature \ Solver | 2D Static Solvers | 2D Quasi-Static Solvers | 2.5D MoM Solvers | 3D FEM Solvers | 3D FDTD or FIT Solvers
Extracted parameters | C, L, Ro, Go Rs, Gs at 1GHz | L(f), R(f) | S(f), Y(f), Z(f) | S(f), Y(f), Z(f) | S(f), Y(f), Z(f)
P.U.L. RLGC(f) | No | R(f) and L(f) | No | No | No
Thin dielectric layers | Difficult | No | Yes | Difficult | Difficult
Transition to skin-effect | No | Yes | No | Difficult | No
Skin and proximity effects | Approximate | Yes with saturation | SIBC | SIBC | Difficult
Metal finishing | No | Difficult | No | No | No
Metal surface roughness | No | No | No | Resistivity adjustment | No
Dielectric dispersion | No | No | No | 1 and 2-pole models | 1 and 2-pole models
3D impedance | No | No | Yes | No | No
SIBC – Surface Impedance Boundary Conditions, works with well-developed skin-effect
Notes: To finalize the overview of advanced transmission line analysis, here is summary of different field solvers technologies and how they model a particular signal degradation effect. An ideal solver has to have yes for all rows. With a static solver you extract capacitance at DC, resistance and conductance at DC, inductance at infinity and loss matrices at 1GHz assuming well developed skin-effect. The intra-metal current redistribution effects cannot be simulated and no dielectric or high-frequency dispersion either. Magneto-quasi-static solver can be useful to simulate the conductor current redistribution with the frequency effects, but have multiple limitations too. And even 3D field solvers have limitations. It is difficult to create accurate models with incommensurably thin layers, frequency-dependent effects require computationally expensive algorithms in time-domain to be valid over 5-6 decades. Typically there are no models to simulate conductor finish and very approximate models for roughness. No automatic extraction of RLGC per unit length and 3D modal impedance.
<number>

## Slide 20: Agenda
07/30/26
© 2008 Simberian Inc.
<number>
Introduction
  De-compositional analysis of multi-gigabit channels
Building models for transmission lines
  Proximity, edge and skin-effects
  Surface roughness
  Metal plating
  Dielectric polarization and high-frequency dispersion and loss
Building models for differential via-holes
  Localizability
  De-embedding
  Effective via-hole impedance and geometry optimization
Conclusion
Notes: Another major obstacle to the high-speed signal on the board are via-holes. We will discuss only differential vias here, because of they essentially have better properties to transmit the signal through the board.
<number>

## Slide 21: Differential via-holes
07/30/26
© 2008 Simberian Inc.
<number>
Differential vias are two-via transitions through multiple parallel planes with possible stitching vias nearby
Two modes propagate independently trough a symmetrical pair
  Differential (+-) – two vias are two conductors: Id=0.5(I1-I2), Vd=V1-V2
  Common (++) – two vias one conductor and planes and stitching vias are another conductor: Ic=I1+I2, Vc=0.5(V1+V2)
Signal in differential pair always contain differential mode (useful) and may contain common mode induced by asymmetries in driver/receiver and by discontinuities
Notes: Differential via-holes is a pair of vias with optional stitching via-holes nearby. In case if via-holes are symmetrical, we can separate solution into solution for differential mode and common mode with current and voltages defined as shown here.
<number>

## Slide 22: Differential mode in via-holes
07/30/26
© 2008 Simberian Inc.
<number>
Differential mode has two identical currents on the via barrels
The via-holes can be isolated from the rest of the board for the electromagnetic analysis with any boundary conditions (PEC, PMC, PML, ABC)
  Distance from the vias to the simulation area boundaries should be large enough to avoid effect of sidewalls
  In that case, the differential mode S-parameters are practically independent of the boundary conditions
+ -
+ -
BC
BC
Notes: The differential mode contains two equal currents flowing in the opposite directions – technically it cancels the fields at relatively short distance from the vias. The problem can be isolated from the rest of the board with any boundary conditions at sufficient distance from the vias. In other words the problem is localizable.
<number>

## Slide 23: Common mode in differential via-holes going through multiple parallel planes
07/30/26
© 2008 Simberian Inc.
<number>
Planes are not terminated and the return current for common mode is the “displacement” current between the planes
  The problem is non-localizable – may require analysis of the whole board
Planes are terminated with the decoupling capacitors and the return current is a combination of the “displacement” currents through capacitors and planes
  The problem is non-localizable - decaps have low impedance only in a narrow frequency band
Stitching vias are used to connect the reference planes for the connected layers and the return current is mostly conductive
  Problem can be localized (localizable) and solved with any boundary conditions
+ +
+ +
BC
BC
+ +
+ +
+ +
+ +
BC
BC
BC
BC
Notes: It is not so simple with the common mode. In case if via-holes go through multiple planes – the return current is actually the displacement current of plane pairs. Without the planes the common mode causes radiation. The problem require simulation of the whole board with boundaries of the simulation area either at the edges of the boards or even outside. The problem is non-localizable. The same is valid for the problem with additional decoupling capacitors attached to the planes. Each decoupling capacitor provides low impedance in relatively low frequency band and at different frequencies capacitors at different locations on the board may be involved. It means that analysis of complete power distribution nets has to be done to predict the return path impedance for the common mode. Just one case is more or less localizable – case if ALL reference planes of the signal for the connected layers are connected or stitched with short-circuiting via-holes. Note that even in this case there will be some dependency on the simulation area and boundary conditions at high frequencies.
<number>

## Slide 24: Any 3D full-wave solver can be used to generate a model for localizable via-holes
07/30/26
© 2008 Simberian Inc.
<number>
# Hz S MA R 50
!Touchstone multiport model file <Project1_DifVias_Simulation1.s4p>
!Created with Simbeor 2007.05
!Frequency Hz |S[1,1]| arg(S[1,1]) |S[1,2]| arg(S[1,2]) |S[1,3]| arg(S[1,3]) |S[1,4]| arg(S[1,4])
! |S[2,1]| arg(S[2,1]) |S[2,2]| arg(S[2,2]) |S[2,3]| arg(S[2,3]) |S[2,4]| arg(S[2,4])
…
1e+007 0.00019967204037128 80.2602696805706 0.99996135358717 -0.0323490304593697 0.999961353587184 -0.0323490304593693 0.000199673211473872 80.2582768233478
0.000322468838468293 82.6000881350992 0.999950431873029 -0.0533202384129493 0.999950431873026 -0.0533202384194636 0.000322467239270051 82.6017028071304
...
...
2e+010 0.248547099289332 32.5237839600036 0.960378206732979 -58.1318674656129 0.960378206732979 -58.1318674656129 0.248469713303658 32.5058580236588
0.244570464339174 35.2840265413718 0.961777164971986 -55.3104068976763 0.961777164971987 -55.3104068976763 0.244498847955767 35.2671173277359
…
4-port
model
Port 1
Port 3
Electromagnetic solver generates Touchstone s4p file with tabulated scattering parameters:
Port 1
Port 2
Port 3
Port 4
Port 2
Port 4
Notes: If the problem is localizable – any 3D full-wave electromagnetic solver can be used to simulate it and produce a 4-port Touchstone model as shown on this slide.
<number>

## Slide 25: Multiport parameters extraction with de-embedding and reference plane shift
07/30/26
© 2008 Simberian Inc.
<number>
Non-reflective transition from the excitation to multiconductor t-lines
4-port
model
Port1
Port2
Port3
Port4
Phase reference plane shifted toward discontinuity
Distance to attenuate high-order modes reflected from discontinuity (near field)
“Pure discontinuity” is the result of de-embedding
Notes: But what about the simulation area. How large it should be? The simulation area should be large enough to avoid interaction of the via-holes near field with the simulation area boundaries. It means that the excitation of the problem with wave-ports or lumped ports has to be done at some distance from the via-holes. Such excitation must launch transmission line modes (differential and common as in this case) or be non-reflective. If the wave-ports are non-reflective we can shift the phase reference planes of S-parameters closer to the vias – at the edges of the anti-pads for instance. Elimination of the reflection from the simulation excitation area and shift of reference planes called de-embedding.
<number>

## Slide 26: Effect of de-embedding on multiport parameters
07/30/26
© 2008 Simberian Inc.
<number>
S1D1D
S1D2D
S1D1D
S1D2D
De-embedded
Not de-embedded
De-embedded
Not de-embedded
Non-reflective excitation ports (lumped or wave-ports) increase the model quality
Shift of reference planes makes model electrically smaller and reusable
Notes: The de-embedding increases the model quality, makes model electrically smaller, that is important if a reduced order model has to be constructed on the base of the “raw” S-parameters model, and finally it makes model independent of the transmission line segments attached to the via-holes during the extraction procedure – it makes the model easy to reuse. Note that the shift of the reference planes keeps the near field of the via-holes intact and when connected to other discontinuities the traces with sufficient length have to be added to avoid the distortion of the fields. If two discontinuities are close to each other (one discontinuity is in the near field of the other) they have to be simulated together.
<number>

## Slide 27: Estimation of the de-embedding quality
07/30/26
© 2008 Simberian Inc.
<number>
Analysis of a transmission line segment can reveal de-embedding defects
Analysis of 25, 50 and 100-Ohm benchmark strip line segments can be used for this purpose
Benchmarks from J.C. Rautio, IEEE on MTT, v.42, N11, 1994, p. 2046-2050.
S-parameters normalized to 25, 50 and 100 Ohm, segment length is 90 deg. at 15 GHz
No losses, no dispersion – |S21| must be unit |S11| must be zero
|S11| - defines dynamic range
Phase(S12) – deviation from 90 is the de-embedding error
Exact value
Notes: The de-embedding quality of your tool can be investigated with the analysis of a segments of transmission lines with exactly known impedances. Such benchmark examples were suggested by Rautio for instance. Three 90-degree segments of strip-lines with exactly 25, 50 and 100 Ohm impedances are simulated here. S-parameters normalized to 25, 50 and 100 Ohm have to have zero reflection, unit transmission and the phases of S21 have to be 90 degrees. The actual reflection defines the dynamic range of your tool (it is usually dependent on some meshing or accuracy parameters) and deviation from 90 will show the phase error of the simulator.
<number>

## Slide 28: Design of impedance-controlled differential via-holes
07/30/26
© 2008 Simberian Inc.
<number>
Effective impedance of via can be defined as the normalization impedance with minimal reflection |SD1D1| and maximal transition |SD1D2|
Optimal via-holes have effective impedance 100 Ohm
Original not optimal via-holes with pads in plane layers and small anti-pads (impedance 60 Ohm)
|S1D1D|
Optimal 100-Ohm via-holes without pads in plane layers and enlarged anti-pads
Acceptable reflection below -25 dB
Large reflection loss
Notes: Let’s assume that we have got through the model building process and extracted de-embedded S-parameters of the via-holes. The question is how to judge the quality of the transition. To do it an effective impedance can be defined as the impedance that provides minimal reflection and maximal transition for the differential mode over a given frequency band. According to this definition, via-holes with the effective impedance 100 Ohm is optimal for a channel with the differential impedance 100 Ohm. Here is an example of an optimal 100-Ohm via for a 6-plane board. Not-optimal via may have substantial reflection loss in a 100-Ohm channel.
<number>

## Slide 29: Not optimal via-holes can significantly degrade the signal at system-level
07/30/26
© 2008 Simberian Inc.
<number>
6-plane PCB
10-mil vias are 24 mil apart with 24 mil anti-pads and 16 mil pads in all layers, traces are 6 mil wide 10 mil apart
Pads in plane layers increase the capacitance and decrease the effective impedance of vias to 60 Ohm
Notes: Even a single not-optimal via may cause substantial reflection and signal degradation for a 10 Gbps signal for instance as illustrated on this slide.
<number>

## Slide 30: Even the optimal via-holes are not ideal transitions and require models
07/30/26
© 2008 Simberian Inc.
<number>
6-plane PCB
8-mil vias are 24 mil apart with 32 mil anti-pads and 20 mil pads only in signal layers, traces are 6 mil wide 10 mil apart
The effective impedance of vias is close to 100 Ohm over a wide frequency band
Notes: On the other hand, the optimal via is not ideal – such complicated geometrical structure can not behave a segment of 100-Ohm transmission line. Thus an S-parameter models have to be constructed even for the optimal vias to estimate its effect at the system level.
<number>

## Slide 31: Conclusion: Transmission line models
Build broadband models for data channels with data rates 10 Gbps and higher
Use 3D full-wave solvers to extract RLGC(f) matrix parameters per unit length for W-element
Use broadband and causal dielectric models
Have conductor models valid over 5-6 frequency decades in general
  Account for transition to skin-effect, shape and proximity effects at medium frequencies
  Account for skin, dispersion and edge effects at high frequencies
  Account for conductor surface finish and roughness
07/30/26
© 2008 Simberian Inc.
<number>
Notes: Read the slide.
<number>

## Slide 32: Conclusion: Via-hole models
Distinguish localizable and non-localizable cases
  Dependence of S-parameters from the boundary conditions usually shows that the problem is non-localizable
Only localizable cases can be analyzed with a 3D full-wave solver
  Differential mode propagation even without stitching vias
  Common mode propagation only with stitching vias nearby
Complete board analysis is required to build accurate models for non-localizable cases
  Hybrid distributed analysis with transmission plane solvers may be the best choice for such problems considering performance and accuracy
  Localized 3D full-wave differential via analysis can be embedded into the system-level hybrid solution to increase accuracy
07/30/26
© 2008 Simberian Inc.
<number>
Notes: Read the slide.
<number>