## Slide 1: EMI Parameters for IBIS
Guy de Burgh
EM Integrity
gdeburgh@nc.rr.com
DesignCon 2009
DesignCon 2009 IBIS Summit
February 5, 2009
Santa Clara, CA

## Slide 2: Introduction
Reason for this presentation
  Increasing interest in modeling EMI
  The parameters that exist today
Recap of BIRD 74
What’s next
DesignCon 2009

## Slide 3: Recap of BIRD 74
BIRD74_recap_a.pdf
  Will be uploaded to the IBIS web site along with this presentation
Contents
  History
  Why the BIRD was introduced
  EMI Mechanisms
  The Parameters
  Using the Parameters
  Reference Documents
DesignCon 2009

## Slide 4: BIRD 74 Parameters
Component
  Component Type Indicates whether the component is a connector.
  Domain Defines whether the component is Analog, Digital or both.
  Family Describes the logic family. This can be one of UNDEF, TTL, CMOS or ECL.
  Cpd Power Dissipation Capacitance. (Used to estimate DC power bus EMI)
  Die_height Height of the die within the package
  Heatsink Heatsink dimensions (used to calculate its capacitance)
DesignCon 2009
Notes: Component type Identifies the I/O nets. Also used in the description of the I/O pins (e.g. shielded, unshielded, con_to_shield, ferrite) to determine the impedance of the monopole antenna.
Domain Analog circuits operate a very low signal levels (mV or uV) and can contain high gain amplifiers. Digital circuits, in contrast, operate at relatively large signal levels (compared to Analog circuits). (See page 276 of reference [5].)
Family There’s no guarantee that an IBIS model is complete. This parameter allows you to make reasonable assumptions regarding missing information (e.g. source impedance, input impedance, max. transient switching current). E.g. an unused, floating, CMOS input is likely to pick up noise because of its high input impedance. This is true for all logic families with high input impedance. This noise could cause unintentional switching. In CMOS, however, an unused gate whose inputs are floating may bias itself into the linear region. This will increase the dc current drawn by the circuit. This is the most important parameter. With it you can make reasonable assumptions for all the other parameters. Note: Cpd only specified for Cmos devices. (See page 295 of reference [5].)
Cpd Cpd includes both internal parasitic capacitance (e.g., gate-to-source and gate-to-drain capacitance) and through currents present while a device is switching and both n-channel and p-channel transistors are momentarily conducting.
National Semiconductor, Texas Instruments, and Fairchild have datasheets and application notes on Cpd.
Cpd is also used for Thermal calculations.
Some catalogs give the value of “Dynamic Power Supply Current Iccd”. Where Iccd = Vcc * Cpd
Simultaneous switching of outputs are one of the main causes of transient noise voltages on the Power Bus resulting in common mode radiation.
From the EMI point of view we need to know the high frequency noise on each DC Power Bus due to the switching of digital circuits.
Fourier transform the transient current drawn from the power bus. Now knowing the current spectrum, the magnitude of each harmonic of the power bus noise voltage can be calculated. (See references [6] and [7].)

## Slide 5: BIRD 74 Parameters
Pin
  CSPEC name Describes a user definable name that corresponds to a model listed in the [Model] keyword. Used to define connector pin impedances. Only used when the component is a connector
Model
  Ferrite Indicates that the model for this pin is a ferrite.
  Cspec Assigns parameters to the pin CSPEC name. Possibilities are: the pin is Unshielded, Shielded (ground pins provide the shield), Shielded_pwr (power pins provide the shield), or Con_to_shield (pin connected to connector shell). In addition the pin can have an explicit filter capacitance. This is used to calculate an antenna impedance for the pin.
DesignCon 2009

## Slide 6: (Some) References
[1] J.L. Drewniak, T.H. Hubing, and T.P. Van Doren, “Investigation of Fundamental Mechanisms of Common-Mode Radiation from Printed Circuit Boards with Attached Cables,” Proceedings of the 1994 IEEE International Symposium on Electromagnetic Compatibility, Chicago, IL, August 1994, pp. 110-115.
[2] C.R. Paul, Introduction to Electromagnetic Compatibility, John Wiley Interscience, New York (1992).
[3] D.M. Hockanson, J.L. Drewniak, T.H. Hubing, T.P. Van Doren, F. Sha, C.-W. Lam, and L. Rubin, “Quantifying EMI Noise Sources Resulting from Finite-Impedance Reference Planes,” IEEE Transactions on Electromagnetic Compatibility, vol. EMC-39, no. 4, November 1997, pp. 286-297.
[6] S. Radu, R.E. DuBroff, T.H. Hubing, and T.P. Van Doren, “Designing Power Bus Decoupling for CMOS Devices,” Proceedings of the 1998 IEEE International Symposium on Electromagnetic Compatibility, Denver, CO, August 1998, pp. 375-380.
[7] J. Mao, B. Archambeault, J.L. Drewniak, and T.P. Van Doren, “Estimating DC Power Bus Noise,” IEEE EMC Symposium, Minneapolis, MN, August 2002, pp. 1032-1036.
[10] Katja Koller, Gerald Bannert, “Crossbar Current out of CMOS IBIS Models”, IBIS meeting at DATE 2002
DesignCon 2009

## Slide 7: What’s next
Information gathering
  What new parameters are needed?
  Reference documentation
  Cookbook
DesignCon 2009