## Slide 1: Mixed mode parameter support: definitions and transformations
Vladimir Dmitriev-Zdorov
February 5, 2009
IBIS Summit
Santa Clara, CA

## Slide 2: Linear multiports. Ports and pins (terminals)
Any Touchstone data file describes linear multiport system by means of NxN frequency-dependent matrix F (could be S, Y, Z or other type parameter matrix)
This matrix links ‘input’ and ‘output’ variable vectors, X and U of similar size (such as current, voltage, incident or reflected wave):
U = F X
Each vector component (variable) corresponds to a particular “port” of the multiport system
The set of port variables in the input and output vector (X and U) must be the same, identically ordered and without repetitions (no identical variables)
If the variables in X and U are differently ordered, then matrix F lacks some inherent properties (such as symmetry, diagonal dominance or positiveness of real part, etc.)
If there are repetitions or if port variables are not independent, the matrix becomes singular by structure (redundant)
Notes: To explain some requirements we have in the touchstone format specification (including common reference pin or identical reference impedance of port pairs) let’s consider the object of our investigation – linear multiport system.

## Slide 3
What is the port?
T1
T2
P1
I1
I1’
V1
Port is the place where we attach two terminal source or load to the multiport system. Port is made from pair of pins. Each port is defined by a single port current and voltage, or incident and reflected wave. The port current flows between port pins. The port voltage is measured between the same pins, in the same direction.
“Direct” and “return” currents must be identical.
Proper connection of multiports should also satisfy above requirement (regularity).
Valid port usage, consistent with port definition
T1
T2
P1
I1
I1’
V1
I2
Inconsistent port usage (I1 I1’), simulation results could be wrong

## Slide 4
How many independent ports we can define?
T1
T2
T3
T4
T5
T6
T7
T8
P1
P2
P4
I1
I1’
V1
P3
T1
T2
T3
T4
T5
T6
T7
T8
P1
P2
P3
P4
P5
P6
P7
If multiport has T terminals (pins) then # of ports should not be less than T/2 or more than T-1.
For example, if we define less than 4 ports for 8-terminal model, some of terminals will not be used.
If we define more than 7 ports, some of the variables will become linearly dependent
If we define less than 7 ports (T-1), some limitations are imposed on possible multiport connection

## Slide 5
What are requirements to mixed mode ports?
~
~
(a)
(Mixed Mode = Differential Mode + Common Mode)
Origination of the differential and common mode concept…
(a) Consider two ports with common reference pin (denoted as “ground”).
Each port is connected to ideal voltage source through the resistor (reference impedance)
~
…
(b)
~
~
(c)
(b) If the applied external voltages and reference resistances are equal, and the 2-port model is symmetric (ports have identical input characteristics), the currents in both branches are identical. Hence, the resistances can be connected in parallel and the 2-port model replaced by equivalent 1-port model. We call it ‘common mode port’.
If we take symmetrical model, but apply opposite voltages, the entire current circulates inside the contour; common ‘ground’ becomes disconnected. Again, we can define 1-port model by considering only signal pins of the original ports. This is differential port.
If the original model is not symmetric, the common mode partially converts into differential (port voltages and currents are not identical, difference current circulates inside the contour). Similarly, differential mode partly converts into common. Some nonzero current flows into common ‘ground’.
Note that above considerations require that (A) original ports have common reference pin and (B) have identical reference impedances.
1
2
1
2
1
2

## Slide 6
What are requirements to mixed mode ports?
X1
X2
X3
X4
D1,2
C1,2
C3,4
X1
X2
X3
X4
D3,4
C1,3
D1,3
D2,4
C2,4
X1
X2
X3
X4
X3
D1,2
???
C2,4
(a)
(b)
(c)
Each pair of SE or standard mode ports, having common reference pin and identical normalizing impedance can be converted into another 2-port model, with differential and common mode ports. Together, they constitute a mixed mode model. Complexity and number of variables is retained
Common reference pin is required for every port pair converted into mixed mode (MM). However, different pairs may have different reference pins and reference impedances.
Each standard port cannot participate in more than one standard-to-mixed mode conversion. Mappings (a) and (b) are legal, (c) is not.
X1
X2
X3
D1,2
C1,2
X3
(d)
Some of the ports may still remain in ‘standard mode’, others converted into MM (d). If standard port was used to create mixed mode port, it cannot remain in the standard mode.

## Slide 7
Types and indexes in variables define the content of the parameter matrix
D1,3 D2,4 C1,3 C2,4
Input vector content:
D1,3
D2,4
C1,3
C2,4
Output
Vector
content:
Matrix content
<D1,3 D1,3> <D1,3 D2,4> <D1,3 C1,3> <D1,3 C2,4>
<D2,4 D1,3> <D2,4 D2,4> <D2,4 C1,3> <D2,4 C2,4>
<C1,3 D1,3> <C1,3 D2,4> <C1,3 C1,3> <C1,3 C2,4>
<C2,4 D1,3> <C2,4 D2,4> <C2,4 C1,3> <C2,4 C2,4>
We only define this
We don’t need to define this
Matrix always retains structural symmetry

## Slide 8
X1
X2
X3
In Touchstone 2.0 format specification we allow mixed mode and single ended ports co-exist
[Mixed-Mode Order]
S<port> - single ended port with its original number
C<port>,<port> - common mode port originated from two other ports
D<port>,<port> - differential port, originated from two other single ports
[Reference] 20.0 20.0 50.0
[Mixed-Mode Order] D1,2 S3 C1,2
Mixed mode order keyword & definition
D1,2
X3
C1,2
D1,2
C1,2
X3
Compact definition, sufficient to track forward and hence required reverse transformation
In most cases, we need to convert the matrix back into its standard form, with variables properly ordered
Reference keyword – if present – refers to properly ordered single ended ports

## Slide 9
Transitions between standard and mixed mode variables
X1
X2
X3
X4
D1,2
C1,2
C3,4
D3,4
2
1
4
3
D1,2
C1,2
C3,4
D3,4
X1
X3
X2
X4
D1,3
C1,3
C2,4
D2,4
D1,3
C1,3
C2,4
D2,4
X1
X2
X3
X4
3
1
4
2
conversion
permutation
permutation
permutation
conversion
Example 1
Example 2
In general, we perform permutation of STD parameters, block-wise conversion of pairs into MM parameters, and permutation of MM parameters
Reverse transition contains similar steps (exact mirror)
If we know port indexes (original STD port numbers) unambiguous reverse transition is possible
How this can be made mathematically?

## Slide 10
Permutation applied to vectors and matrices
X3
X2
X4
X1
X1
X2
X3
X4
=
0
0
1
0
0
1
0
0
1
0
0
0
0
0
0
1
Column shows previous position in the vector
Row shows new position
UP = P * U0
Output vector permutation:
Input vector permutation:
XP = P * X0
Matrix is non-singular
Has exactly one ‘1’ in every row and column
Transpose is its inverse: Pt = P-1
Parameter matrix permutation:
FP = P F0 Pt
Requires left and right multiplication on permutation matrix and its transpose, to identically reorder rows and columns (i.e. symmetry is preserved)
Permutation applies to all types of vectors and matrices identically (a, b, V, I and S, Y, Z)
(1)

## Slide 11
Mode conversion for a pair of ports
ad1,2
ac1,2

-


=
a1
a2
S-parameters: b = S a, bmm = Smm amm
where
Single ended incident wave vector to MM incident wave vector:
bd1,2
bc1,2

-


=
b1
b2
Single ended reflected wave vector to MM reflected wave vector (identical to above):
ad1,2
ac1,2


-

=
a1
a2
MM incident wave vector to SE or standard vector:
bd1,2
bc1,2


=
b1
b2
MM reflected wave vector to SE vector (identical to above):
-

In a more formal way:
S-parameter matrix undergoes 2-side transformation:
(2)

## Slide 12
Mode conversion for a pair of ports
vd1,2
vc1,2
1
-1
0.5
=
v1
v2
Y and Z parameters: I = Y V, V = Z I,
Imm = Ymm Vmm , Vmm = Zmm Imm
Single ended voltage to MM voltage:
id1,2
ic1,2
=
i1
i2
Single ended current MM current (differs from above!):
vd1,2
vc1,2
=
v1
v2
MM voltage to SE or standard voltage vector:
id1,2
ic1,2
=
i1
i2
MM current vector to SE vector:
In a formal way:
0.5
0.5
-0.5
1
1
0.5
-0.5
1
1
1
-1
0.5
0.5
where:
Theoretically, mode conversion for Y and Z types could be made exactly same way as for S-parameters, with same matrices. However, we proceed from existing definitions of the mixed mode voltage and current:

## Slide 13
What’s the difference between S and non-S type conversion?
a1
a2
ac
ad
b1
b2
bc
bd
v1
v2
vc
vd
i1
i2
ic
id
S
Y/Z
S parameter style conversion between STD and MM is represented by rotation
Y or Z parameter conversion between STD and MM is represented by rotation and scaling
Scaling does not affect effective power from the common and differential components
The ratio between modules of voltage and current vectors in STD and MM form differs by factor 2 and ½. From here, it follows that reference impedance of differential mode is twice the STD impedance, common is half of it.
Theoretically, the conversion similar to S-parameters can also be applied to Y and Z parameters. However, as we stick to conventional definitions of differential and common mode voltage and current, we have to use different conversion formulas
Geometrical interpretation of mode conversion

## Slide 14
Mode conversion for a pair of ports
Y and Z parameters:
All types of STD/MM conversions are made by congruent transformations with matrices whose abs(eig()) all equal 1.
(3)
(4)
Similar to standard parameters, we have:
(2)
S parameters:

## Slide 15
Mode conversion for a pair of ports What happens if two ports have identical properties?
If single ended ports 1 and 2 have identical properties, 2x2 standard mode parameter matrix has identical diagonal components. This translates into purely diagonal MM matrix.

## Slide 16
How to convert multi-port parameters into standard mode
By inspection, as shown on slide 10, create permutation matrix Pmm that collects all pairs of differential and common mode ports together. Apply two side multiplication to the parameter matrix, as in (1)
Apply appropriate mode conversion, as in (2)-(4), by multiplying the matrix on two mutually transposed matrices from left and right. In case of several (N) pairs of ports, the conversion matrices consist of N diagonal 2x2 blocks
After all mixed mode pairs are converted into standard parameters, they should be properly re-ordered, according to the port numbers. This requires additional permutation by two side multiplication on matrix Pstd.
For example:
First perm
Mode conversion
Second permutation
More details in Touchstone File format specification, Appendix A

## Slide 17
4-port example
3
1
4
2
[Mixed-Mode order]
D1,3 D2,4 C1,3 C2,4
D1,3
C1,3
C2,4
D2,4
D1,3
C1,3
C2,4
D2,4
1. MM permutation
2. Mode conversion
S1
S3
S4
S2
D1,3
D2,4
C2,4
C1,3
3. STD permutation
S1
S3
S4
S2
S1
S2
S4
S3

## Slide 18
Consistency of the matrix conversion
As follows from considered relations, including (1)-(4), and the fact that transformation matrices are not frequency dependent, conversion from mixed mode into standard and reverse preserves such basic properties as:
Matrix symmetry (reciprocity of the system):
Passivity:
Causality: every matrix component obeys e.g. Kronig-Kramers relation
Geometrical symmetry (between port 1 and 2) creates diagonal sub-matrices in MM
The procedure outlined above is a convenient illustration that serves as a guideline. Practical implementations may include some modifications (i.e. finding a single matrix, combining permutation and mode conversion, etc.)
More details in Touchstone File format specification, Appendix A

## Slide 19
Transformation between parameter types (S/Y/Z) in mixed mode
We do not define here direct transformations between different parameter types in mixed mode
These transformations have been defined for the standard mode parameters, including the case of different reference impedances
Given these transformations, and conversions between MM and STD modes shown in this document, it is straightforward to derive transformations between different parameter types in MM
Due to different scaling in STD to MM conversions, the transformations between S/Y/Z parameters in mixed mode are formally different from similar transformations in standard mode
Ymm
Smm
Ystd
Sstd
Can be uniquely defined
known
defined
defined

## Slide 20
Thank you!