## Slide 1: How IBIS Models Relate to SI, PI, and EMI-EMC
Roy Leventhal
DesignCon 2009
IBIS Summit Meeting
Santa Clara, CA
February 5, 2009

## Slide 2: An Example of a Complex Network
An 18-Slot Bi-Directional Backplane Bus
Notes: <header>
<date/time>

## Slide 3: Simulation Results from too Simple a Model
Complex nets are hard to terminate and have many reflections
Simple dV/dt modeling and device behavior is inadequate
V-T curves need to be modeled for correct results in GTL/GTLP busses
Notes: <header>
<date/time>

## Slide 4: IBIS Modeling of V-T Curves How GTLP Really Behaves
This slide shows how to correctly model GTL/GTLP
Soft turn-on/turn-off removes many high-frequency components (think about Fourier transformation) from driving the line
The results of the change in modeling detail are shown next:
Notes: <header>
<date/time>

## Slide 5: Better Models Give Better Results
“Everything should be as simple as possible and no simpler.” -----Albert Einstein
Notes: <header>
<date/time>

## Slide 6: Test Net for SI and EMI
66MHz Clock Topology as Modified Courtesy of Hamilton-Sundstrand
Notes: <header>
<date/time>

## Slide 7: How SI is Affected by Overshoot
Before Termination After Termination
Before termination, SI and stress on the receiver is not a high concern – the real payoff will be in EMI control as shown in the next slide.
Notes: <header>
<date/time>

## Slide 8: How EMI is Affected by Overshoot
Before Termination After Termination
The SI Engineer has to manage harmonics out to about the 5th .
The EMI engineer has to manage harmonics out to, perhaps, the 100th.
Notes: <header>
<date/time>

## Slide 9: Example of Virtual Test Board
 | The board on the left has the following stackup: top: 1.2 mil Cu signal Zo = 89 next: 12 mil FR4 (r = 4.5) next: 1.2 mil Cu shield Vcc next: 12 mil FR4 next: 1.2 mil Cu shield GND next: 12 mil FR4 bottom: 1.2 mil Cu signal Zo = 89 Etch width is nominally 6 mils For the shielded version outer shield layers of 1.2 mil Cu spaced by 12 mils of FR4 were added The nominal 6 mil etch on such an inner layer results in Zo = 59.6  The board is about 3 inches long.
Layout of the Test Board | Stackup of the Test Board
Notes: <header>
<date/time>

## Slide 10: Virtual Test Board Before and After EMI Treatment
Unshielded, Unterminated, Non-Constant Impedance Net | Shielded, Terminated, Constant Impedance Net
Notes: <header>
<date/time>

## Slide 11: Near Field EMI Simulators
Image Courtesy of Johnson Controls Automotive, Inc. Used with permission

## Slide 12: PI and the IEC 62014-3 Proposal
Slide courtesy of Etienne Sicard, INSA-Toulouse
What is happening with IEC 62014-3?
Notes: <header>
<date/time>

## Slide 13: Bypassing the Power Supply for PI
      Slide courtesy of Lee Ritchey, Speeding Edge
Reminder to myself: Let’s have a discussion of some of the latest PCB techniques for controlling power plane bounce, crosstalk, and emissions
Notes: <header>
<date/time>

## Slide 14: 3D Full-Wave EMI Simulators
Baseline
Ground Pins Only
Standoffs Only
Pins and Standoffs
Strong Coupling to Slot-WHY?
Slide courtesy of FloEMC used with permission

## Slide 15: Far-Field EMI Simulators
U1 Star com Box
U1 Star com Box
Slide courtesy of FloEMC used with permission
Notes: <header>
<date/time>

## Slide 16: The Virtual Test Bench
Slide courtesy of Jerry Meyerhoff, Continental AG, and CST/FloEMC. Used with permission.
Notes: <header>
<date/time>

## Slide 17: Modelers Need to Use the Language of the Frequency Domain in Talking to EMI Engineers
Before
Plots of a typical regulatory EMI problem and its solution
After

## Slide 18: Summary
EMI
  Is driven by the strength and speed of the output driver
  Is driven by the discontinuities of the transmission net
  Extends to much higher harmonics than SI issues
EMI can be controlled by sophisticated techniques for resolving the problems created by high-speed drivers
EMI issues at the PCB, enclosure, and system level can be studied with sophisticated CEM tools. CEM facilitates the study of EMI design tradeoffs related to models and net design.
Modelers use time domain concepts. EMI Engineers use frequency domain concepts. They need to communicate in each other’s language.

## Slide 19
http://www.semiconductorsimulation.com
http://www.semiconductormodel.com
Roy.Leventhal@ieee.org
847-590-9398