## Slide 1: Primer on Mixed-Mode Transformations in Differential Interconnects DesignCon IBIS Summit, Santa Clara, February 5, 2008
Copyright © 2009 by Simberian Inc. Reuse by written permission only. All rights reserved.
Yuriy Shlepnev
shlepnev@simberian.com
Notes: <number>

## Slide 2: Agenda
Introduction
Mixed-mode transformations and geometrical symmetry
Double micro-strip line bend
Investigation of micro-strip channel with two reversed bends in frequency and time domain
Experimental validation
Possible ways to minimize the mode transformation
Conclusion
07/28/26
© 2009 Simberian Inc.
<number>

## Slide 3: Introduction
07/28/26
© 2009 Simberian Inc.
<number>
Transformation from differential to common modes is unwanted effect in differential interconnects
  Common mode may cause differential signal degradation (skew) and electromagnetic emission
Transformation usually takes place at bends and non-symmetrical routing near via-holes
The most accurate way to quantify the effect is in the frequency domain with S-parameters in the mixed-mode space
In case of bends the transformation effect can be simulated with the local electromagnetic analysis
This presentation contains some practical observations on the estimation and minimization of the mode transformation effect
Experimental validation provided by Teraspeed Consulting Group
Simbeor 2008 software has been used for all computations
Notes: <number>

## Slide 4: Mode transformation in reciprocal 4-port
See details in D.E. Bockelman, W.R. Eisenstadt, Combined differential and common-mode scattering parameters: Theory and simulation, IEEE Trans. on MTT, vol. 43, 1995, N7, p. 1530-1539
07/28/26
© 2009 Simberian Inc.
<number>
2
1
3
4
C1
D1
D2
C2
[S]
[Smm]
Mode Transformation Terms:
Terminal space
Mixed-mode space
All S-matrices are symmetrical (S[i,j]=S[j,i]) due to reciprocity property (if only isotropic materials used to manufacture interconnects)
- congruent transformation preserves matrix symmetry

## Slide 5: Mixed-Mode Terminology
Block DC describes modal transformations or conversion (highlighted blocks of the mixed-mode S-parameters)
07/28/26
© 2009 Simberian Inc.
<number>
C1
D1
D2
C2
[Smm]
Notation used here:
Alternative forms:
S[D1,C1], S[D2,C2] – Near end mode transformation or transformation from differential to common mode at the same side of the multiport
S[D1,C2], S[D2,C1] – Far end mode transformation or transformation from differential mode on one side to the common mode on the opposite side of the multiport
Transformation from common to differential is exactly the same due to reciprocity (symmetrical S-matrix)

## Slide 6: Properties of S-parameters of reciprocal 4-port with geometrical mirror symmetry
Group theory can be used to investigate properties of S-matrix a 4-port with geometrical symmetry – see details in R.H. Dicke - Symmetry of waveguide junctions, in Montgomery, Dicke, Purcell, Principles of Microwave Circuits, 1964
07/28/26
© 2009 Simberian Inc.
<number>
S-matrix of reciprocal 4-port is symmetric as shown below (S[i,j]=S[j,i]):
Group generator for mirror symmetry operator for 4-port structure:
S-matrix must commute with F:
It means that:
Final S-matrix of reciprocal symmetrical 4-port:
2
1
3
4
Holds for mirror or axial symmetry with the plane or axis along the propagation direction
only 6 independent parameters

## Slide 7: Mode transformation in reciprocal 4-port with geometrical mirror symmetry
07/28/26
© 2009 Simberian Inc.
<number>
2
1
3
4
C1
D1
D2
C2
Terminal space
Mixed-mode space
Mode Transformation Terms are Zeroes!
No mode transformation!
[Smm]

## Slide 8: NO Mode Transformation Condition
Mirror symmetry about the plane along the interconnects is the necessary and sufficient condition of no mode transformation
07/28/26
© 2009 Simberian Inc.
<number>
Rotational symmetry about the axis along the interconnect is another case that is less interesting for practical applications
Port 1
Port 2
Port 3
Port 4
Traces
Symmetry plane
NO TRANSFORMATION from Differential to Common mode and back – follows from the symmetry property

## Slide 9: Typical interconnect elements that cause mode transformations
All share one property – no symmetry of type discussed above
07/28/26
© 2009 Simberian Inc.
<number>
Can be simulated locally:
May require board-level simulation to capture common mode behavior (hybrid or full-wave):
Bypass or “length equalization” elements as shown:
Bends (single and dual):
Non-symmetrical break-out from vias:
With stitching vias between all reference planes of the connected lines – can be simulated locally (conditional on the distance between vias)

## Slide 10: Double bend in micro-strip line: Materials and Stackup
07/28/26
© 2009 Simberian Inc.
<number>
Materials:
  Copper bulk resistivity 1.724e-8 Ohm meters, roughness 0.5 um (roughness factor 2)
  Solder mask: DK=3.3, LT=0.02
  FR-4 core dielectric: DK=4.7, LT=0.02 @ 1 GHz
  FR-4 dielectric between signal and plane layers: DK=4.25, LT=0.02 @ 1 GHz
  All dielectrics are modeled with the Wideband Debye model

## Slide 11: Mode transformation at micro-strip line bend
07/28/26
© 2009 Simberian Inc.
<number>
Small near end mode transformation S[D1,C1]
Large far end mode transformation S[D1,C2]
C1
D1
D2
C2
[Smm]
Composed of two 45-deg bends
Strip width 15 mil, separation 22 mil
Mode transformation due to non-symmetry
-5.5 dB
156 mil
95 mil
Two-port inputs are de-embedded and S-parameters phase reference planes are shifted to these planes

## Slide 12: Can we compensate the transformation?
By using reversed bend to match the length of the traces?
07/28/26
© 2009 Simberian Inc.
<number>
250-mil segment
200-mil segment
200-mil segment
S-parameters of simulated bends
Small near end transformation S[D1,C1]
Still large far end transformation S[D1,C2]
Far end transformation has been reduced by 10 dB, but did not disappear even with ideal match of the trace lengths!
-15.5 dB
D1
C1
D2
C2

## Slide 13: What is the reason of the transformation in case with dual bends?
Difference in the propagation velocities of differential and common modes in micro-strip line:
  Difference in the group velocities is about 6% over the frequency band
07/28/26
© 2009 Simberian Inc.
<number>
Strip width 15 mil, separation 22 mil
Group velocities
Differential mode
Common mode

## Slide 14: What if we move bends closer?
Parametric sweep with the Distance between two bends as a parameter allows us to investigate this scenario
07/28/26
© 2009 Simberian Inc.
<number>
Distance
200-mil segment
200-mil segment
S-parameters of simulated bends
The smaller the Distance between the bends, the smaller the far end mode transformation coefficient S[D1,C2]
1 GHz
5 GHz
10 GHz
15 GHz
20 GHz
D1
C1
D2
C2

## Slide 15: What about the near end mode transformation coefficient?
The Distance between two bends does not have much effect on the maximal value of the near end mode transformation coefficient
07/28/26
© 2009 Simberian Inc.
<number>
Distance
200-mil segment
200-mil segment
S-parameters of simulated bends
Though, the level of S[D1,C1] is relatively small (below -20 dB) due to 45-degree section used in each bend
1 GHz
5 GHz
10 GHz
15 GHz
20 GHz
D1
C1
D2
C2

## Slide 16: Effect of mode transformation on signal degradation in time domain
10 Gbps NRZ bipolar pulse train with 10 ps rise and fall time and 1 V magnitude, 100 Ohm termination for differential mode and 25 Ohm for the common mode
07/28/26
© 2009 Simberian Inc.
<number>
250-mil segment
200-mil segment
200-mil segment
S-parameters of simulated bends
Acceptable signal degradation can be observed - partially due to the mismatch of the source (100 Ohm) and the differential mode (about 96 Ohm) – almost no skew!
D1
C1
D2
C2

## Slide 17: Possible effect of mode transformation on EMI
10 Gbps NRZ bipolar pulse train with 10 ps rise and fall time and 1 V magnitude, 100 Ohm termination for differential mode and 25 Ohm for the common mode
07/28/26
© 2009 Simberian Inc.
<number>
250-mil segment
200-mil segment
200-mil segment
S-parameters of simulated bends
Without termination and with some other favorable conditions 15 mV injected into common mode may cause radiation (EMI problem)
D1
C1
D2
C2

## Slide 18: Experimental validation
PLRD-1 low cost FR4 board created and independently investigated by Teraspeed Consulting Group www.teraspeed.com
Stackup is the same as in the previous numerical examples
All structures are equipped with optimized SMA connectors and investigated from 300 KHz to 20 GHz
07/28/26
© 2008 Teraspeed Consulting Group LLC
© 2008 Simberian Inc.
<number>
Differential dual bend (non-symmetrical structure)
Segment of differential line (symmetrical structure)

## Slide 19: Differential line segment: Correspondence of measured and simulated results
07/28/26
© 2009 Simberian Inc.
<number>
Magnitudes of single-ended S-parameters (1 row)
Measured (stars)
Simulated (circles)
Transmission (green)
Good correspondence of the model and experiment both for single-ended and mixed-mode S-parameters.
FEXT (brown)
NEXT (blue)
Reflection (red)

## Slide 20: Mode transformation in the differential line segment
Numerical model predicts zero mode transformation due to the mirror symmetry about the plane along the wave propagation direction
07/28/26
© 2009 Simberian Inc.
<number>
C1
D1
D2
C2
[Smm]
In reality, non-symmetry of connectors, glass fiber in dielectric and trace manufacturing tolerances cause small mode transformations!
Any optimization of mode transformation below this floor level (-25 dB in that case) does not make sense.
Far end mode transformation
Near end mode transformation

## Slide 21: Differential bends: Comparison with de-embedded measurement results
07/28/26
© 2008 Teraspeed Consulting Group LLC
© 2008 Simberian Inc.
<number>
Magnitudes of mixed-mode S-parameters (DD block)
Measured (stars)
Simulated (circles)
Differential mode reflection
Good correspondence!
C1
D1
D2
C2
[Smm]
Differential mode transmission

## Slide 22: Differential bends: Mode transformation
Acceptable correspondence between the measurements and simulation
07/28/26
© 2009 Simberian Inc.
<number>
C1
D1
D2
C2
[Smm]
Theoretical and experimental differential to common mode transformation despite the identical lengths!
Far end mode transformation
Near end mode transformation
Measured – stars Simulated – circles
De-embedding noise below -25 dB
-16 dB @ 20 GHz may become -8 dB if distance between the bends is extended to 1 inch

## Slide 23: How to minimize the mode transformation?
Reduce size of the bends to minimize both far and near end mode transformation
Use dual or complimentary discontinuities with forward and reversed mode transformation as close to each other as possible to minimize far end mode transformation in micro-strip channels
Use strip line structure with equal common and differential mode propagation velocity to reduce far end mode transformation
  Disadvantages of such configuration are via-hole transitions to get to the strip layer and stitching vias for both reference planes for possibility to predict the common mode behavior
See more practical examples in Simberian App Note #2009_01 available at www.simberian.com/AppNotes.php
07/28/26
© 2009 Simberian Inc.
<number>

## Slide 24: Conclusion
07/28/26
© 2009 Simberian Inc.
<number>
Transformation of differential mode to common mode in interconnects is unavoidable if structures without the mirror symmetry such as bends are used
Amount of energy transformed into common modes at the bends can be effectively estimated with localized full-wave electromagnetic analysis and S-parameters in the mixed-mode space
Configurations and patterns that minimize the transformation can be derived on the base of the numerical investigation of interconnects
Even structures with the mirror symmetry by design may have mode transformation due to non-symmetries introduced by dielectric structure and manufacturing tolerances – the transformation value can be used as the floor for the mode transformation optimization
Transformation may have minor effect on signal quality (signal integrity), but may have more serious consequences on EMI if common mode is not appropriately terminated