## Slide 1: Quality metrics for S-parameter models DesignCon IBIS Summit, Santa Clara, February 4, 2010
Copyright © 2010 by Simberian Inc. Reuse by written permission only. All rights reserved.
Yuriy Shlepnev
shlepnev@simberian.com
Notes: <number>

## Slide 2: Agenda
Introduction
Reciprocity metric
Passivity metric
Causality metrics
Global quality metrics
Examples
Conclusion
Contacts and resources
07/28/26
© 2010 Simberian Inc.
<number>

## Slide 3: Introduction
07/28/26
© 2010 Simberian Inc.
<number>
S-parameter models are becoming ubiquitous in design of multi-gigabit interconnects
  Connectors, cables, PCBs, packages, backplanes, … can be characterized with S-parameters from DC to daylight
Such models come from measurement or electromagnetic analysis
And very often have some quality issues
  Passivity and reciprocity violations
  Causality problems
Notes: <number>

## Slide 4: If You happen to…
Build interconnect models for internal use
Send interconnect models to customers developing consumer products
Confirm models with measurements or electromagnetic analysis
Use models for compliance level testing
…
You need to have…
07/28/26
© 2010 Simberian Inc.
<number>

## Slide 5: Pristine S-parameters
07/28/26
© 2010 Simberian Inc.
<number>
Reciprocal (no non-linear anisotropic materials)
Passive (interconnects do not generate energy)
Causal – no response before the excitation
Stable analysis in time domain
What if some of those properties are violated – can we still use such model and trust the results?
This presentation introduces metrics to distinguish good models from bad ones and methodology to improve the model quality for consistent frequency and time-domain analyses

## Slide 6: Reciprocity
Linear circuits with linear isotropic materials are reciprocal according to Lorentz’s theorem of reciprocity: Reflected wave measured at port 2 with incident wave at port 1 is equal to reflected wave measured at port 1 with the same incident wave at port 2
In general it means that the scattering matrices are symmetric
07/28/26
© 2010 Simberian Inc.
<number>
at all frequencies
Notes: Circuits with non-linear elements or with anisotropic materials (magnetized ferrites for instance) are non-reciprocal – S-matrices may be not symmetric in those cases
<number>

## Slide 7: Reciprocity estimation and enforcement
Example of S-parameters of reciprocal 4-port interconnect (symmetric matrix):
07/28/26
© 2010 Simberian Inc.
<number>
2
1
3
4
[S]
Reciprocity measure can be computed as mean difference between elements that have to be equal (at each frequency point):
RM is compared with a threshold: if RM > threshold, the multiport is reported as not reciprocal
Averaging can be used to “enforce” the reciprocity (works only with noisy data):
or max singular value of can be used
Notes: Reciprocity is the fundamental property of multiports built with reciprocal materials and linear components (non-reciprocal and non-linear materials are not used in interconnects)
<number>

## Slide 8: Passivity (necessary but not sufficient conditions)
Power transmitted to multiport is a difference of power transmitted by incident and reflected waves: or
Transmitted power is defined by Hermitian quadratic form and must be not negative for passive multiport for any combination of incident waves
Quadratic form is non-negative if eigenvalues of the matrix are non-negative (Golub & Van Loan):
07/28/26
© 2010 Simberian Inc.
<number>
(U is unit matrix)

## Slide 9: More on passivity
Maximal singular value of S can be used for passivity estimation, because of non-zero singular values of S are square roots of eigenvalues of S*S (Golub & Van Loan)
Passivity of symmetric S can be estimated with eigenvalues as
  It is possible due to the fact that singular values of symmetric matrices are equal to the magnitudes of the eigenvalues
Common mistake is to estimate passivity as:
07/28/26
© 2010 Simberian Inc.
<number>
or
This is necessary but not sufficient condition!
Notes:   In case of non-symmetric matrix - eigen-values of non-symmetric matrix do not have correspondence to singular values in general
<number>

## Slide 10: Passivity estimation and enforcement
Passivity conditions for S-parameters (energy dissipation condition):
07/28/26
© 2010 Simberian Inc.
<number>
Passivity measure is computed at each frequency point as:
PM is compared with a threshold: if PM > threshold, the multiport is reported as not passive
Normalization at each frequency point can be used to “enforce” the passivity (works only with minor violations):
is equal to max singular value of S
Alternatively a rational filter can be used
Notes: System does not generate energy if it contains only passive elements - interconnects are always passive
<number>

## Slide 11: Causality in frequency-domain
Condition for the unit pulse response matrix and leads to Kramers-Kronig relations for the frequency-domain parameters (Hilbert transform)
Imaginary part can be derived from real (or vice versa), but the other part must be known from DC to infinity
07/28/26
© 2010 Simberian Inc.
<number>
Kramers, H.A., Nature, v 117, 1926 p. 775..
Kronig, R. de L., J. Opt. Soc. Am. N12, 1926, p 547.
derivation
Notes: Real and imaginary parts are clearly dependent
Originally derived for dielectric constants, but applicable for all multiport parameters (S/Y/Z)!
<number>

## Slide 12: Causality estimation - difficult way
Kramers-Kronig relations cannot be directly used for the frequency-domain response known over the limited bandwidth
Causality boundaries can be introduced to estimate causality of the tabulated and band-limited data sets
  Milton, G.W., Eyre, D.J. and Mantese, J.V, Finite Frequency Range Kramers Kronig Relations: Bounds on the Dispersion, Phys. Rev. Lett. 79, 1997, p. 3062-3064
  Triverio, P. Grivet-Talocia S., Robust Causality Characterization via Generalized Dispersion Relations, IEEE Trans. on Adv. Packaging, N 3, 2008, p. 579-593.
07/28/26
© 2010 Simberian Inc.
<number>

## Slide 13: Causality estimation - easy way
“Heuristic” causality measure based on the observation that polar plot of a causal system rotates mostly clockwise (suggested by V. Dmitriev-Zdorov)
07/28/26
© 2010 Simberian Inc.
<number>
Plot of Re(S[i,j]) as function of Im(S[i,j]), or polar plot
Start frequency
End frequency
Rotation in complex plane is mostly clockwise around local centers
Re
Im
Causality measure (CM) can be computed as the ratio of clockwise rotation measure to total rotation measure in %.
If this value is below 80%, the parameters are reported as suspect for possible violation of causality.
Notes: Exact estimation of causality of a system described with a frequency-domain response within a limited frequency band is not possible in general
Alternative causality measure is Root Mean Square (RMS) Error of a Rational approximation of tabulated data (always causal)
<number>

## Slide 14: Causality improvement
Filtration or decimating – the simplest technique, but may further degrade the response quality
Artificially extend real or imaginary part, or magnitude of the frequency response to DC and to the infinity and restore the other part with the Kramers-Kronig equations
  The restored part will strongly depend on the artificial extension
  Iterative extension adjustment is possible to improve accuracy over the sampled frequency band - difficult to implement
Fit the response with causal rational basis functions (use rational compact model)
  Provides controlled accuracy over the sampled frequency band
  Consistent results in both frequency and time domains
  Can be extended to DC and to infinity
07/28/26
© 2010 Simberian Inc.
<number>
Notes: Small measurement noise can be eliminated with moving average or Gaussian filtration or decimating – the simplest technique, but may further degrade the response quality if the response is under-sampled
<number>

## Slide 15: Use of Rational Compact Model (RCM) for S-parameters causality “improvement”
Pulse response is real and delay-causal
Stable
Passive if
Reciprocal if
07/28/26
© 2010 Simberian Inc.
<number>
May require enforcement
Continuous functions of frequency
Notes: Can be converted in broad-band SPICE model for consistent TD and AC analyses
<number>

## Slide 16: What are RCMs for?
Improve quality of tabulated Touchstone models
  Fix minor passivity and causality violations
  Interpolate and extrapolate with guarantied passivity
Produce broad-band SPICE models
  Much smaller model size
  No artifacts and guarantied stability of SPICE simulation
  Consistent frequency and time domain analyses
Compute time-domain response of a channel with a fast recursive convolution algorithm (exact solution for PWL signals)
07/28/26
© 2010 Simberian Inc.
<number>

## Slide 17: Global quality metrics (0-100%)
Passivity Quality Measure: PQM or zero if PQM<0
Reciprocity Quality Measure: RQM or zero if RQM<0
Causality Quality Measure: Minimal ratio of clockwise rotation measure to total rotation measure in % (should be >80%)
RMS error of the rational compact model can be also used to characterize the causality of the original data set
07/28/26
© 2010 Simberian Inc.
<number>
should be >98%
should be >98%

## Slide 18: Example 1: High-quality model
07/28/26
© 2010 Simberian Inc.
<number>
100% Passive (good)
98.4 % Reciprocal (good)
Causality problem, but it can be restored with RCM
Single controlled via from PLRD-1 benchmark board – SOLT calibration
Data provided by Teraspeed Consulting Group

## Slide 19: Single controlled via (SOLT): Improving S-parameters with RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
RCM model has RMS Error is 0.0034 (very good), is passive from DC to infinity and 100% causal and reciprocal
Touchstone model with DC and reduced number of frequency points or BB SPICE model can be produced from RCM
RCM (circles)
VNA (stars)
transmission
reflection

## Slide 20: Single controlled via (SOLT): Original S[1,1] and RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
VNA Measurement: 3201 points starting from 300 KHz
Re-sampled RCM: 769 points distributed adaptively starting from 0 Hz
CAUSAL!
Visible noise and large segments with counter-clockwise rotation
S[1,1]
Red line – original VNA
Green line with circles - RCM

## Slide 21: Single controlled via (SOLT): Original S[1,1] and RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
Stars – VNA data
Circles – RCM
RCM: 46 poles, RMS Error 0.0034
Re(S11)
Im(S11)
Practically indistinguishable!

## Slide 22: Single controlled via TDR from RCM (SOLT)
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
From measured S[1,1]
20 ps rise time
Measured TDR
Z(t)
Z(t)
Launches
Z1
Z2
Port 1
Port 2
Minor non-symmetry in the impedance profile: SQM=72%
via
Good correspondence!

## Slide 23: Example 2: Model that needs improvement
07/28/26
© 2010 Simberian Inc.
<number>
97.5 % Reciprocal (acceptable)
Causality is 17.7%, that is even slightly better than the original SOLT 9.5%
TRL Reference Planes (250 mil from via)
Passivity violated at few points PQM=99.95% (acceptable)
Passivity and reciprocity worsened comparing to SOLT, but still OK
Data provided by Teraspeed Consulting Group
Single controlled via from PLRD-1 benchmark board – TRL calibration

## Slide 24: Single controlled via (TRL): Causality problems both in transmission and reflection
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
TRL Reference Planes (250 mil from stubs)
S[1,2]
S[2,2]
Some problems both in the transmission and reflection parameters (can be fixed):
Port 1
Port 2
CCW rotation

## Slide 25: Single controlled via (TRL): Improving S-parameters with RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
RCM RMS Error is 0.045 (still OK)
Passive from DC to infinity, causal and reciprocal
Problem is in the reflection parameters and RCM “fixes” it with the best possible fit
Problematic areas due to “oscillating” reflection are “fixed”
RCM
TRL
Transmission and group delay is OK

## Slide 26: Single controlled via (TRL): Original S[1,2] and RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
VNA Measurement: 3201 points starting from 300 KHz
Re-sampled RCM: 633 points distributed adaptively starting from 0 Hz
CAUSAL!
Very noisy data is corrected with RCM!
S[1,2]

## Slide 27: Single controlled via (TRL): Original S[2,2] and RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
<number>
VNA Measurement: 3201 points starting from 300 KHz
Re-sampled RCM: 633 points distributed adaptively starting from 0 Hz
Does not match well but CAUSAL 
Very noisy non-causal data with wrong rotation!
S[2,2]
S[2,2]
Red line – original TRL data
Green line with circles - RCM

## Slide 28: Single controlled via (TRL): Original S[2,2] and RCM
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
Problematic non-causal areas are fitted as close as possible
RMS Error 0.045, 44 poles
Does the corrected data contain information about the via?
Stars – original TRL data
Circles – RCM model
Re(S22)
Im(S22)

## Slide 29: Single controlled via TDR from RCM (TRL)
<number>
07/28/26
© 2010 Teraspeed Consulting Group LLC
© 2010 Simberian Inc.
Pure via in a t-line: no connector and launch discontinuities
V(t)
time, sec
Blue curve: from measured S-parameters
Brown curve: from EM model of via
Good correspondence – all via properties are preserved and the model is actually usable in the time and frequency domains!
TRL Reference Planes (250 mil from stubs)

## Slide 30: Conclusion
<number>
Reciprocity, passivity and causality of interconnect component models must be verified before use
  Measured models may be not acceptable for the analysis
  Electromagnetic models may have severe problems too
Quality metrics allow distinguishing minor “fixable” violations with acceptable accuracy degradation from severe violations
Rational macro-models with controllable accuracy can be used to “improve” tabulated models and to correct minor violations of passivity and causality
Standardization of the quality metrics and exchange formats for rational compact models are needed
07/28/26
© 2010 Simberian Inc.

## Slide 31: Contact and resources
Yuriy Shlepnev, Simberian Inc.
  shlepnev@simberian.com
  Cell: 206-409-2368
Free version of Simbeor 2008.L0 used to plot and estimate quality of S-parameters is available at www.simberian.com
To learn on quality metrics further see slides from DesignCon2010 tutorial (also available on request)
  TF-MP12 H. Barnes, Y. Shlepnev, J. Nadolny, T. Dagostino, S. McMorrow, Quality of High Frequency Measurements: Practical Examples, Theoretical Foundations, and Successful Techniques that Work Past the 40GHz Realm
07/28/26
© 2010 Simberian Inc.
<number>