## Slide 1
[External Test Load/Data] Concepts
DesignCon IBIS Summit, Santa Clara, CA
Feb 3, 2011
Anders Ekholm, Ericsson & Mike LaBonte, Cisco Systems

## Slide 2
IBIS Quality Task Group
Status:
Correlation discussion put on hold for now
A BIRD draft to improve the [Test Data] and [Test Load] structures of the IBIS spec was introduced by Anders Ekholm and is currently discussed
An [External Test Load/ Test Data] BIRD has been drafted by Anders Ekholm (Ericsson) and Mike LaBonte (Cisco systems)
This BIRD draft is the current topic of weekly IQ meetings

## Slide 3
|
| V_term1
| o-----------o
| | |
| \ \ receiver_model_name
| ______ / / ______
| | | NEAR Rp1_near \ \ Rp1_far FAR | |
| | |\ | / / | |\ |
| | | \ | Rs_near Ls_near | _____ | Ls_far Rs_far | | \ |
| | | >-|---o--/\/\--@@@@--o----o--O_____)--o----o--@@@@--/\/\--o---|-| > |
| | | / | | | | Td | | | | | / |
| | |/ | | C1_near | \ Zo \ | C2_far | | |/ |
| |______| === === / / === === |______|
| | C2_near | \ \ | C1_far |
| | | / / | |
| | | | V_term2 | | |
| o--------------o o-----------o o--------------o
| | Rp2_near Rp2_far |
| GND GND
|
[External Test Load/Data] Concepts
[Test Load] limitations
Size of [Test Data] (internal to IBIS file)
[Test Data] limited to single edge stimuli (no pulse train)
[Test Load] limited to a fixed topology (inflexible)
Limited differential load support
Bench measured [Test Data] usually can not be measured at pad
[Test Load] has probe points only at pads
Buffer models
Without pin parasitics

## Slide 4: [External Test Load/Data] Concepts
Improvements over [Test Load] / [Test Data]
Full pulse train stimulus
More general/flexible test load topology
Larger test data sets possible
IBIS File: Buffer
..
[External Test Load]
..
[External Test Data]
..
[External Test Stimulus]
Test_load.iss
(Test load in IBIS Interconnect
Spice Subcircuit format)
Test_data.csv
(Format needs to be defined.)
Test_stimuli.csv
(Format needs to be defined.
Also may define internal [Test Stimulus])

## Slide 5: [External Test Load/Data] Concepts
[External Test Data]
  Kept in a separate file, size not as limiting
  Support more than two probe points
[External Test Load]
  Support more than two probe points
  Any load supported by IBIS-ISS can be used
  Probe points defined as .subckt terminals
  Easily re-used for many models
[External Test Stimulus]
  Any pulse train possible
  Idealized transition times used (no rise/fall time)
Test_data.csv
(Format needs to be defined)
Test_load.iss
(Test load in IBIS-ISS SPICE format.)

## Slide 6
Notes: External load bird
2010-12-07
<number>