## Slide 1: IBIS-ISS Introduction and Futures
IBIS Interconnect Task Group
Presented by Michael Mirmak
Intel Corporation
IBIS Summit at DesignCon
February 3, 2011
Portions presented during Nov. 2010 Asian IBIS Summits

## Slide 2: Agenda
The Problem of SPICE* Model Portability
The Concept of IBIS-ISS
What Is and Isn’t Supported
Status and Future Directions
Summary

## Slide 3: A Standard SPICE* Does Not Exist
What does the following SPICE* statement do?
  Bexample 1 2 I=sin(V(3,0))
Results depend on the SPICE tool you use
  IBIS or non-linear dependent source?
Ambiguous elements exist across SPICEs
  Other non-universal elements include P, W, Y, Z
  Recall “The 3S Proposal” from June 2007 DAC Summit
    http://www.eda.org/ibis/summits/jun07/mirmak2.pdf
How do you ensure a model works in your tool or your customers’ tools?

## Slide 4: A Solution for SI/PI Interconnects
SPICE* netlists include interconnects, devices and engine commands
  e.g., .tran analysis for a driver and receiver on a PCB trace
IBIS supports portable device models directly
Engine commands are specific to EDA tools
How to ensure interconnect models are portable?
  Package, via, connector, PCB trace, on-die PDN…
IBIS-ISS: an industry baseline for interconnect modeling in SPICE

## Slide 5: IBIS-ISS in Simple Terms
IBIS-ISS: IBIS Interconnect SPICE* Subcircuits
Defines a limited set of common, basic elements useful for SI interconnect modeling
Based on documents and concepts donated by Synopsys as seen in Synopsys HSPICE*
  Originally assembled and edited by Walter Katz, SiSoft
Developed with SI community through IBIS Interconnect Task Group
  EDA vendors, IC vendors and system vendors

## Slide 6: What Is (and Is Not) Supported
Fundamental circuit elements
  Resistors, Inductors, Capacitors: R, L, K, C
  Dependent Sources: E, F, G, H
  Transmission Lines: T, W (including tabular, Foster, etc.)
  S-parameters: S (Touchstone)
Subcircuit definitions and instantiation
  .subckt, .ends, X element
Other basic commands
  .include, .param
… but no engine commands, no active device support, and no field solver

## Slide 7: Usage Model
IBIS-ISS consists entirely of subcircuits and subcircuit definitions
  IBIS-ISS does not define netlists
  Subcircuits may be nested or independent
All parameters are local, and passed explicitly
Multiple files are supported (.include)
Compliant tools simply accept IBIS-ISS files
  Meaning, properly apply IBIS-ISS assumptions within the scope of the top-level subcircuit

## Slide 8: How Does It Work?
.subckt my_trace_group 1 2 3 4 5 6 7 8 ref length=5e-3
* Units are meters
* This is a top-level subcircuit
* The user/system designer will instantiate this circuit in a netlist
Xtrace_a 1 ref 2 ref single_trace local_length=length
Xtrace_b 3 ref 4 ref single_trace local_length=length
Xtrace_c 5 ref 6 ref single_trace local_length=length
Xtrace_d 7 ref 8 ref single_trace local_length=length
* This circuit assumes no crosstalk
.subckt single_trace in local_ref out local_ref local_length=1
Wsingle in local_ref out local_ref N=1 L=‘local_length’
+ TABLEMODEL=‘single_line_table’
.include ‘single_line_table.inc’
* This file defines the tabular data using .MODEL
* This file should also be written using ISS rules
.ends
.ends

## Slide 9: Announcement
Draft 1.0 is officially submitted to the IBIS Open Forum for review and approval as a standard!
  http://www.eda.org/ibis/ibis-iss_wip/

## Slide 10: Issues and Future Directions
Items of controversy
  Independent voltage sources vs. external power ports
  Replaces ICM?
Links to other specifications
  MCP? EMD?
  IBIS? EBD?
  Touchstone 2.x and port/node mapping?
A parser is under consideration
Possible extensions?
  IBIS-ISS as basis for behavioral device model format?

## Slide 11: Summary
If you model interconnects, IBIS-ISS can help ensure usability across SPICE* tools
If you use SPICE of any kind, IBIS-ISS will be familiar to you
IBIS-ISS will be reviewed in the next few IBIS Open Forum meetings for official approval
Please study, discuss and comment on the IBIS-ISS draft.
Your contributions are important!

## Slide 12: References
Documents and background materials on-line:
  http://www.eda.org/ibis/interconnect_wip/
Mailing list available for updates and discussion:
  http://www.freelists.org/list/ibis-interconn/