## Slide 1: Reflections on S-parameter Quality DesignCon IBIS Summit, Santa Clara, February 3, 2011
Copyright © 2011 by Simberian Inc. Reuse by written permission only. All rights reserved.
Yuriy Shlepnev
shlepnev@simberian.com
Notes: <number>

## Slide 2: Outline
Introduction
Quality of S-parameter models
Rational macro-models of S-parameters and final quality metric
Examples
Conclusion
Contacts and resources
<number>
© 2011 Simberian Inc.

## Slide 3: Introduction
<number>
S-parameter models are becoming ubiquitous in design of multi-gigabit interconnects
  Connectors, cables, PCBs, packages, backplanes, … ,any LTI-system in general can be characterized with S-parameters from DC to daylight
Electromagnetic analysis or measurements are used to build S-parameter Touchstone models
Very often such models have quality issues:
  Reciprocity violations
  Passivity and causality violations
  Common sense violations
And produce different time-domain and even frequency-domain responses in different solvers!
© 2011 Simberian Inc.
Notes: <number>

## Slide 4: What are the major problems?
<number>
Model bandwidth deficiency
  S-parameter models are band-limited due to limited capabilities of solvers and measurement equipment
  Model should include DC point or allow extrapolation, and high frequencies defined by the signal spectrum
Model discreteness
  S-parameter models are matrix elements at a set of frequencies
  Interpolation or approximation of tabulated matrix elements may be necessary both for time and frequency domain analyses
Model distortions due to
  Measurement or simulation artifacts
  Passivity violations and local “enforcements”
  Causality violations and “enforcements”
Human mistakes of model developers and users in general
© 2011 Simberian Inc.
Notes: <number>
In general, use of different algorithms in EDA or in-house tools to increase the bandwidth, interpolate data, enforce quality and to do time-domain analysis lead to differences in the responses.

## Slide 5: Pristine models of interconnects
Must have sufficient bandwidth matching signal spectrum
Must be appropriately sampled to resolve all resonances
Must be reciprocal (linear reciprocal materials used in PCBs)
Must be passive (do not generate energy)
Have causal step or pulse response (response only after the excitation)
07/30/26
© 2011 Simberian Inc.
<number>
from DC to infinity!

## Slide 6: What if models are not pristine?
Reciprocity, passivity and causality metrics was recently introduced for the model pre-qualification at DesignCon 2010 IBIS summit (references at the end)
Models with low metrics must be discarded!
Models that pass the quality metrics may still be not usable or mishandled by a system simulator
The main reasons are band-limitedness, discreteness and brut force model fixing
<number>
© 2011 Simberian Inc.

## Slide 7: Computation of system response requires frequency-continuous models
<number>
Fourier Transforms
pulse response matrix
stimulus
system response – time domain (TD)
scattering matrix
stimulus
system response – frequency domain (FD)
For TD analysis we can either use Discrete Fourier Transforms (DFT) and convolution or approximate discrete S-parameters with frequency-continuous causal functions with analytical pulse response
FD
TD
© 2011 Simberian Inc.
Notes: Integrals in these equations and infinite limits of the integration are the major problem when we are doing time domain computations with tabulated S-parameters defined at a discrete set of frequencies. Even computations in frequency domain are not trivial, because of a channel component models may be discretized differently and S-matrix interpolation is not trivial task.
<number>

## Slide 8: Rational approximation of S-parameters is such frequency-continuous model
Pulse response is analytical, real and delay-causal:
Stable
Passive if
Reciprocal if
<number>
May require enforcement
Continuous functions of frequency defined from DC to infinity
© 2011 Simberian Inc.
Notes: Rational approximation is particularly suitable for S-parameters. S-parameters of any LTI system can be approximated with the rational functions over a limited frequency band. There is a form of rational approximation with multiple delays.
<number>

## Slide 9: Bandwidth and sampling for rational approximation
If no DC point, the lowest frequency in the sweep should be
  Below the transition to skin-effect (1-50 MHz for PCB applications)
  Below the first possible resonance in the system (important for cables, L is physical length)
The highest frequency in the sweep must be defined by the required resolution in time-domain or by spectrum of the signal (by rise time or data rate)
The sampling is very important for DFT and convolution- based algorithms, but not so for algorithms based on fitting
  There must be 4-5 frequency point per each resonance
  The electrical length of a system should not change more than quarter of wave-length between two consecutive points
<number>
© 2011 Simberian Inc.
Notes: Ideally the response should be measured from DC to optical frequencies, but in reality we have to decide on lowest and highest frequency and on sampling (number of points and location)
<number>

## Slide 10: Rational approximation can be used for
Compute time-domain response of a channel with a fast recursive convolution algorithm (exact solution for PWL signals)
Improve quality of tabulated Touchstone models
  Fix minor passivity and causality violations
  Interpolate and extrapolate with guarantied passivity
Produce broad-band SPICE macro-models
  Smaller model size, stable analysis
  Consistent frequency and time domain analyses in any solver
Measure the original model quality with the Root Mean Square Error (RMSE) of the rational approximation:
07/30/26
© 2011 Simberian Inc.
<number>

## Slide 11: So, how to avoid bad S-parameters?
Use reciprocity and passivity metrics for preliminary analysis
  RQM and PQM metrics should be > 80%
Use the rational model quality metric as the final measure
  QM should be > 90%
Otherwise discard the model
  The main reason is we do not know what it originally was and should be – no information
<number>
© 2011 Simberian Inc.

## Slide 12: Example 1: Network with one real pole – shunt capacitor sampled up to 50 GHz
13 pF capacitance shunt to the ground
1
2
Identified with RMSE=8.0e-7 (~100%)
Sampled up to 50 GHz with 1 GHz step (circles)
C
real pole at 489.707 MHz can be identified with just 5 frequency samples
Identified with RMSE=1.0e-6 (~100%)
Sampled up to 50 GHz with 10 GHz step (stars)
Zero at infinity
2-ps pulse responses are identical and practically independent of discretization in the frequency domain!
No artifacts!
<number>
© 2011 Simberian Inc.
Notes: Even 4 samples is sufficient for the identification. Increase of the number of samples or there position does not increase the accuracy of the RCM.

## Slide 13: Example 1: Network with one real pole – shunt capacitor sampled up to 5 GHz
13 pF capacitance shunt to the ground
1
2
Identified with RMSE=5.4e-7 (~100%)
Sampled up to 5 GHz with 100 MHz step (circles)
C
real pole at 489.707 MHz can be identified with just 5 frequency samples
Identified with RMSE=9.3e-7 (~100%)
Sampled up to 5 GHz with 1 GHz step (stars)
Still no artifacts!
2-ps pulse responses are identical and practically independent of discretization in the frequency domain!
<number>
© 2011 Simberian Inc.
Notes: If we reduce the bandwidth to just 5 GHz, the model is still usable and provides very accurate pulse or step response.

## Slide 14: Example 2: Network with two complex poles – shunt RLC circuit sampled up to 50 GHz
Shunt tank: C=13 pF, L=50 pH, R=1 K
Identified with RMSE=6.4e-7 (~100%)
Sampled up to 50 GHz with 1 GHz step (circles)
resonance at 6.24 GHz can be identified with 5 frequency samples
Identified with RMSE=6.7e-7 (~100%)
Sampled up to 50 GHz with 10 GHz step (stars)
2-ps pulse responses are identical and practically independent of discretization in the frequency domain!
<number>
© 2011 Simberian Inc.
Notes: There is a pair of complex conjugate poles here. Again, even 4 samples is sufficient for the identification. Increase of the number of samples or there position does not have much effect on the accuracy of the RCM.

## Slide 15: Example 2: Network with two complex poles – shunt RLC circuit sampled up to 5 GHz
Shunt tank: C=13 pF, L=50 pH, R=1 K
Identified with RMSE=9.8e-7 (~100%)
Sampled up to 5 GHz with 100 MHz step (circles)
resonance at 6.24 GHz can be identified with 5 frequency samples
2-ps pulse responses are identical and practically independent of discretization in the frequency domain!
Identified with RMSE=3.4e-7 (~100%)
Sampled up to 5 GHz with 1 GHz step (stars)
<number>
© 2011 Simberian Inc.
Notes: Samples below the resonance allow to identify the whole model from DC to infinity with very high accuracy!

## Slide 16: Example 3: Network with infinite number of poles – segment of ideal transmission line
T-line segment: Zo=50 Ohm, Td=1 ns 50 Ohm termination
|S11| is exactly 0 from DC to infinity
|S12| is exactly 1 from DC to infinity
Phase is growing linearly
Group Delay is exactly 1 ns from DC to infinity
Such network is obviously non-physical
We will try to sample and approximate |S21| over some frequency band and compare the step responses
Exact response to 100 ps delayed step with 20 ps rise time (10-90%)
1.1 ns
0.5
V
0
T
<number>
© 2011 Simberian Inc.
Notes: 1 ns is about 12 inches in the air and 6 inches on PCB. What would be the frequency band to simulate the response of such system? 25 or 50 GHz?

## Slide 17: Example 3: Segment of ideal transmission line sampled up to 25 GHz
Sampled with adaptive frequency sweep from 1 MHz to 25 GHz (628 samples) – stars and pluses on the left graph
Approximated with rational macro-model with 100 poles (RMSE=0.0037, Q=99.63) – solid lines on left graph and TD graph
|S11|
Group Delay
Ripples due to energy above 25 GHz
Non-causality?
<number>
© 2011 Simberian Inc.
Notes: The case is typically interpreted as non-causality. Though, it is just bandwidth deficiency of the original model. Delay extraction in this case would produce the exact response.

## Slide 18: Example 3: Segment of ideal transmission line sampled up to 50 GHz
Sampled with adaptive sweep from 1 MHz to 50 GHz (1278 samples) – stars and pluses on the left graph
Approximated with rational macro-model with 190 poles (RMSE=0.0045, Q=99.55) – solid lines on left graph and TD graph
|S11|
Group Delay
Smaller ripples due to small energy above 50 GHz!
Spectrum of ramped step stimulus still exceeds the bandwidth of the model!
<number>
© 2011 Simberian Inc.
Notes: Extension of the bandwidth reduces the ripples, but they still visible even with the bandwidth is twice as necessary for the analysis! Sharp corners of the ramp stimulus have frequency harmonics above

## Slide 19: Example 3: Segment of ideal transmission line sampled up to 50 GHz
No ripples in the computed time-domain response – model bandwidth matches the excitation spectrum!
Gaussian step stimulus with 20 ps rise time (10-90%) Spectrum: -20 dB at 44 GHz and -40 dB at 62 GHz
Gaussian Step (ideal step filtered with the Gaussian filter)
Rational Macro-Model Response
No corners
No ripples!
<number>
© 2011 Simberian Inc.

## Slide 20: Practical examples from panel TP-T3
<number>
Acceptable (see next slides)
Discard
Acceptable
Common sense analysis of system response may be also useful
© 2011 Simberian Inc.
Notes: Fred is marginally acceptable. It is actually a useful model with the restricted bandwidth. It has large bandwidth and appropriate sampling, but it cannot be approximated with high accuracy and passive continuation to infinity at the same time! Causality and passivity here are the same thing.
<number>

## Slide 21: Acceptable Measured Model Example: U-shaped 10-in differential link
Model supplied by Peter Pupalaikis (LeCroy), 2001 points from 0 to 40 GHz
4 by 4 S-matrix is approximated with rational macro-model with 300-400 poles per element, max RMSE=0.055, Q=94.5%
|SD1D2|
|SD1D1|
Rational Macro-Model
There is transmission along the traces and additional pad-to-pad transmission at all frequencies
<number>
© 2011 Simberian Inc.
Notes: Rational macro-model and measured data are practically on top of each other. From |SD1D2| we can see that there is no transmission saturation as expected. It means that in addition to the path along the traces, signal propagates directly between the probes (or vias). Group delay also supports this conclusion.

## Slide 22: Acceptable Measured Model Example: U-shaped differential link TDT
40 ps 10-90% Gaussian step response (-20 dB at 22 GHz, -40 dB at 31 GHz)
The response shows clearly that there are “shortcuts” in the system
Any “causality enforcement” may be erroneous for such cases!
~0.2 ns
~2.1 ns
<number>
© 2011 Simberian Inc.
Notes: “Enforcing” causality you can easily throw the baby with the bathwater. In this case the sideway transmission is not substantial, but it may be different from case to case.

## Slide 23: Conclusion
<number>
Models must be appropriately sampled over the bandwidth matching the signal spectrum
Reciprocity, passivity and causality of interconnect component models must be verified before use
  Both measured and computational models may have severe problems and not acceptable for any analysis
Rational macro-models with controlled accuracy over the model frequency band can be used to
  Do consistent frequency and time domain analyses
  Estimate quality of the tabulated models
Bad models with small quality metrics must be discarded
© 2011 Simberian Inc.

## Slide 24: Contact and resources
Yuriy Shlepnev, Simberian Inc.
  shlepnev@simberian.com
  Tel: 206-409-2368
Free version of software used to plot and estimate quality of S-parameters is available at www.simberian.com
To learn more on S-parameters quality see the following presentations (also available on request):
  Y. Shlepnev, Quality Metrics for S-parameter Models, DesignCon 2010 IBIS Summit, Santa Clara, February 4, 2010
  H. Barnes, Y. Shlepnev, J. Nadolny, T. Dagostino, S. McMorrow, Quality of High Frequency Measurements: Practical Examples, Theoretical Foundations, and Successful Techniques that Work Past the 40GHz Realm, DesignCon 2010, Santa Clara, February 1, 2010.
  E. Bogatin, B. Kirk, M. Jenkins,Y. Shlepnev, M. Steinberger, How to Avoid Butchering S-Parameters, DesignCon 2011
07/30/26
© 2011 Simberian Inc.
<number>