## Slide 1: A System Developer's Perspective on AMI
Greg Edlund
February 2, 2012

## Slide 2: Agenda
AMI user’s experience at IBM
AMI Check List
DLL verification

## Slide 3: State of AMI at IBM
Two years into the effort
Models from three suppliers
Iterated with suppliers to get DLL to run
Simulator evaluation is in round two
Model-to-hardware correlation in progress
IBM’s internal simulator supports AMI
No hardware yet designed with AMI models

## Slide 4: Ideal TX & RX with 20 in. of 4-mil wire

## Slide 5: Swapped in AMI model…

## Slide 6: Example simulation from supplier

## Slide 7: AMI Check List
Completeness
Usage
Documentation
Accuracy
Statement of understanding between AMI supplier and
customer; communication of expectations.

## Slide 8: Completeness
.ibs file passes syntax checker
TX .ami and .dll files
RX .ami and .dll files
Analog model included in .ibs file
Touchstone package model(s)
RX training algorithm included in DLL
List other software necessary to run simulations

## Slide 9: Usage
All files distributed in a single archive
Model installation directory independent of execution directory
Support for Windows and Linux
Multiple instances of one model will run in one simulation/analysis
Multiple instance of multiple models will run in one simulation/analysis
Support for multiple simultaneous simulations/analyses (parallel processing)
Unrecognized parameters do not cause failure

## Slide 10: Usage, con’t
Useful parameter description
Model returns correct results at any samples-per-bit setting
Ability to manually override equalizer settings
No double counting of package, e.g. s-parameters and .ibs file
No double counting of C_Comp, e.g. s-parameters and .ibs file

## Slide 11: Documentation
Support contact information
User guide
Software used to develop model
Simulator(s) and version used to test model
Company that developed model
Company that designed serializer-deserializer (serdes) circuit
Company that manufactured chip
Type of TX equalization and number of taps
Type of RX equalization and number of taps
S-parameter port map

## Slide 12: Accuracy
Lab report to include:
  TX jitter decomposition measurements
  RX stressed eye testing
  Model-to-hardware correlation
  Proof of industry standard compliance
Does the PHY have an “on-chip oscilloscope” feature and software?
Will the PHY output a test pattern with an oscilloscope connected?
PRBS length?

## Slide 13: IBM’s PHY Lab Report: PVT Corners

## Slide 14: IBM’s PHY Lab Report: TX Jitter

## Slide 15: IBM’s PHY Lab Report: RX Stressed Eye

## Slide 16: DLL Test Bed
DLL
0100011000100
impulse
response
Convolution
Engine
report
GetWave