## Slide 1: Case Study: IBM 15Gb IBIS-AMI Model using Dependency Tables Adge Hawes, IBM; Walter Katz, SiSoft
DesignCon IBIS Summit, Santa Clara, CA
02 Feb 2012

## Slide 2: The IBM 15Gb Chip-to-Chip (C2C) Core
Chip-chip only (lower cost)
Cu032 technology
15.0 Gb operation (12.5Gb for 1.05v termination voltage)
3 FFE taps
1 DFE tap
AGC
Dynamic Peaking (15 filter settings)

## Slide 3: The IBM 15Gb Chip-to-Chip (C2C) Core – User settings
4 Corners
  Nominal, Best, Worst, Extreme
Termination Voltage (2 settings)
  1.20V or 1.05V operation
NEGZ control (2 settings)
  Switches in a stronger level of peaking
H1Limit (4 settings)
  DFE limit algorithm
FC1667 noise integration bandwidth (2 settings)
  Uses different Rx RJ parameters
Tx coupling (2 settings)
  AC or DC
Gain (3 settings)
  Reflects characteristics of AGC gain, different on-die S-parameters and peaking profile
Tx power setting
140 support files covering all combinations

## Slide 4: AMI configuration - conventional
2 versions of "Corner" mapping
  (Nom, Best, Worst) & (Nom, Best, Extreme)
2 versions for VTT/VTR
  1.05V and 1.20V
2 versions for NEGZ control
3 versions for "gain" settings
  mid, min, max
4 versions for H1Limit
2 versions for RJ version
Perhaps 192 AMI configuration files to choose from, e.g.
"VTR1_05NEGZ0midH10FC0W.ami"

## Slide 5: Dependency Tables
Allow parameter values to be dependent on user selection of other variables
Resolved by the EDA tool before simulation
Expands the number of corners that may be simulated
Dependent conditions can have multiple effect
  i.e. more than one variable can be dependent
Variable substitution can reduce table entries
Drastically reduces the number of configuration files required
Was BIRD 124

## Slide 6: AMI Configuration using Dependency Tables: User Variables
(txcorner (Usage Info) (Type String) (Description "Tx Corners") (List "nc" "wc" "bc" "ec")) (cmode (Usage Info) (Type String) (Description "Coupling mode") (List "ac" "dc")) (VTT (Usage Info) (Type Float) (Description "Transmitter terminal voltage") (List 1.05 1.20)) (txpow (Usage Info) (Type Integer) (Description "Tx power register") (Range 60 32 64))
(rxcorner (Usage Info)(Type String) (Description "Corners") (List "nc" "wc" "bc" "ec")) (gain (Usage Info)(Type String) (Description "S-parameter gain settings") (List "mid" "min" "max")) (negz (Usage Info)(Type Integer) (Description "NEGZEN bit") (List 0 1)) (VTR (Usage Info)(Type Float) (Description "Receiver terminal voltage") (List 1.05 1.20)) (H1limit (Usage Info)(Type Integer) (Description "DFE H1 Limit") (Range 3 0 7)) (Fc1667 (Usage Info)(Type Integer) (Description "Fc/1667 (6Mz) noise integration bandwidth") (List 0 1))

## Slide 7: IBM 15G C2C Dependencies
Transmitter Voltage level
  PWL relationship to TXPOW user setting
SJ magnitude
  Corner, mode, VTT/VTR
On-die S-parameters (Tx/Rx)
  Corner, gain, NEGZ, VTT/VTR
Peaking Filters
  Corner, gain, VTR, NEGZ
AGC
  Corner, VTR
Rotator Linearity
  Corner, VTR, baud rate

## Slide 8: AGC Dependency Table example
(Rx_AGC_Dependency_Table (Usage Info) (Type String Float Float Float Float Float) (Table (Labels "rxcorner In" "VTR In" "RX_Receiver_Sensitivity Out_Range" "agcmax Out_Range" "agcmin Out_Range" "agclev Out_Range") ("ec" 1.05 0.018 1.460 0.293 0.247) ("wc" 1.05 0.016 1.490 0.285 0.260) ("nc" 1.05 0.013 1.338 0.258 0.264) ("bc" 1.05 0.015 1.220 0.241 0.281) ("ec" 1.20 0.019 1.567 0.292 0.216) ("wc" 1.20 0.018 1.607 0.292 0.226) ("nc" 1.20 0.016 1.464 0.271 0.245) ("bc" 1.20 0.012 1.330 0.256 0.260) ) )

## Slide 9: Rx IC and Peaking Dependency Table
(rx_Dependency_Table (Usage Info) (Type String String Integer Float String String) (Table (Labels "rxcorner In" "gain In" "negz In" "VTR In" "Tstonefile Out_Range" "rxcte Out_Range") ("nc" "mid" 0 1.05 ".../ncAVTR1_05negzen0gain_dec255peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_05negzen0gain_dec255.cte.ami") ("nc" "mid" 0 1.20 ".../ncAVTR1_2negzen0gain_dec255peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_2negzen0gain_dec255.cte.ami") ("wc" "mid" 0 1.05 ".../wcAVTR1negzen0gain_dec255peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1negzen0gain_dec255.cte.ami") ("wc" "mid" 0 1.20 ".../wcAVTR1_1negzen0gain_dec255peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1_1negzen0gain_dec255.cte.ami") ("bc" "mid" 0 1.05 ".../bcAVTR1_08negzen0gain_dec255peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_08negzen0gain_dec255.cte.ami") ("bc" "mid" 0 1.20 ".../bcAVTR1_26negzen0gain_dec255peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_26negzen0gain_dec255.cte.ami") ("nc" "min" 0 1.05 ".../ncAVTR1_05negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_05negzen0gain_dec0.cte.ami" ) ("nc" "min" 0 1.20 ".../ncAVTR1_2negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_2negzen0gain_dec0.cte.ami" ) ("wc" "min" 0 1.05 ".../wcAVTR1negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1negzen0gain_dec0.cte.ami" ) ("wc" "min" 0 1.20 ".../wcAVTR1_1negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1_1negzen0gain_dec0.cte.ami" ) ("bc" "min" 0 1.05 ".../bcAVTR1_08negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_08negzen0gain_dec0.cte.ami" ) ("bc" "min" 0 1.20 ".../bcAVTR1_26negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_26negzen0gain_dec0.cte.ami" ) ("ec" "min" 0 1.05 ".../ecAVTR0_95negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ecAVTR0_95negzen0gain_dec0.cte.ami" ) ("ec" "min" 0 1.20 ".../ecAVTR1_05negzen0gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ecAVTR1_05negzen0gain_dec0.cte.ami" ) ("nc" "max" 0 1.05 ".../ncAVTR1_05negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_05negzen0gain_dec65535.cte.ami" ) ("nc" "max" 0 1.20 ".../ncAVTR1_2negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_2negzen0gain_dec65535.cte.ami" ) ("wc" "max" 0 1.05 ".../wcAVTR1negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1negzen0gain_dec65535.cte.ami" ) ("wc" "max" 0 1.20 ".../wcAVTR1_1negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1_1negzen0gain_dec65535.cte.ami" ) ("bc" "max" 0 1.05 ".../bcAVTR1_08negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_08negzen0gain_dec65535.cte.ami" ) ("bc" "max" 0 1.20 ".../bcAVTR1_26negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_26negzen0gain_dec65535.cte.ami" ) ("ec" "max" 0 1.05 ".../ecAVTR0_95negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ecAVTR0_95negzen0gain_dec65535.cte.ami" ) ("ec" "max" 0 1.20 ".../ecAVTR1_05negzen0gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ecAVTR1_05negzen0gain_dec65535.cte.ami" ) ("nc" "mid" 1 1.05 ".../ncAVTR1_05negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_05negzen1gain_dec255.cte.ami" ) ("nc" "mid" 1 1.20 ".../ncAVTR1_2negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_2negzen1gain_dec255.cte.ami" ) ("wc" "mid" 1 1.05 ".../wcAVTR1negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1negzen1gain_dec255.cte.ami" ) ("wc" "mid" 1 1.20 ".../wcAVTR1_1negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1_1negzen1gain_dec255.cte.ami" ) ("bc" "mid" 1 1.05 ".../bcAVTR1_08negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_08negzen1gain_dec255.cte.ami" ) ("bc" "mid" 1 1.20 ".../bcAVTR1_26negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_26negzen1gain_dec255.cte.ami" ) ("ec" "mid" 1 1.05 ".../ecAVTR0_95negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_ecAVTR0_95negzen1gain_dec255.cte.ami" ) ("ec" "mid" 1 1.20 ".../ecAVTR1_05negzen1gain_dec255peak_dec0_norm.s4p" ".../ic_rx_ecAVTR1_05negzen1gain_dec255.cte.ami" ) ("nc" "min" 1 1.05 ".../ncAVTR1_05negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_05negzen1gain_dec0.cte.ami" ) ("nc" "min" 1 1.20 ".../ncAVTR1_2negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_2negzen1gain_dec0.cte.ami" ) ("wc" "min" 1 1.05 ".../wcAVTR1negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1negzen1gain_dec0.cte.ami" ) ("wc" "min" 1 1.20 ".../wcAVTR1_1negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1_1negzen1gain_dec0.cte.ami" ) ("bc" "min" 1 1.05 ".../bcAVTR1_08negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_08negzen1gain_dec0.cte.ami" ) ("bc" "min" 1 1.20 ".../bcAVTR1_26negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_26negzen1gain_dec0.cte.ami" ) ("ec" "min" 1 1.05 ".../ecAVTR0_95negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ecAVTR0_95negzen1gain_dec0.cte.ami" ) ("ec" "min" 1 1.20 ".../ecAVTR1_05negzen1gain_dec0peak_dec0_norm.s4p" ".../ic_rx_ecAVTR1_05negzen1gain_dec0.cte.ami" ) ("nc" "max" 1 1.05 ".../ncAVTR1_05negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_05negzen1gain_dec65535.cte.ami" ) ("nc" "max" 1 1.20 ".../ncAVTR1_2negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ncAVTR1_2negzen1gain_dec65535.cte.ami" ) ("wc" "max" 1 1.05 ".../wcAVTR1negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1negzen1gain_dec65535.cte.ami" ) ("wc" "max" 1 1.20 ".../wcAVTR1_1negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_wcAVTR1_1negzen1gain_dec65535.cte.ami" ) ("bc" "max" 1 1.05 ".../bcAVTR1_08negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_08negzen1gain_dec65535.cte.ami" ) ("bc" "max" 1 1.20 ".../bcAVTR1_26negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_bcAVTR1_26negzen1gain_dec65535.cte.ami" ) ("ec" "max" 1 1.05 ".../ecAVTR0_95negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ecAVTR0_95negzen1gain_dec65535.cte.ami" ) ("ec" "max" 1 1.20 ".../ecAVTR1_05negzen1gain_dec65535peak_dec0_norm.s4p" ".../ic_rx_ecAVTR1_05negzen1gain_dec65535.cte.ami" )))

## Slide 10: Variable substitution
Curly brackets indicate variable substitution
Can save space where parameter filenames are logical
Dependency tables can prepare variables for substitution
(Tstonefile (Usage Info) (Type String) (Value "hss15c2c/cu032/{rxcorner}{VTRV}negzen{negz}gain_dec{gain_dec}peak_dec0_norm.s4p"))
"hss15c2c/cu032/ncAVTR1_05negzen0gain_dec255peak_dec0_norm.s4p"
Curly brackets banned from normal variable names

## Slide 11: Example variable substitution
(VTRV (Usage Info) (Type String) (Description "AVTR name string") (List "AVTR0_95" "AVTR1" "AVTR1_05" "AVTR1_08" "AVTR1_1" "AVTR1_26" "AVTR1_2") ) (VTRV_Dependency_Table (Usage Info) (Type String Float String ) (Table (Labels "rxcorner In" "VTR In" "VTRV Out_Match") ( "nc" 1.05 "AVTR1_05" ) ( "bc" 1.05 "AVTR1_08" ) ( "wc" 1.05 "AVTR1" ) ( "ec" 1.05 "AVTR0_95" ) ( "nc" 1.20 "AVTR1_2" ) ( "bc" 1.20 "AVTR1_26" ) ( "wc" 1.20 "AVTR1_1" ) ( "ec" 1.20 "AVTR1_05" ))) (gain_dec (Usage Info) (Type String) (Description "Gain value string") (List "0" "255" "65535")) (gain_dec_Dependency_Table (Usage Info) (Type String String ) (Table (Labels "gain In" "gain_dec Out_Match") ( "min" "0" ) ( "mid" "255" ) ( "max" "65535" ))) (Tstonefile (Usage Info) (Type String) (Value "hss15c2c/cu032/{rxcorner}{VTRV}negzen{negz}gain_dec{gain_dec}peak_dec0_norm.s4p"))

## Slide 12: Other "modern" parameters in IBM 15G C2C configuration file
Tstonefile/RxIC
  On-die s-parameters called up by ami config file
DLLPath
  Path to tx/rx DLL
Supporting_Files
  HSSCDR executables, data files
DLLid
  Allows multiple instances
Labels
  Gives extra information about user-selectable variables

## Slide 13: Conclusions
New models have outgrown simple AMI configuration – and it's only going to get more complicated:
  IBM 15G backplane (BP)
  IBM 28G BP
Dependency tables allow selection based on other variables
Variable substitution allows filenames to be automatically chosen
Latest configuration parameters
Alternative is 100+ .ami configuration files