## Slide 1: Modeling On-Die Power Supply Decoupling
Randy Wolff – Micron Technology
Lance Wang – IO Methodology
DesignCon IBIS Summit
Santa Clara, CA, USA
February 2, 2012

## Slide 2: Outline
Elements of an IBIS 5.0 model for Power Integrity simulation
On-die power supply decoupling models
  Parasitic vs. non-parasitic
  Optimization of models
Simulation results - Transistor-level vs. IBIS 3.2, 5.0
Conclusions

## Slide 3: IBIS 5.0 Power Integrity Modeling
PI modeling requires [Composite Current], [ISSO PU], [ISSO PD] and a detailed model of decoupling capacitance
* Image from IBIS 5.1 Draft Specification
ISSO PU
ISSO PD
Decoupling

## Slide 4: Power Supply Decoupling Elements
Bypass Cap
Bond Pad Layout Floorplan
Parasitic Decoupling

## Slide 5: Parasitic Decoupling Capacitance
Chart: 
| 1.3 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.6500000000000001 | 1.7000000000000002
1.00E+06 | 13.317 | 13.293 | 13.269 | 13.245 | 13.22 | 13.195 | 13.17 | 13.146 | 13.122
1.00E+07 | 13.065 | 13.059 | 13.05 | 13.039 | 13.026 | 13.012 | 12.996 | 12.98 | 12.963
1.00E+08 | 11.986 | 11.969 | 11.951 | 11.933 | 11.914 | 11.895 | 11.875 | 11.856 | 11.837
1.00E+09 | 10.08 | 10.122 | 10.155 | 10.183 | 10.205 | 10.223 | 10.237 | 10.248 | 10.257
1.00E+10 | 4.4975 | 4.5193 | 4.5399 | 4.5594 | 4.5779 | 4.5955 | 4.6122 | 4.6281 | 4.6434
DC Bias Voltage
Frequency
Capacitance
Note:
Strongly frequency dependant
Weakly voltage dependant

## Slide 6: Optimization of Parasitic Decoupling
~ 13.4pF - not insignificant
Transistor-level vs. Model

## Slide 7: Optimization of All Decoupling
Adds ~450pF!
Transistor-level vs. Model

## Slide 8: Simulation Setup
DDR3 DQ I/O buffer, 1.5V
PRBS pattern, minimum bit width of 1.25ns
Typical corner
Various On-die decoupling capacitance models included as SPICE models
DQ1 + DQ2 switching (with different PRBS patterns) with fully coupled SPICE package model
VTT
50 Ω
Zo=50 Ω
3pF
PKG
VSSQ
PKG
VTT
50 Ω
Zo=50 Ω
3pF
PKG
VCCQ
PKG
DQ1
DQ2
V_load
I_vccq
DECAP
DECAP

## Slide 9: No Decoupling Model

## Slide 10: No Decoupling Model

## Slide 11: Parasitic Decoupling Model Included
Good match to ringing behavior

## Slide 12: Parasitic Decoupling Model Included

## Slide 13: All Decoupling Modeled
Ringing behavior no longer matches. Why?

## Slide 14: All Decoupling Modeled

## Slide 15: Conclusions
A complete model for on-die power supply decoupling must include models for parasitic caps and designed-in caps
Simple, multi-stage RC circuits accurately model on-die decoupling circuits
A method is needed for including complex decoupling models along with an IBIS 5.0 model
More investigation needed to understand circumstances where IBIS 5.0 power-aware models do not match SPICE models