## Slide 1: IBIS Futures
Thoughts on where we are, and were we need to go
Stephen Peters - Intel Corp
Vice Chair, EIA/IBIS Open Forum

## Slide 2: What we do well
Model a single buffer/receiver in isolation
  I/V - V/T great for CMOS/TTL/ECL
  [Driver Schedule] expands methodology to controlled rise time parts (GTL, etc.)
  bus hold, etc. now available for receivers
Model a Pad to Pin connection
  EBD and Enhanced packages model complex paths
    as long as you don’t want coupling

## Slide 3: What we don’t do so well (or at all)
Model Multiple buffers switching
  SSO effects due to pin to pin coupling
  SSO effects due to power/gnd rail bounce
Allow description of Lossy Transmission Line
  G matrix and/or frequency dependent loss needed for .ebd and enhanced .pkg files.
Model effects of non ideal ground return paths
  A needed capability in the next generation simulators

## Slide 4: Why Are These Important Now?
Very Fast Processor Busses
  timing budgets are super tight, can’t just ‘guestimate’
Source Synchronous Signaling
  effects previously “2nd Order” now dominate
    skew due to gnd/pwr bounce effects
    skew due to ground return paths and losses
    crosstalk (both package and board)

## Slide 5: IBIS and The SSO Problem(s)
[Pin Mapping] is a start, but it is not complete
  can’t really include on-die capacitance
  effort involved to abstract complex package power distribution into simple (fixed) R/L/C
Pin to Pin coupling almost there. . .
  Full board extraction not always appropriate for packages
  Problem may lend itself to ‘regular’ solution
  Need a champion!

## Slide 6: Some Thoughts and Observations
Key for SSO modeling is to make buffer pwr/gnd nodes available
  IMIC is interesting, but it doesn’t use standard I/V - V/T description of buffer
[Add Submodel] keyword has lots of possibilities
  IBIS file provides the shell, but submodel becomes a group of buffers?
  Description of buffer imbeds package descriptions?