## Slide 1: Macro extensions for IBIS
Al Davis
HyperLynx

## Slide 2: Why?
Ibis problems
Birds
We like IBIS.

## Slide 3: Why not?
Spice format
IMEC
VHDL/Verilog-AMS

## Slide 4: How?
Define the circuit topology
Parameterize it
Provide a library

## Slide 5: Example 1

## Slide 6: Example 1
[Define Model] Simple_Terminator (pin gnd
power_clamp_ref gnd_clamp_ref)
Rpc (power_clamp_ref pin) I = Clamp[V]
Rgc (pin gnd_clamp_ref) I = Clamp[V]
Rterm (pin gnd) R = Rterm || open
[End Define Model]

## Slide 7: Example 1
[Model] term_1
Model_type Simple_Ter
[Rterm] 50 45 60
[Clamp]
-5 900m 800m 1100m
-4 700m 600m 802m
-3 500m 400m 580m
-2 300m 200m 480m
-1 100m 90m 170m
-.8 60m 50m 90m
-.7 39m 28m 44m
-.6 22m 11m 27m
-.5 10m 0 15m
-.4 0 0 4m
-.3 0 0 0
0 0 0 0

## Slide 8: Example 1
[Define Model] Simple_Terminator (pin gnd
power_clamp_ref gnd_clamp_ref)
Rpc (power_clamp_ref pin) I = Clamp[V]
Rgc (pin gnd_clamp_ref) I = Clamp[V]
Rterm (pin gnd) R = Rterm || open
[End Define Model]

## Slide 9: Example 1a
[Define Model] Simple_Terminator (pin gnd
power_clamp_ref gnd_clamp_ref)
.if (!power_clamp_ref)
.local power_clamp_ref
Vpcr (power_clamp_ref gnd) V = PC_Ref
.endif

## Slide 10: Example 2

## Slide 11: Example 2
[Define Model] Simple_Driver (pin gnd control)
.local t1
Vsource (t1 gnd) V = Rise[T-TR] || Fall[T-TF]
Rsource (pin t1) R = Rsrc[T-TR] || Rsrc[T-TF]
.trigger TR (Logic(control) == 1)
.trigger TF (Logic(control) == 0)
[End Define Model]

## Slide 12: Example 1
[Model] term_1
Model_type Simple_Dr
[Rise]
0 0
2n 1
5n 4
7n 5
[Fall]
0 5
2n 4
5n 1
7n 0
[Rsrc]
0 10
2n 1k
3.5n 10k
5n 1k
7n 10

## Slide 13: Example 3
[Define Model] Clamped_Driver_with_Ccomp
.inherit Simple_Terminator
.inherit Simple_Driver
Ccomp (pin gnd) C = C_comp || open
Cpc (pin power_clamp_ref)C = C_comp_pcl || open
Cgc (pin gnd_clamp_ref) C = C_comp_gcl || open
[End Define Model]

## Slide 14: Compatibility
Waveform, pullup, pulldown interactions
Series Switch [On] [Off]
Correlation (typ, min, max)
Attachments (Add Submodel, Driver Schedule)

## Slide 15: Example 4
.driver Udrv (pin gnd pullup_ref pulldown_ref
tr tf en) (
S1 = Pullup[-V],
S0 = Pulldown[V],
T10 = Falling_Waveform[T-TF,*] ||
[Ramp]dv/dt_f,
T01 = Rising_Waveform[T-TR,*] ||
[Ramp]dv/dt_r,
V1 = Pullup_Reference || Voltage_Range,
V0 = Pulldown_Reference || 0 )

## Slide 16: Example 4
.trigger TR (Logic(control) == 1)
.trigger TF (Logic(control) == 0)
.correlate strong/weak=max/min Pull*
.correlate fast/slow=max/min *Waveform, [Ramp]*

## Slide 17: What components?
Spice: R, L, C, V, I, E, G
Some-Spice extras: vcg, vcr, vccap
No-Spice: driver, trigger, alarm
Programming: assert, define, export, if, inherit, local, select

## Slide 18: Conclusion
A new section [Define Model]
Describe topology of a [Model] or [Submodel]