## Slide 1: Modeling Approaches Dr. Lynne Green HyperLynx
Tables vs. Equations

## Slide 2: WHERE ARE WE HEADED?
MORE POINTS
MORE TABLES
BIGGER FILES
LONGER TIME TO LOAD

## Slide 3: WORST CASE TABLE SIZE
1 POINT EVERY MILLIVOLT
5V TRANSITION (-2 to +7V)
60 CHARACTERS PER LINE
12 TABLES PER BUFFER
4 I/O BUFFERS PER FILE
1000 FILE LIBRARY
25.9 MBYTE FILE
25.9 GBYTE LIBRARY

## Slide 4: WORST CASE MEMORY
LOAD 25.9 MBYTE FILES
16 BYTES STORED PER LINE
6.9 MBYTE PER FILE
100 FILES IN SIMULATION
690 MBYTE OF DATA

## Slide 5: TABLES
A FEW SMALL TABLES
  FAST TO LOAD
  FAST TO SEARCH
  FAST TO SIMULATE
LARGE OR MANY TABLES
  SLOW TO LOAD
  SLOW TO SEARCH
  CACHE LIMITATIONS

## Slide 6: TABLES GROW BIGGER
V-I TABLES WITH MORE POINTS
V-T TABLES WITH BOTH MORE TABLES + MORE POINTS
FREQUENCY DEPENDENT “LOSSY” LINES
FREQUENCY DEPENDENT COUPLING MATRICES

## Slide 7: EQUATIONS
ALWAYS SMALL
  COMPARED TO TABLES
  FAST TO LOAD/SEARCH
  FAST TO RUN
AVOID ITERATIVE EQUATIONS
  ITERATION IS SLOW
  VARIABLES MUST BE SAVED

## Slide 8: EQUATIONS
EXAMPLE: UNIV. OF WASH.
POWER FET MODEL
INDUSTRY: >100 PARAMETERS
NEW MODEL: 8-10 PARAMETERS
ONE TEST PER PARAMETER
SIMULATIONS >10X FASTER
IMPROVED ACCURACY!

## Slide 9: TABLES VS. EQUATIONS
TABLES
FORMAT
# POINTS & TABLES
LOAD TIME
FITTING BETWEEN POINTS
EQUATIONS
FORMAT
# PARAMS & VARIABLES
LOAD TIME
CALCULATE AT POINTS.

## Slide 10: TABLES AND EQUATIONS
BENEFITS
  REDUCE SIZE OF TABLES
  INTERPOLATION METHODS
FORMATS FOR
  DATA VALUES
  STANDARD EQUATIONS
  PARAMETER VALUES
  MIX EQUATIONS AND DATA

## Slide 11: TABLES AND EQUATIONS
ONE APPROACH
  GOLDEN PARSER
  “PKZIP™ ” FOR IBIS TABLES
  FIXED SET OF EQUATIONS
  REDUCES LARGE TABLES
OTHER APPROACHES
  USER-DEFINED EQUATIONS
  PARSER HANDLES EQUATIONS

## Slide 12: WHAT CAN WE DO?
UNIV. INVESTIGATION
  SMALL EQUATION SET
  MIX TABLES / EQUATIONS
  PARSER FOR EQUATIONS
  FILE SIZE IMPACT
  SIMULATION IMPACT