## Slide 1
®
IBIS Summit Meeting at DesignCon 2000
Westin Hotel, Santa Clara, CA
January 31, 2000
®
Future directions for IBIS
Arpad Muranyi
Signal Integrity Engineering
Intel Corporation
arpad.muranyi@intel.com
http://www-fes.fm.intel.com/pcdsehw
I
S
e
Notes: 1

## Slide 2
Outline
IBIS e-mail reflector summary
Problem description
Solution
Advantages of the solution
Surprise
Action requested
Appendix

## Slide 3
IBIS e-mail reflector summary
Posted a thought provoker message to the IBIS e-mail reflector in early December of 1999 to get feedback on what everyone thinks should be done with the IBIS specification
  received numerous responses with varying opinions
  a lot of good observations and suggestions were made
  Al Davis proposed a specific syntax and volunteered to help write it
Analyzed the responses and sorted ideas into various groups
  positives
  observations, negatives
  needs (comments, recommendations)
    do we need IBIS?
    what to keep and/or add?
    language, syntax
    package
    IBIS-X
Due to a similar discussion running on the SI-list reflector, not every aspect of IBIS modeling was mentioned in this thread
The summary can be found in the Appendix of this presentation

## Slide 4
The problem
The current IBIS syntax is inflexible because the majority of the keywords are based on (individual) assumptions and usage rules
  assumptions need to be removed or incorporated in the data
  usage rules of keywords should be generalized or be universal
Connectivity between die and package is also based on assumptions and usage rules
  limits detailed return current path and power distribution modeling
  [Pin Mapping] doesn’t provide a complete solution
This type of a syntax slows down growth and limits the possibility of adding of new features quickly
  almost every new feature requires a new keyword
  new keywords usually bring new assumptions and usage rules
A specification with such syntax becomes unmanageable
  five slightly different syntax (could soon) exist for interconnects alone: segmented uncoupled package, full matrix package, Electrical Board Description file, connector model, on-die interconnect

## Slide 5
The solution
A scalable, general purpose nodal syntax could solve most of our current and future problems
Scalable: two, three, … N-terminal black boxes
General purpose: allow anything in the black boxes
  single elements and/or networks
  passive and/or active devices, building blocks
    R, G, L, C, T-lines, packages, PCB interconnects, diodes, transistors, anything from inverters to full/partial buffer blocks, etc.
  any kind of description method
    tables (IV, Vt, RV, RT, Rt, Rf, Lf, CV, etc.),
    matrixes, expressions, transfer functions, S-parameters, etc.
  include a “node” for radiated energy
Nodal: allow arbitrary connections between black boxes and between a collection of black boxes and the outside world
  support multiple black boxes per buffer
  nested black boxes should also be allowed

## Slide 6
Block diagram
PCB
package
die interconnect
buffer2
buffer1
conn.

## Slide 7
Advantages
Supports current IBIS format (backward compatible)
  black boxes could hold current IBIS information blocks, (Model, Package, EBD, Connector, etc.)
Supports IMIC format
  three terminal black boxes with the appropriate tables could be used to describe transistors
Supports full SPICE format
  three terminal black boxes with process file information (or process file references) could be used to describe transistors
  discretes, diodes and N-well resistors could be described similarly
Allows any level of abstraction available for flexibility, accuracy, and security (IP protection)
  behavioral and/or transistor level modeling could be mixed
  multiple building blocks could be constructed to describe any behavior to any accuracy level
  IP protection through behavioral description still available
  no need to rewrite the spec for every new buffer behavior

## Slide 8
Surprise
This syntax is practically the same as the SPICE syntax
  black boxes are equivalents of subcircuits
  two terminal black boxes are equivalents of C, D, L, R, etc.
  three terminal black boxes are equivalents of M, Q, etc.
  four terminal black boxes are equivalents of E, F, G, H, T-line, etc.
The difference is in the extensive behavioral features
  many SPICE flavors do not have good behavioral elements, if at all
    E, F, G, H elements are not available in every SPICE version
    E, F, G, H elements are not sufficient for behavioral buffer modeling
  arbitrary level of abstraction
    complicated buffer behavior can be broken up into several blocks, each of which can be a simple behavioral submodel
    mixed mode models could consist of behavioral predriver with a transistorized output stage, for example
Border line between “model” or “just data” becomes blurry
  this syntax includes some netlisting due to its nodal nature
  if the description utilizes full SPICE features, it will be a “model”
  if only behavioral blocks are used, the file will contain “data” only

## Slide 9
Action requested
We need to adopt a SPICE-like nodal syntax
  no need to re-invent the wheel
  the SPICE syntax alone may not be sufficient for everything
Object oriented programming language style syntax may be another option
  this could define not just the data but the “assumptions” as well
  this format may be more vendor neutral
XML language should also be considered
Let’s make this our next major goal!