## Slide 1: Discussion - Future of IBIS
The IBIS-X proposal
Stephen Peters, Intel Corp.

## Slide 2: A Proposal: IBIS-X
IBIS Extended
  retain features that support Board level simulators and electrical rule driven routers
    “component” centric format
    explicit declaration of drivers and receiver nodes
    information that enables timing and waveform analysis
  Add features that support circuit type simulators
    add multi-ported models (explicit pwr/gnd pin connections)
    nodal interconnects of passive and controlled sources
  Provides path for external models (I.e. API interface)

## Slide 3: IBIS-X: General Outline
File Header section
Component Section
  Defines pin to individual model mapping
Model Section
  identifies model type (input, output, I/O)
  lists data book specs of I/O pin
  defines model ports, port -> pin mapping
  place to put guts of model

## Slide 4: File Header Section
FILE HEADER
The file header info remains pretty much the same as in
the current IBIS spec.
[Template Version] version #
[Comment Char] | by default
[File Name] file name.ibx
[Date] date
[Source] ASCII text
[Notes] ASCII text
[Disclaimer] ASCII text
[Copyright] ASCII text

## Slide 5: Component Section
[Begin Component]
[Component] component name
[Manufacture] manufactures name
[Pin] pin_name signal_name model_name port_name R_pin L_pin C_pin
(Note: only a *model_name* is allowed, not a submodel name. To support
IBIS compatible descriptions NC, PWR and GND are legal pin connections, and
a generic R_pin, L_pin and C_pin can be included.)
[Diff Pin]
inverting_pin non_inverting skew_typ skew_typ skew_max
[Model Selector]
[End Component]

## Slide 6: Model Section
[Begin Model] model_name
model_type = select from list
C_comp* = I/O capacitance value
[Temperature_Range] typ min max
[Pullup Reference] typ min max
[Pulldown Reference] typ min max
[POWER Clamp Reference] typ min max
[GND Clamp Reference] typ min max
[Receiver Reference] type min max
[Driver Spec]
(timing test loads, Vmeas, etc. Use if a model is an output or I/O)
[Receiver Spec]
(input thresholds, overshoot/undershoot thresholds, etc. Use if a model
is a receiver or I/O)
[Port list]
port_name port_type
(see accompanying list)
[Begin Model Description]
(put the guts of the model here)
[End Model Description]
[End Model]

## Slide 7: Model Section - Port Lists
[Port list]
port_name port_type
(port types are:
primary_io | primary I/O pin
pullup_ref | power connection pin
pulldown_ref | power connection pin
pwrclamp_ref | power connection pin
gndclamp_ref | power connection pin
rcvr_ref | power connection pin
gnd | reference pin
ctl | a digital (1/0) control pin
analog | an analog control pin
stim_in | external stimulus (not a component pin)
recevier_out | output of a receiver (not a component pin)
)

## Slide 8: Model Section - Description Formats
For a traditional behavioral description, the following keywords are supported
[Pullup]/[Pulldown]/[POWER Clamp]/[GND Clamp]
[Rising Waveform]/[Falling Waveform]
[Ramp]
[TTgnd]/[TTpower]
[Driver Schedule]
[Add Submodel]
[SubModel]
-- OR --
A nodal description connects passive components, submodels and independent
voltage and current sources together. Transistors are not supported, but
a general three terminal device is included. Syntax would be some most
common denominator of the existing SPICE variants.
Rxxx node1 node2 value= explicit value or equation (resistance)
Lxxx node1 node2 value= explicit value or equation (inductance)
Cxxx node1 node2 value= explicit value or equation (capacitance)
Vxxx node1 node2 value= explicit value, equation or table (V source)
Ixxx node1 node2 value= explicit value, equation or table (I source)
Sxxx node1 node2 node3 value = equation or table(s) (three terminal device)
Xxxx port1=>node1, port2=>node2, ...parameter1=>value,... (submodel)