## Slide 1: Behavioral Receiver Modeling
Donald Telian
Cadence, PCB Systems Division
IBIS Summit: January 31, 2000
rev. 1.0

## Slide 2: AGENDA: Behavioral Receiver Modeling
Who? The Digital Receiver Steps Forward
Why? Reasons to Use Behavioral Receivers
What? Comparing Various Receiver Modeling Methods
How? The Macro-Structure of a Behavioral Receiver
Where? That is the BIG Question

## Slide 3: AGENDA: Behavioral Receiver Modeling
Who? The Digital Receiver Steps Forward
        termination modeling
        driver sizing & scaling
        interconnect optimization
        who’s left ???
Why? Reasons to Use Behavioral Receivers
What? Comparing Various Receiver Modeling Methods
How? The Macro-Structure of a Behavioral Receiver
Where? That is the BIG Question

## Slide 4: The Study & Optimization of Digital Interfacing
Mid - ‘80s = Terminations !
Most of the rest was “off-the-shelf” to the digital engineer

## Slide 5: Next Came Driver Scaling & Tuning
Custom IC & ASIC Design brought the ability to sweep and tune Driver Characteristics
Set the stage for “IBIS” representation in early ‘90s
Current
Voltage
Reference: “Treat pc-board traces as transmission lines to specify drive buffers” EDN September 2, 1993 page 129

## Slide 6: IBIS & Tools Allowed Topology Optimization
Given well-tuned driver technology, constraining “Topology” factors brought more speed advances in the mid ‘90s
Buffers acquired new dynamic behaviors

## Slide 7: But What About the Lowly Receiver?
What?
Me?
…a b-b-BIRD?
I, uh, I guess I hoped no one would notice!

## Slide 8: AGENDA: Behavioral Receiver Modeling
Who? The Digital Receiver Steps Forward
Why? Reasons to Use Behavioral Receivers
        Simplification
        Performance
        Design Optimization
What? Comparing Various Receiver Modeling Methods
How? The Macro-Structure of a Behavioral Receiver
Where? That is the BIG Question

## Slide 9: A Receiver is Basically an A - D Converter
Consequently, it simplifies the question of how the (not-so-digital) digital signal is responded to by the device.
It’s a “digital” problem once again!

## Slide 10: Receiver Modeling Allows Greater Performance
Puts the whole digital transmission into one succinct transaction
Eliminates awkward signaling hand-off at receiver node
  double counting
  extrapolations
Allows the high-speed problem to be studied at one time

## Slide 11: Receiver Modeling Allows Optimization
What switching function do I need?
What type of pulses will need to be rejected?
What sort of propagation characteristics will work?
What voltages should this all operate at?
In short, the Receiver can be “tuned” just like we’re used to doing with the driver and the interconnect !

## Slide 12: AGENDA: Behavioral Receiver Modeling
Who? The Digital Receiver Steps Forward
Why? Reasons to Use Behavioral Receivers
What? Comparing Various Receiver Modeling Methods
        Methods Available
        Methods Contrasted
        Cadence’s Solution
How? The Macro-Structure of a Behavioral Receiver
Where? That is the BIG Question

## Slide 13: Methods to Model a Complete Receiver
Silicon-level SPICE Description
  too slow, or is it ??
  too proprietary ?
Pre-Configured Behavioral Description
  model has defined structure / construction
  imitates one thing only, not a design tool
  too limiting (leads to IBIS’ current roadblocks)
Nodal Behavioral Description
  allows modeling a receiver’s characteristics
  easily adapts to arbitrary behaviors
  this is what Cadence implemented

## Slide 14: Pre-Configured vs Nodal Behavioral Models
PRE-CONFIGURED NODAL
Data Behaviors
Data Behaviors
Define Format Code Test

## Slide 15: Nodal Better for “Design” not Just “Design In”
More and more “Driver” design problems are solved this way
Sure is better to work this way, when you can!
DESIGN SILICON
MAKE MODEL
STUDY PROBLEM
DESIGN SILICON
MAKE MODEL
STUDY PROBLEM
DESIGN-IN
DESIGN
!
!

## Slide 16: 1998: The Digital Universal Behavioral Receiver
Working with Intel, on a certain unnamed project, in 1998 Cadence used Nodal Behavioral Modeling to develop the first Digital Universal Behavioral (DUB) Receiver Model
Sounds DUBious to me!!
I dub thee a DUB

## Slide 17: AGENDA: Behavioral Receiver Modeling
Who? The Digital Receiver Steps Forward
Why? Reasons to Use Behavioral Receivers
What? Comparing Various Receiver Modeling Methods
How? The Macro-Structure of a Behavioral Receiver
        Block Diagram
        Block - by - Block Explanation
        Elements Required
        How Fast? How Accurate?
Where? That is the BIG Question

## Slide 18: DUB Block Diagram
5 Basic Elements of any Receiver
Low Pass Filter
Switching Function
Delay Adder
Intrinsic Delay
Edge Rate Detection

## Slide 19: DUB Block #1: Low Pass Filter
Every Receiver Rejects Certain Pulse Spikes
Simple to Characterize and Implement
Low Pass Filter

## Slide 20: DUB Block #2: Switching Function
Receiver’s Basic Transfer Function
Even Simpler for non-Differential Receiver
Switching Function

## Slide 21: DUB Block #5: Intrinsic Delay
Every Receiver has an Intrinsic (minimum) Delay
Easily Determined by Measuring Against the Fastest Edge Expected
Intrinsic Delay

## Slide 22: DUB Block #3: Edge Rate Detection
Receiver Delay Changes with Input Edge Rate
Mathematically Determine Derivative of Input Signal
Use Real-time Derivative to Adapt Propagation Delay
Edge Rate Detection

## Slide 23: DUB Block #4: Delay Adder
Circuit to Adjust Propagation Delay Based on Input Slope
Real-time Adaptive Delay Line Construction
Delay Adder

## Slide 24: What is Needed for Nodal Behavioral DUB?
Nodal Language
G (VCCS) and E (VCVS) sources
  pwl table driven
  equation driven, with derivatives
  event driven and time-controlled as well
Real-time Adaptive Delay Line
Subcircuit Nesting and Random Node Printing
These are all available in SPECCTRAQuest’s MacroModeling language

## Slide 25: How Fast is the DUB Method?
Values Derived from Receiver Benchmark, not Application
“Intel DUB” needed additional elements to work right
For “small” SPICE circuits, “Behavioral” can be slower !!
  that was the big surprise to this engineer
However, in the Intel application, the pure receiver delta above was insignificant because the elaborate package model contributed to ~90% of the run-time hit

## Slide 26: How Accurate? As Accurate as You Want !
Picosecond variations for 242 extremely difficult test waveforms
Average difference was 19 pS (std. dev. of 14 pS)
Could have matched even closer with more work, if desired
50 pS limit
DUB Receiver Variation vs SPICE Model

## Slide 27: And Here’s the Rest of the Story...
For the Original Intel DUB, other Elements Were Added to Accommodate Unique (Proprietary) Effects
  this is what caused the extra 50% simulation slow down
Cadence HIGHLY Recommends that if IBIS Implements Behavioral Receivers that a Nodal Syntax Language Be Used
  any approach needs to be adaptable to unique situations

## Slide 28: AGENDA: Behavioral Receiver Modeling
Who? The Digital Receiver Steps Forward
Why? Reasons to Use Behavioral Receivers
What? Comparing Various Receiver Modeling Methods
How? The Macro-Structure of a Behavioral Receiver
Where? That is the BIG Question
        why do answers always raise more questions?

## Slide 29: The DUB is All Dressed Up...
…and Ready to Go!

## Slide 30: The Big Question:
Will the Compelling Application Please Step Forward ????
IBIS Drivers had PCI and Pentium, but who will Rub-A-DUB?