## Slide 1
Simultaneous Switching Noise (SSN) Modelling
Bernhard Unger
Siemens AG
Information Technology Services
High Speed Design and EMC Engineering

## Slide 2: Intention
To investigate the quality of the „Enhanced Two Waveform Model“ regarding simultaneous switching noise modelling (first proposal: IBIS summit meeting Munich March 1999)
To exchange ideas how to get SSN modelling into IBIS
To start discussions if SSN effects could be simulated by behavioral models based on the existing IBIS or more complex models like IMIC ore SPICE syntax based models are needed
Not to present the „Enhanced Two Waveform Model“ as a final solution. More investigations have to be done to figure out the validity range of the proposed model

## Slide 3: Basis of Investigations
HSPICE and IBIS models: VCX16244 Fairchild Semiconductor BD4 G10 Technology LSI LOGIC
IBIS models: Generated from HSPICE models. R_fixture = 50 Generation is done without package parasitics
Analysis conditions: VCX16244: Distributed loaded tr-line; Z0(trace) = 66 Vdd/Vss package parasitics: TSSOP48 BD4: tr-line (Z0 = 50; td = 1ns) loaded with 5pF Vdd/Vss package parasitics: L=5nH; Rs=100m

## Slide 4: Device Output Loading Conditions
BD4
BD4 Loading: Transmisson Line
VCX16244 Loading: Loaded Transmisson Line

## Slide 5: Simultaneous Switching Noise Analysis Set-up
T1
T2
H / L
VCC
GND
I
F1
=m
x I
VDD
I
F2
=m
x I
GND
I
VDD
I
GND
C
GND
C
VDD
L
VD
D
L
GND
R
VD
D
R
GND
Package
RLC
Package
RLC
TRANSMITTER
RECEIVER
R1
R2
tr-line
tr-line
Quiet Output
Switching Output
T1: Quiet transmitter
T2: Switching transmitter
Both transmitter are modeled by two waveform behavioral models
Number of simultaneously switching outputs: m + 1

## Slide 6: Enhanced two Waveform Behavioral Model
Model enhancement by a second multiplier for rising (kssnr) and falling (kssnf) edges
Both multipliers are controlled by the (Vdd-Vss) voltage drop
The multipliers model the feedback on the gate source voltage of the output transistors
Multiplier generation:
  Golden Waveform SSO-V/t-table
  Pullup/down V/I-tables as a function of Vdd

## Slide 7: kssnr/f Multiplier Generation Method
I(3.6V)
I(3.3V)
50 Ohm loading characteristic
CMOS Driver Output High Characteristic
kssnr(3.6V) = I(3.6V)/I(3.3V)

## Slide 8: VCX16244 SSN analysis results (rising edge) Usual two waveform behavioral model Number of SSO = 6
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral
Lvss = 3.18nH
Lvdd = 7.23nH

## Slide 9: VCX16244 SSN analysis results (rising edge) Enhanced two waveform behavioral model Number of SSO = 6
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral

## Slide 10: BD4 SSN analysis results (rising edge) Usual two waveform behavioral model Number of SSO = 10
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral
1ns

## Slide 11: BD4 SSN analysis results (rising edge) Enhanced two waveform behavioral model Number of SSO = 10
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral

## Slide 12: BD4 SSN analysis results (rising edge) Enhanced two waveform behavioral model with prestage capacitance Number of SSO = 10
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral

## Slide 13: Enhanced two Waveform Behavioral Model including prestage Vdd-Vss Capacitance
kssnr(Vdd-Vss) *
kpu(t)
*
Ipu(Vout)
kssnf(Vdd-Vss) *
kpd(t)
*
Ipd(Vout)
Ipc(Vout)
Igc(Vout)
C_comp/2
C_comp/2
OUT
VSS
VDD
Cpre
Cpre:
Vdd-Vss prestage
Capacitance
Evaluation:
SPICE simulation using a capacitance
bridge

## Slide 14: BD4 SSN analysis results (falling edge) Usual two waveform behavioral model Number of SSO = 10
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral
1ns

## Slide 15: BD4 SSN analysis results (falling edge) Enhanced two waveform behavioral model with prestage capacitance Number of SSO = 10
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral

## Slide 16: BD4 SSN analysis results (rising edge) Enhanced two waveform behavioral model with prestage capacitance Number of SSO = 5
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral

## Slide 17: BD4 SSN analysis results (falling edge) Enhanced two waveform behavioral model with prestage capacitance Number of SSO = 5
Node OUT:
Transistor based
Behavioral
Node END:
Transistor based
Behavioral

## Slide 18: BD4 SSN analysis results (rising edge) Vdd current of 1 bd4 buffer Number of SSO = 10
Supply currents:
Transistor based
Enhanced behavioral
including prestage C
Usual behavioral

## Slide 19: BD4 SSN analysis results (rising edge) Noise on quiet outputs Number of SSO = 10
Quiet output High
Quiet output Low
Quiet output signals:
Transistor based
Enhanced behavioral
including prestage C
Usual behavioral

## Slide 20: VCX16224 SSN analysis results (falling edge) Noise on quiet outputs. Mismatch in case of pulldown resistor Number of SSO = 6
Quiet output signals:
Transistor based
Enhanced behavioral
Usual behavioral
Quiet output High
Quiet output Low
Quiet output High
Quiet output Low

## Slide 21: Conclusions
The SSN modelling of CMOS buffers can be improved by the proposed enhanced two waveform behavioral model
  SSO output waveforms, voltage drops on quiet outputs and supply currents can be modelled
  A single model can handle different numbers of simultaneous switching outputs and different packages
  The additional model parameters can easy be evaluated by simulations and implemented into IBIS
More investigations have to be done to allow statements about the validity range and the accuracy of the proposed model
Additional improvements or other model structures are a real need to get a general solution