## Slide 1: SCSI Compensation Modeling

## Slide 2: Small Computer Systems Interface
Evolution:
  Shugart Associates Sytems Interface (SASI) developed in the late ‘70’, single-ended, 8 bit bus, 1.5Mbytes/s
  High voltage differential, early 90’s, 10MBytes/s
  16 bit bus, mid 90’s, 40 Mbytes/s
  Low-voltage differential, late 90’s, 80 MBytes/s
  Adaptive signaling, early 00’s, 320 Mbytes/s

## Slide 3: SCSI Specification
Developed by T10 which also develops standards for CAM, and SSA
T10 is a Technical Committee of the National Committee for Information Technology Standards (NCITS)
NCITS is accredited by and operates under rules approved by the American National Standards Institute (ANSI)
NCITS was formerly known as the X3 Committee
Notes: CAM - Common Access Method - SCSI software layering standard
SSA - Serial Storage Architecture
SMD -

## Slide 4: Selected Members of T10
Adaptec
Advansys
Agilent Technologies
Brocade
Cirrus Logic
Cisco Systems
Compaq Computer
Dallas Semiconductor
Dell Computer
Eastman Kodak
EMC
Emulex
Emulex
Exabyte
Fujitsu
General Dynamics
Gigalabs
Hewlett Packard
Hitachi
IBM
Intel
Iomega
LSI Logic
Matsushita
Maxtor
Methode
Microsoft
Molex
Mylex.
NSTOR
Panasonic
Philips
QLogic
Quantum
Sanyo
Seagate
Sieko Epson
Siemens Nixdorf
Sony
Standard Microsystems
Storage Technology
Sun Microsystems
Texas Instruments
Toshiba
Tyco Electronics
UNISYS

## Slide 5: SCSI Configurations
Bus structure with 27 data, 8 ground, 4 termination power, 2 reserved.
68 conductors, 90-120 ohms, single ended or differential
25 meters point-to-point
12.5 meters with 16 stubs
Allowable loading of 30pF / stub

## Slide 6: SCSI Structure

## Slide 7: The Issue
Data transfer rate of 320MBytes/sec
Setup and hold decreased
Inter-symbol interference
Cable charge time decreased
Factor in 16 capacitively loaded stubs
Bottom line - data errors

## Slide 8: Example Eye Diagram Without Compensation

## Slide 9: Example Worst Case Eye Simulation Without Compensation

## Slide 10: The Solution
Run length encoded compensation at the transmitter
  Transmitter overdrives unless two or more data bits are sequentially the same value
  Second data bit and subsequent bits of the same value have the drive level reduced
  Drive strength, rise time and fallback are programmable
Training pattern upon initialization with bit rate negotiation

## Slide 11: Example Eye Diagram With Transmitter Compensation

## Slide 12: SCSI Signal Modeling
Ad hoc group of T10 tasked to write an ANSI/ NCITS Technical Report specifying:
  SCSI physical environment common simulation methodology
  Modeling of devices, cables, connectors, terminators
  Signal performance information exchange standards
  Methods for extracting electrical and signal attributes
  Acceptable modeling methods
  Acceptable simulation methods

## Slide 13: SCSI Signal Modeling
Group has selected IBIS as the data exchange format for:
  Semiconductor device models
  Terminator models
  Connector models (when codified)
Would like to continue to use IBIS if fallback modeling can be accomodated

## Slide 14: 40 Years of SCSI

## Slide 15: IBIS and SCSI Fallback
IBIS 3.2 can be used for present SCSI devices
  Single-ended models
  High voltage differential models
  Low voltage differential models
SCSI 320 Mbyte/s drivers characteristics
  Differential current mode transmitters
  Negotiable data rates
  Multi-level parallel positive and negative current drivers
  Uses programmable fallback

## Slide 16: IBIS and SCSI Fallback
Fallback can not be modeled in IBIS 3.2
  Driver schedule keyword is close
  Needs bit position dependency not time
  Future may include overdrive past 1st bit
  Needs accommodation for parallel current mode drivers

## Slide 17: Proposed IBIS Modifications
Add Fallback Schedule Keyword
  Similar in construction to Driver shedule
  Describes switching sequence fallback modeling
  Delay parameters are in terms of bit times
  Accommodates min, typ, max conditions
  Differential operation
  Two current sources and sinks for each line

## Slide 18: SCSI and IBIS Futures
Next generation of SCSI has a 640 Mbyte/s transfer rate scheduled for 2003
  Will use transmitter fallback compensation
  Overdrive may extend past 1st bit
  Will most likely also implement adaptive receiver equalization
Subsequent generations may include phase encoding
How do we fit this in with the future IBIS ?