## Slide 2: The Joy of Web Models
Tom Dagostino
ICX Modeling Manager
Mentor Graphics Corporation

## Slide 3: Models from the Web
The following IBIS models are all from the IC manufacturers
I was asked to QC them
They were all for a single project for the same customer
Notes: We received a request from a customer to QC models for a project he was working on. All of the models we received were collected by the customer from the respective IC manufacturers.

## Slide 4: Process
Checked file with IBISCK3
Visual Inspection
Notes: Though the QC process we used to validate the models is more complex than shown here, I only used the above two steps for the purposes of this presentation. Each model was checked for IBIS syntax by the IBIS parser and then was visually inspected. The problems found/discussed were fairly obvious. Most files had more problems than shown.

## Slide 5: Clock Driver
|************************************************************************
| IBIS file clock.ibs created by s2ibis2 version 1.1
| North Carolina State University Electronics Research Laboratory 1995
|************************************************************************
|[IBIS ver] 2.1
[File name] clock.ibs
[File Rev] 1.0
[Date] Monday, January 24, 2000
[Source] Company1, Inc.
[Notes] 1. Temperatures: typ=25C, min=100C, max=0C 2. Comp1 0.5 Double
Poly Double Metal process 3. RRmp rates based on 500 ohm load.
Notes: I will change the name and part number to protect the guilty. This part is a low skew clock driver/buffer.

## Slide 6: Clock Driver
Checking clock.ibs for IBIS 2.1 Compatibility...
WARNING - Model 'out': TYP AC Falling Endpoints ( 0.04V, 3.30V) not within 0.065V (2%) of ( 3.30V, 3.30V) on VI curves for 500 Ohms to 3.3V
WARNING - Model 'out': MIN AC Falling Endpoints ( 0.07V, 3.00V) not within 0.059V (2%) of ( 3.00V, 3.00V) on VI curves for 500 Ohms to 3V
WARNING - Model 'out': MAX AC Falling Endpoints ( 0.03V, 3.60V) not within0.071V (2%) of ( 3.30V, 3.60V) on VI curves for 500 Ohms to 3.6V
File Passed
Notes: This is the results from the IBIS parser. Note the mismatch between the endpoints from the AC waveforms and the values predicted by the IV curves. I’ll propose a change to the parser. If the difference is more than 10% it should be flagged as an error, not a warning.

## Slide 7: Clock Driver
[Model] out
Model_type Output
Polarity Inverting
Enable Active-High
C_comp 7.00pF 7.00pF 7.00pF
[Temperature Range] 25.00 100.00 0.000
[Voltage Range] 3.30V 3.00V 3.60V
[Pulldown]
| voltage I(typ) I(min) I(max)
-3.30 0.000A 0.000A 0.000A
3.20 0.000A 0.000A 0.000A
3.30 0.000A 0.000A 0.000A
3.40 0.13A 79.70mA 0.18A
3.50 0.13A 0.11A 0.18A
3.60 0.13A 0.21A 0.18A
|
5.50 2.86A 3.64A 2.25A
5.70 3.23A 4.02A 2.63A
5.90 3.61A 4.40A 3.00A
6.10 3.99A 4.77A 3.38A
6.60 4.94A 5.72A 4.33A
Notes: Here we see part of the model. I’m concerned about the C_comp value being the same for the min/typ/max cases. But that is a small concern compared to the zero current in the pulldown table in the active region.

## Slide 8: Clock Driver
Status
  Contacted manufacturer twice
  Received corrected model after second call

## Slide 9: Terminator 12345
[IBIS ver] 2.1
[File name] 12345.ibs
[File Rev] 1.0
[Date] 20 May 1998
[Source] Semiconductor2 -- 12345 HSPICE model
[Notes] Created by S. S.
Component 12345
[Component] 12345
[Manufacturer] Semiconductor2
[Package]
| variable typ min max
R_pkg 20.00m 16.00m 24.00m
L_pkg 1.50nH 1.10nH 1.90nH
C_pkg 0.15pF 0.10pF 0.20pF
Notes: This is a Ultra2 LVD/SE SCSI Terminator.

## Slide 10: 12345
Checking 12345.ibs for IBIS 2.1 Compatibility...
Errors : 0
File Passed
Notes: The file passed the IBIS parser with no errors or warnings.

## Slide 11: 12345 Ultra2 LVD/SE SCSI Terminator
[Model] rnpin
Model_type Output
C_comp 3.00pF 3.00pF 3.00pF
Vmeas=1.5V
[Temperature Range] 27.00 70.00 0.000
[Voltage Range] 5.00V 4.00V 5.50V
[Pulldown]
|
[Pullup]
|
[Ramp]
| variable typ min max
dV/dt_r 67.20u/1.39n 71.40u/1.03n 67.20u/1.41n
dV/dt_f -0.53m/0.19n -0.34m/0.24n -0.64m/0.15n
R_load = 0.10k
End [Model] rnpin
Notes: This part acts as a terminator for SCSI busses. It will terminate the SCSI line into the appropriate R and V. The model is an output model though, complete with pullup and pulldown tables and rise and fall times.????

## Slide 12: 12345
Status
  Contacted Vendor
  Said would pass info on to correct group
  No response yet

## Slide 13: 789_in
|************************************************************************
| IBIS file miiin3x.ibs created by s2ibis2 version 0.91BETA
| North Carolina State University Electronics Research Laboratory 1995
|************************************************************************
|
[IBIS ver] 2.1
[File name] 789_in_e.ibs
[File Rev] 1.0
[Date] Friday, June 23, 2000
[Source] Semiconductor3.
[Notes] Unless otherwise specified, the data above and below the
typical POWER supply rails is presented only as a rough
approximation based on lab measurements. The pin parasitics
are from simulated data.
[Disclaimer] This file only describes the I/V characteristics of the
standard digital type pads for the 33333 product. Note, the
MAX corner represents the worst case operation (low supply
voltage, high temperature, slow spice models).
Notes: This is a partial model of an 789 part. This one seems to be a model of an input. The notes indicate that the data is an approximation of data on the IV characteristics above and below the power rails and only models the IV characteristics for the remainder of the model. It has an interesting definition of the MAX model.

## Slide 14: 789_in
Checking 789_in_e.ibs for IBIS 2.1 Compatibility...
WARNING - Model 'mii_IN': TYP AC Rising Endpoints ( 0.00V, 0.00V) not within
0.000V (2%) of (-0.00V, -0.00V) on VI curves for 50 Ohms to 0V
WARNING - Model 'mii_IN': TYP AC Falling Endpoints ( 3.30V, 3.30V) not within
0.000V (2%) of ( 3.30V, 3.30V) on VI curves for 50 Ohms to 3.3V
WARNING - Model 'mii_IN': MIN AC Rising Endpoints ( 0.00V, 0.00V) not within
0.000V (2%) of (-0.00V, -0.00V) on VI curves for 50 Ohms to 0V
WARNING - Model 'mii_IN': MIN AC Falling Endpoints ( 3.30V, 3.30V) not within
0.000V (2%) of ( 3.30V, 3.30V) on VI curves for 50 Ohms to 3.3V
WARNING - Model 'mii_IN': MAX AC Rising Endpoints ( 0.00V, 0.00V) not within
0.000V (2%) of (-0.00V, -0.00V) on VI curves for 50 Ohms to 0V
WARNING - Model 'mii_IN': MAX AC Falling Endpoints ( 3.30V, 3.30V) not within
0.000V (2%) of ( 3.30V, 3.30V) on VI curves for 50 Ohms to 3.3V
Errors : 0
Warnings: 6
File Passed
Notes: Interesting warning for an input model.
I think there is a bug in the IBIS parser. 0.00V is within 2% of 0.00V last I checked.

## Slide 15: 789_in
|************************************************************************
| Component mii_IBIS_model
|************************************************************************
|
[Component] mii_IBIS_model
[Manufacturer] Semiconductor3
[Package]
| variable typ min max
R_pkg 1.74 1.47 2.01
L_pkg 8.16nH 6.59nH 9.64nH
C_pkg 1.02pF 650.00fF 1.39pF
|
[Pin] signal_name model_name R_pin L_pin C_pin
PWR VCC POWER
GND1 GND GND
PAD2 out2 mii_IN
D1in Din1 Input1
Notes: This part seems to have 2 pin models, one for an output called Out2 and one for an input Din1. But wait, there’s more. Out2 is called mii_IN!

## Slide 16: 789_in
|************************************************************************
| Model Input1
|************************************************************************
|
[Model] Input1
Model_type Output
Polarity Non-Inverting
Vinl = 0.00V
Vinh = 3.30V
C_comp 472.00fF 615.00fF 352.00fF
|
[Temperature Range] 25.00 -40.00 150.00
[Voltage Range] 3.30V 3.46V 3.13V
|
[Pulldown]
| voltage I(typ) I(min) I(max)
|
-3.30 -0.00A -0.00A -0.00A
-3.10 -0.00A -0.00A -0.00A
0.00 -0.00A -0.00A -0.00A
0.10 -0.00A -0.00A -0.00A
2.90 -0.00A -0.00A -0.00A
3.00 -0.00A -0.00A -0.00A
3.10 -0.00A -0.00A -0.00A
3.20 -0.00A -0.00A -0.00A
3.30 -0.00A -0.00A -0.00A
3.40 -0.00A -0.00A -0.00A
Notes: Interesting set of tables for a model Input1.
Interesting definition of typ/min/max.
Interesting Vinl and Vinh data
At least the data is consistent, 0.00A

## Slide 17: 789_in
[Pullup]
| voltage I(typ) I(min) I(max)
|
-3.30 -0.00A -0.00A -0.00A
-3.10 -0.00A -0.00A -0.00A
6.00 -0.00A -0.00A -0.00A
6.20 -0.00A -0.00A -0.00A
|
[Ramp]
| variable typ min max
dV/dt_r 0.00/0.00 0.00/0.00 0.00/0.00
dV/dt_f 0.00/0.00 0.00/0.00 0.00/0.00
|
| End [Model] Input1
Notes: Another input with pullup and ramp data

## Slide 18: 789_in
[Model] mii_IN
Model_type I/O
Polarity Non-Inverting
Vinl = 800.00mV
Vinh = 2.00V
C_comp 472.00fF 615.00fF 352.00fF
|
|
[Temperature Range] 25.00 -40.00 150.00
[Voltage Range] 3.30V 3.46V 3.13V
[Pulldown]
| voltage I(typ) I(min) I(max)
|
-3.30 -5.48A -5.33A -5.79A
-3.10 -5.03A -4.88A -5.34A
-2.90 -4.59A -4.43A -4.90A
-2.70 -4.14A -3.99A -4.46A
0.00 -48.98pA -48.54pA -10.40nA
0.10 923.30nA 1.44uA 525.30nA
0.20 1.57uA 2.39uA 931.20nA
0.30 2.04uA 3.02uA 1.24uA
0.40 2.37uA 3.46uA 1.47uA
0.50 2.60uA 3.76uA 1.64uA
2.90 3.02uA 4.25uA 2.04uA
3.00 3.02uA 4.26uA 2.04uA
3.10 3.02uA 4.26uA 2.05uA
3.20 3.03uA 4.26uA 2.05uA
3.30 3.03uA 4.27uA 2.06uA
3.40 3.04uA 4.27uA 2.06uA
3.50 3.04uA 4.28uA 2.07uA
3.60 3.04uA 4.28uA 2.07uA
Notes: Again, a very weak pull down for an I/O
A very interesting definition of min/typ/max
Why does something that is described as an nii_IN have a pull down or is modeled as I/O?

## Slide 19: 789_in
[Pullup]
| voltage I(typ) I(min) I(max)
|
-3.30 3.14uA 4.38uA 2.23uA
-3.10 3.14uA 4.38uA 2.22uA
-2.90 3.13uA 4.37uA 2.21uA
-2.70 3.12uA 4.36uA 2.19uA
0.20 3.02uA 4.27uA 2.04uA
0.30 3.02uA 4.26uA 2.03uA
0.40 3.02uA 4.26uA 2.03uA
0.50 3.02uA 4.26uA 2.02uA
3.60 -2.30uA -1.90uA -6.24mA
3.70 -3.60uA -2.83uA -47.26mA
3.80 -45.61uA -3.56uA -163.80mA
3.90 -863.10uA -8.58uA -329.50mA
4.00 -11.38mA -284.60uA -516.60mA

## Slide 20: 789_in
[Ramp]
| variable typ min max
dV/dt_r 0.00/0.00 0.00/0.00 4.74n/-235.10p
dV/dt_f 0.00/0.00 0.00/0.00 0.00/0.00
Notes: Input model with rise and fall times
-235.10 psec risetime????

## Slide 21: 789_in
[Rising Waveform]
R_fixture = 50.00
V_fixture = 0.00
| time V(typ) V(min) V(max)
|
0.00S 0.00V 0.00V 520.00nV
200.00pS -974.50nV -1.16uV -1.24uV
400.00pS 415.05nV 78.40nV 2.24uV
600.00pS 0.00V 0.00V 420.93nV
800.00pS 0.00V 0.00V 402.80nV
1.00nS 0.00V 0.00V 229.33nV
9.40nS 0.00V 0.00V 520.30nV
9.60nS 0.00V 0.00V 521.33nV
9.80nS 0.00V 0.00V 516.65nV
10.00nS 0.00V 0.00V 527.90nV
Notes: Not a very interesting VT waveform.

## Slide 22: 789_in
[Falling Waveform]
R_fixture = 50.00
V_fixture = 3.30
| time V(typ) V(min) V(max)
|
0.00S 3.30V 3.30V 3.30V
200.00pS 3.30V 3.30V 3.30V
400.00pS 3.30V 3.30V 3.30V
600.00pS 3.30V 3.30V 3.30V
800.00pS 3.30V 3.30V 3.30V
1.00nS 3.30V 3.30V 3.30V
9.00nS 3.30V 3.30V 3.30V
9.20nS 3.30V 3.30V 3.30V
9.40nS 3.30V 3.30V 3.30V
9.60nS 3.30V 3.30V 3.30V
9.80nS 3.30V 3.30V 3.30V
10.00nS 3.30V 3.30V 3.30V
|
| End [Model] mii_IN
Notes: The falling waveform is not very interesting either.

## Slide 23: 789_out
[IBIS ver] 2.1
[File name] 789_out_e.ibs
[File Rev] 1.0
[Date] Friday, June 23, 2000
[Source] Semiconductor3.
[Notes] Unless otherwise specified, the data above and below the
typical POWER supply rails is presented only as a rough
approximation based on lab measurements. The pin parasitics
are from simulated data.
[Disclaimer] This file only describes the I/V characteristics of the
standard digital type pads for the 789 product. Note, the
MAX corner represents the worst case operation (low supply
voltage, high temperature, slow spice models).
Notes: Another pin model for the 789 part. The same kinds of qualifiers are present

## Slide 24: 789_out
[Component] mii_IBIS_model
[Manufacturer] Semiconductor3.
[Package]
| variable typ min max
R_pkg 1.74 1.47 2.01
L_pkg 8.16nH 6.59nH 9.64nH
C_pkg 1.02pF 650.00fF 1.39pF
|
[Pin] signal_name model_name R_pin L_pin C_pin
PWR VCC POWER
GND1 GND GND
PAD out2 mii_OUT
D1in Din1 Input1
Notes: Here they define the function of the two model, one is an output and the other in an input

## Slide 25: 789_out
Checking 789_out_e.ibs for IBIS 2.1 Compatibility...
WARNING - Model 'mii_OUT': TYP AC Rising Endpoints ( 0.00V, 1.18V) not within
0.024V (2%) of (-0.00V, 0.58V) on VI curves for 50 Ohms to 0V
WARNING - Model 'mii_OUT': TYP AC Falling Endpoints ( 2.13V, 3.30V) not within
0.023V (2%) of ( 1.14V, 2.42V) on VI curves for 50 Ohms to 3.3V
WARNING - Model 'mii_OUT': MIN AC Rising Endpoints ( 0.00V, 1.54V) not within
0.031V (2%) of (-0.00V, 0.64V) on VI curves for 50 Ohms to 0V
WARNING - Model 'mii_OUT': MIN AC Falling Endpoints ( 1.52V, 3.30V) not within
0.036V (2%) of ( 0.63V, 2.31V) on VI curves for 50 Ohms to 3.3V
WARNING - Model 'mii_OUT': MAX AC Rising Endpoints ( 0.00V, 0.82V) not within
0.016V (2%) of (-0.00V, 0.53V) on VI curves for 50 Ohms to 0V
WARNING - Model 'mii_OUT': MAX AC Falling Endpoints ( 2.67V, 3.30V) not within
0.013V (2%) of ( 2.04V, 2.67V) on VI curves for 50 Ohms to 3.3V
Errors : 0
Warnings: 6
File Passed
Notes: It passes with warnings

## Slide 26: 789_out
[Model] mii_OUT
Model_type I/O
Polarity Non-Inverting
Vinl = 800.00mV
Vinh = 2.00V
C_comp 472.00fF 615.00fF 352.00fF
|
|
[Temperature Range] 25.00 -40.00 150.00
[Voltage Range] 3.30V 3.46V 3.13V
|
[Pulldown]
| voltage I(typ) I(min) I(max)
|
-3.30 -5.48A -5.33A -5.79A
-3.10 -5.03A -4.88A -5.34A
-2.90 -4.59A -4.43A -4.90A
-2.70 -4.14A -3.99A -4.46A
0.20 6.32mA 10.76mA 3.05mA
0.30 9.09mA 15.39mA 4.42mA
0.40 11.60mA 19.48mA 5.68mA
0.50 13.82mA 23.02mA 6.82mA
0.60 15.77mA 26.01mA 7.85mA
0.70 17.44mA 28.45mA 8.76mA
0.80 18.83mA 30.37mA 9.55mA
0.90 19.96mA 31.78mA 10.24mA
1.00 20.82mA 32.81mA 10.80mA
1.10 21.46mA 33.66mA 11.26mA
1.20 21.97mA 34.34mA 11.60mA
Notes: This is modeled as an I/O pin. Funny min/typ/max definitions. Compare the data in this table with the data in the ground clamp table.

## Slide 27: 789_out
[Pullup]
| voltage I(typ) I(min) I(max)
|
-3.30 3.17uA 4.49uA 2.35uA
-3.10 3.16uA 4.45uA 2.31uA
-2.90 3.14uA 4.42uA 2.28uA
1.40 -14.68mA -21.58mA -8.96mA
1.50 -16.16mA -23.53mA -10.01mA
1.60 -17.56mA -25.38mA -11.01mA
1.70 -18.87mA -27.15mA -11.96mA
1.80 -20.10mA -28.82mA -12.84mA
1.90 -21.25mA -30.39mA -13.67mA
2.00 -22.31mA -31.86mA -14.44mA
Notes: Funny min/typ/max definitions.

## Slide 28: 789_out
[GND_clamp]
| voltage I(typ) I(min) I(max)
|
-3.30 -5.48A -5.33A -5.79A
-3.20 -5.25A -5.10A -5.57A
-3.10 -5.03A -4.88A -5.34A
-3.00 -4.81A -4.66A -5.12A
-2.90 -4.59A -4.43A -4.90A
-2.80 -4.37A -4.21A -4.68A
-2.70 -4.14A -3.99A -4.46A
0.20 6.32mA 10.76mA 3.05mA
0.30 9.09mA 15.39mA 4.42mA
0.40 11.60mA 19.48mA 5.68mA
0.50 13.82mA 23.02mA 6.82mA
0.60 15.77mA 26.01mA 7.85mA
0.70 17.44mA 28.45mA 8.76mA
0.80 18.83mA 30.37mA 9.55mA
0.90 19.96mA 31.78mA 10.24mA
1.00 20.82mA 32.81mA 10.80mA
1.10 21.46mA 33.66mA 11.26mA
1.20 21.97mA 34.34mA 11.60mA
Notes: Ground clamp and pulldown seem to be the same data.

## Slide 29: 789_out
[POWER_clamp]
| voltage I(typ) I(min) I(max)
|
-3.30 3.17uA 4.49uA 2.35uA
-3.20 3.16uA 4.46uA 2.33uA
-3.10 3.16uA 4.45uA 2.31uA
-3.00 3.15uA 4.43uA 2.29uA
-2.90 3.14uA 4.42uA 2.28uA
-2.80 3.14uA 4.41uA 2.27uA
-2.70 3.13uA 4.40uA 2.25uA
-2.60 3.13uA 4.39uA 2.24uA
-2.50 3.12uA 4.38uA 2.23uA
-2.40 3.12uA 4.37uA 2.22uA
-2.30 3.11uA 4.37uA 2.21uA
-2.20 3.11uA 4.36uA 2.20uA
-1.30 3.08uA 4.32uA 2.12uA
-1.20 3.07uA 4.32uA 2.12uA
-1.10 3.07uA 4.31uA 2.11uA
-1.00 3.07uA 4.31uA 2.11uA
-0.90 3.06uA 4.31uA 2.10uA
-0.80 3.06uA 4.30uA 2.09uA
-0.70 3.06uA 4.30uA 2.09uA
-0.60 3.05uA 4.30uA 2.08uA
-0.50 3.05uA 4.29uA 2.07uA
-0.40 3.05uA 4.29uA 2.07uA
-0.30 3.04uA 4.28uA 2.06uA
-0.20 3.04uA 4.28uA 2.06uA
-0.10 3.04uA 4.28uA 2.05uA
0.00 3.03uA 4.27uA 2.04uA

## Slide 30: 789_out
[Ramp]
| variable typ min max
dV/dt_r 705.00m/331.03p 923.40m/209.06p 492.66m/571.48p
dV/dt_f 700.80m/700.00p 1.08/400.00p 379.20m/800.00p
|
[Rising Waveform]
R_fixture = 50.00
V_fixture = 0.00
| time V(typ) V(min) V(max)
|
0.00S 0.00V 0.00V 0.00V
200.00pS 278.54uV -119.46uV -6.89uV
400.00pS -9.53mV -38.20mV 690.25uV
600.00pS -31.53mV 307.20mV -13.37mV
800.00pS 21.79mV 1.17V -32.68mV
1.00nS 448.43mV 1.47V -18.43mV
1.20nS 885.60mV 1.54V -3.51mV
1.40nS 1.05V 1.54V 73.24mV
1.60nS 1.14V 1.54V 264.40mV
1.80nS 1.16V 1.54V 457.35mV
2.00nS 1.17V 1.54V 612.75mV
2.20nS 1.17V 1.54V 712.00mV
2.40nS 1.17V 1.54V 765.20mV
2.60nS 1.18V 1.54V 792.30mV
2.80nS 1.18V 1.54V 807.40mV
3.00nS 1.18V 1.54V 813.40mV
10.00nS 1.18V 1.54V 821.10mV
Notes: The dt values for the fall are suspicious

## Slide 31: 789_out
[Falling Waveform]
R_fixture = 50.00
V_fixture = 3.30
| time V(typ) V(min) V(max)
|
0.00S 3.30V 3.30V 3.30V
200.00pS 3.30V 3.30V 3.30V
400.00pS 3.30V 3.30V 3.30V
600.00pS 3.30V 2.93V 3.30V
800.00pS 3.20V 2.35V 3.30V
1.00nS 2.82V 1.90V 3.30V
1.20nS 2.57V 1.68V 3.30V
1.40nS 2.48V 1.61V 3.19V
1.60nS 2.34V 1.57V 3.05V
1.80nS 2.23V 1.54V 2.94V
2.00nS 2.18V 1.53V 2.85V
2.20nS 2.16V 1.53V 2.78V
2.40nS 2.15V 1.52V 2.74V
2.60nS 2.14V 1.52V 2.72V
2.80nS 2.14V 1.52V 2.70V
3.00nS 2.13V 1.52V 2.69V
|
10.00nS 2.13V 1.52V 2.67V

## Slide 32: 789_out
[Model] Input1
Model_type Output
Polarity Non-Inverting
Vinl = 0.00V
Vinh = 3.30V
C_comp 472.00fF 615.00fF 352.00fF
|
[Temperature Range] 25.00 -40.00 150.00
[Voltage Range] 3.30V 3.46V 3.13V
[Pulldown]
| voltage I(typ) I(min) I(max)
|
-3.30 -0.00A -0.00A -0.00A
-3.10 -0.00A -0.00A -0.00A
-2.90 -0.00A -0.00A -0.00A
0.20 -0.00A -0.00A -0.00A
0.30 -0.00A -0.00A -0.00A
0.40 -0.00A -0.00A -0.00A
0.50 -0.00A -0.00A -0.00A
5.40 -0.00A -0.00A -0.00A
5.60 -0.00A -0.00A -0.00A
5.80 -0.00A -0.00A -0.00A
6.00 -0.00A -0.00A -0.00A
6.20 -0.00A -0.00A -0.00A
Notes: The pin that was defined as an input is modeled as an output. Vinl and Vinh are not realistic. The min/typ/max definitions are wrong. A very weak driver to say the least.

## Slide 33: 789_out
[Pullup]
| voltage I(typ) I(min) I(max)
|
-3.30 -0.00A -0.00A -0.00A
-3.10 -0.00A -0.00A -0.00A
-2.90 -0.00A -0.00A -0.00A
0.20 -0.00A -0.00A -0.00A
0.30 -0.00A -0.00A -0.00A
0.40 -0.00A -0.00A -0.00A
0.50 -0.00A -0.00A -0.00A
5.60 -0.00A -0.00A -0.00A
5.80 -0.00A -0.00A -0.00A
6.00 -0.00A -0.00A -0.00A
6.20 -0.00A -0.00A -0.00A
[Ramp]
| variable typ min max
dV/dt_r 0.00/0.00 0.00/0.00 0.00/0.00
dV/dt_f 0.00/0.00 0.00/0.00 0.00/0.00
|
| End [Model] Input1
Notes: A very weak pullup with consistent dV/dT’s

## Slide 34: 789
Status
  Contacted Vendor
  No reply

## Slide 35: Conclusions
We need to do a better job of making models
We need to do a much better job of QC’ing models before they are released