## Slide 1: PROPOSED NEW DIRECTIONS FOR IBIS PCB SIGNAL INTEGRITY MODELS
Ian C Dodd

## Slide 2: IBIS: I/O Buffer Information Specification
Machine-readable analog behavioral description of:
  digital integrated circuit I/Os.
  terminators
  packages and simple electrical modules
Primary target is PCB interconnect simulation
Core of present I/O buffer model is tabular I/V and V/T curve data derived from measurement or full circuit simulation.

## Slide 3: Brief IBIS History
1992 Intel invited Cadence and other EDA vendors to define a common behavioral modeling language
1993 IBIS 1.0 released, Open Forum established.
1995 IBIS Open Forum affiliated with EIA, IBIS 2.1 approved as ANSI/EIA-656
1999 IBIS 3.2 approved as ANSI/EIA-656A

## Slide 4: IBIS Major Feature Additions
IBIS 1.0
  I/V Curve Data, simple Rise and Fall Times
IBIS 2.1
  V/T Curve Data
  Delay measurement specifications
  Package model
  Differential logic support, supply pin mapping
IBIS 3.2
  Series elements, driver scheduling, bus hold and lots more!

## Slide 5: IBIS modeling advantages
Simulations are faster than for equivalent structural models.
Majority of present day devices can be accurately modeled.
Data sheet style description.
Intellectual property is protected.
Adopted by all the major EDA vendors.
Many Semiconductor vendors routinely provide IBIS models for new products.

## Slide 6: IBIS limitations
Feature changes require new keywords to be debated, agreed upon and ratified through the international standards process
Rate of requests for feature changes is accelerating.
Models assume a fixed circuit topology.
Present accuracy is inadequate for today's needs in:
  input transition detection
  simultaneous switching noise
  power delivery.
  coupling within packages and more!

## Slide 7: Goals for the next generation of IBIS
Provide an extensible syntax so new technologies and requirements can be supported without changing the standard.
Allow the advanced model creator to define the model’s structural topology and parameters
Support equation based modeling in addition to tables
Maintain backward compatibility with previous IBIS versions
Support public key encryption
Secondary Goal
  Allow HTML compatibility so text can be formatted and pictures, graphs and diagrams can be included in comments.

## Slide 8: IBIS-X the proposed next generation
Extend the data sheet
  remove requirement limiting keywords to those defined in the standard
  Allow each data point to have an arbitrary number of values rather than the three representing typical, minimum and maximum in the present standard
Add a new structure template

## Slide 9: The IBIS-X structure template
Is created by the advanced modeler and is used for many devices by customizing the data section.
Defines the structural topology of the simulation model
  SPICE style nodal description
  flexible set of behavioral simulation elements
  macro language for creating model prototypes
Maps the keyword specified data file entries to parameters on elements in the model structure.
Maps the sets of values for data points to process, temperature and other simulation user specified conditions

## Slide 10: Example of IBIS-X Data Section
[Model] switchout
Model_type Terminator
| variable typ min max
C_comp 1pF NA NA
[Temperature Range] 25 0 100
[Voltage Range] 5.0 4.75 5.25
[Rac] 1k NA NA
[Cac] 0.5pF NA NA

## Slide 11: Example of IBIS-X Circuit Topology
[Define Model] Terminator
.inherit model_base
.node t1
resistor Rac (pin t1) R = [Rac] || short
capacitor Cac (t1 gnd) C = [Cac] || open
resistor Rpwr (pin power_clamp_ref) R = [Rpower] || open
resistor Rgnd (pin gnd_clamp_ref) R = [Rgnd] || open
[End Define Model]

## Slide 12: Circuit Elements
Basic Elements: resistors, capacitors, inductors.
Equation controlled sources
Piecewise linear table driven sources
Advanced transmission lines: RLGC = function (frequency)
Triggers: detect threshold transitions
Alarms: report violations
Heritage behavioral drivers and loads

## Slide 13: Proposed HTML compatible IBIS/IBIS-X
Originally proposed as a IBIS 4.0 feature.
Feature only activated for documents with a HTML declaration at the start of the file
Lines with “<“ in column one are assumed to be HTML formatting commands to be ignored by IBIS parser.
Machine readable text can be displayed with full formatting
Graphics can be incorporated into comments. Allows:
  Schematic symbols
  connector pinout diagrams

## Slide 14: HTML compatible IBIS Example
Graphics from HTML IBIS example go here

## Slide 15: Source for HTML IBIS Example
Source for HTML IBIS example goes here

## Slide 16: IBIS-X Advantages
IBIS-X meets the goal of being inherently extensible.
Partitioning IBIS into a structure template and a data section separates of the re-usable portion of the model from that which is specific to a device.
The partitioning also separates out the data sheet which should be relatively easy to populate from the structure template which may require advanced modeling skills

## Slide 17: IBIS-X Advantages (continued)
Devices in a wide range of logic families should be able to share the same structure template.
An appropriate template will allow existing IBIS models to be read by IBIS-X tools.
Nodal structure allows multiple levels of abstraction.

## Slide 18: IBIS-X Concerns
A high degree of expertise and specialization will be required to create new IBIS-X structure templates.
Model developers will have to be trained to create more than one type of data sheet
Simulation tools will have to be much more intelligent in their model syntax checking.
The task of model validation will be more difficult than at present

## Slide 19: Further IBIS-X Work
At first stage of the definition process
  Formal specification is now being created
  Target date has yet to be set for full Open Forum review
Concerns of what level of abstraction to use for basic building blocks:
  SPICE primitive, controlled voltage and current sources
  Nodal charge, flux equations
Can more work from existing analog behavioral standards be incorporated into this proposal
Can XML methodology be adopted for the data section?

## Slide 20: Conclusions
The IBIS-X proposal represents a promising way to move the task of defining the simulation model data sheet from the standards committee to the expert user.
IBIS-X support will require an increase in the sophistication of validation tools and increased training for model developers.

## Slide 21: Acknowledgements
The IBIS Open Forum continues to provide technological innovation for the mutual benefit of EDA customers, EDA vendors and IC manufacturers

## Slide 22: IBIS Open Forum: Futures Subcommittee
Cadence: Ian Dodd, (Mike LaBonte - no longer active)
IBM: Michael Cohen
InnovEDA: John Angulo
Independent: Al Davis
Intel: Arpad Muranyi, Stephen Peters.
Mentor Graphics: Bob Ross
Texas Instruments: Stephen Nolan