## Slide 1: IBIS Futures Group Update on IBIS-X
Stephen Peters,
Intel Corp.

## Slide 2: IBIS Futures Committee Members
Cadence: Ian Dodd
IBM: Michael Cohen
InnovEDA: John Angulo
Independent: Al Davis
Intel: Arpad Muranyi, Stephen Peters (chair).
Mentor Graphics: Bob Ross
Texas Instruments: Stephen Nolan

## Slide 3: Goals of IBIS-X
Provide extensible syntax
  Support for new technologies/requirements without constantly changing the standard
Enable complex/coupled package descriptions
  Support pwr delivery, coupled pins, gnd bounce, etc.
Maintain backwards compatibility
  Enable reuse of current 3.2 models
Additional Requirements (since inception of project)
  Support for equation based modeling
  Allow HTML viewing of .ibs files
  Support for public key encryption

## Slide 4: IBIS-X in a Nutshell…
Provides a nodal based pkg description
  die interconnect (pad <-> pin) descriptions
  power delivery and pin-pin coupling
Provides a macro language for creating new model types
  flexible, extendable, allows existing IBIS models to be reused
  enables a wide variety of descriptions
Bottom Line: user will have the ability to create his/her own custom buffer (model_type), then specify a pkg model in a standard format.

## Slide 5: Current IBIS-X Status
IBIS 3.2 has been implemented in IBIS macro lang.
  See Al Davis for presentation on IBIS-X parser
Working group meets bi-weekly to work on writing formal spec(s)
  Overall IBIS-X spec – see handout for sample
  Library guide
  Programmers LRM (next couple of months)
Much work remains on die interconnect section
  Need for additional volunteers

## Slide 6: Some Current Issues
Alignment with Connector Spec
  changes required in header section to make both the same
Case Sensitivity in .ibs files
  Currently case sensitive.
  Need to create rules for capitalization.
How best to support HTML viewing of .ibs files
When to support general equations & black boxes (I.e. Berkley ‘B-element’)
  On first release? Subsequent release?
How does API fit into all this?