## Slide 1
Lossy Line Characterization and Modeling for SPICE and IBIS
Steve Corey
TDA Systems, Inc.

## Slide 2: In This Talk...
Examples of loss
Why loss matters
Physical basis for loss
Modeling approaches
Loss modeling issues
Our approach
Results
Conclusions

## Slide 3: Loss Example: Time Domain

## Slide 4: Loss Example: Frequency Domain

## Slide 5: Why Loss Matters
Ignoring loss can cause design failures
  Data rates too high
  Drivers too weak
Overestimating loss can result in overly conservative designs
  Slower than necessary
  Stronger drive than necessary

## Slide 6: Why Loss is a “Recent” Issue
Loss is only recently significant in common digital design
  Faster rise times and data rates
  Narrower traces
  Same old materials…
Loss has long been significant in analog design
  Frequency-Domain analysis methods
  Not targeted toward broadband modeling

## Slide 7: Physical Basis for Loss
Resistance in metal
  Varying skin depth causes frequency-dependent resistance
  Magnetic flux internal to metal causes frequency-dependent inductance
Conductance in dielectric
  Constant non-zero loss tangent causes frequency-dependent conductance
  Charges moving within dielectric cause frequency-dependent capacitance

## Slide 8: Different TEM Modeling Approaches
Lumped
  Defined for all frequencies
  Slow for long lines
Distributed
  Based on parameters (Rskin, Gdielectric)
    Defined for all frequencies
    Not as general
  Based on RLGC data
    General for quasi-TEM
    Not defined for all frequencies

## Slide 9: Loss Modeling Issues
Accuracy of model
  Defined for sufficient range of frequencies
Passivity of model
  Cannot generate energy
  Required for use in a time-domain simulator which handles feedback
  Requires model to be causal
Stability of algorithm
  Unstable algorithms can cause passive models to blow up

## Slide 10: Causality in TEM Models
From basic physics, the real and imaginary parts of the dielectric constant are tightly related to ensure causality.
The same is true of the permeability constant, 
In TEM modeling, this means that R and L are related, and G and C are related
Models based on RLGC data should address this issue

## Slide 11: Our Model Extraction Approach
Assume equations:
Extract/Optimize loss parameters: Rdc, Rac, Gdc, Gac, L, C
Write resulting model in various formats
  Lumped
  Distributed with parameters
  Distributed with RLGC data

## Slide 12: Example: Extraction Results

## Slide 13: Example: Lumped Simulation Results

## Slide 14: Example: Parameterized Simulation Results

## Slide 15: Example: RLGC Data Simulation Results

## Slide 16: Conclusions
Industry needs lossy line models for board-level simulation
The capability exists for accurate modeling
  Lumped elements, parameters, RLGC data
  Our modeling approach is based on TDR measurements
Care is required to ensure that models are physical and algorithms are stable