## Slide 1
EMI Parameters for IBIS
Guy de Burgh
DesignCon 2002

## Slide 2: Introduction
This is part 2 (of 2).
  Part 1 was given at DAC 2001.
EMI is too complicated for today’s computers to simulate.
  You can use a Cray and simulate for 10 years, but engineers (and companies) want answers sooner than that, preferably within a few minutes. So some assumptions are necessary.
Use easily obtainable parameters.
  Want IC vendors and users to be able to create models easily and quickly.
All the parameters are optional.
  The more you have the better the analysis.
  Some are more important than others.
<number>

## Slide 3: Radiation Modes
Differential Mode
On surface layers, the current loop formed by the signal trace and its associated return path will radiate as a loop antenna.
On surface layers, the return current on a return plane due to a signal current induces a ground voltage differential across the return plane. This noise voltage will drive external cables.
Current-Driven Common Mode
High frequency voltages on an I/O trace due to X-talk or the I/O signal itself drive the off-board signal wire against GND/PWR plane of a board.
Voltage-Driven Common Mode

## Slide 4: EMI Mechanisms
Differential Mode
  Direct radiation from signal loops.
Current-Driven Common Mode
  Signal return currents create noise voltages across finite return planes that drive attached cables.
Voltage-Driven Common Mode
  Signal voltages and noise voltages due to crosstalk drive attached cables.
Power Bus
  Digital switching creates power bus noise.
Heatsinks
  Act as antennas driven by potential differences on the return plane.
Crosstalk
  Coupling among nearby traces.
Immunity
  ESD, Magnetic and Electric Field Susceptibility.
<number>

## Slide 5: Differential Mode
The differential mode EMI from a net is estimated based on the far field approximation as follows:
where I is current, f is frequency, l is trace length, s is signal return distance, and r is antenna distance.

## Slide 6: References
[1] J.L. Drewniak, T.H. Hubing, and T.P. Van Doren, “Investigation of Fundamental Mechanisms of Common-Mode Radiation from Printed Circuit Boards with Attached Cables,” Proceedings of the 1994 IEEE International Symposium on Electromagnetic Compatibility, Chicago, IL, August 1994, pp. 110-115.
[2] C.R. Paul, Introduction to Electromagnetic Compatibility, John Wiley Interscience, New York (1992).
[3] D.M. Hockanson, J.L. Drewniak, T.H. Hubing, T.P. Van Doren, F. Sha, C.-W. Lam, and L. Rubin, “Quantifying EMI Noise Sources Resulting from Finite-Impedance Reference Planes,” IEEE Transactions on Electromagnetic Compatibility, vol. EMC-39, no. 4, November 1997, pp. 286-297.
[4] C.R. Paul, “Printed Circuit Board EMC.”, 6th Symposium on EMC, Zurich, March 1985.
[5] H.W. Ott, Noise Reduction Techniques in Electronic Systems, 2nd Edition, John Wiley Interscience, New York (1988).

## Slide 7: Proposed (additional) EMI parameters
Component
  Voltage Range Describes the voltage range of a driver (or bi-directional output). Note that these voltages are not necessarily the same as the power rails. E.g. for ECL the power rails are 0V and 3.3V, but the voltage range is 1.625V to 2.375V.
  Component Type Indicates whether the component is a connector.
  Domain Defines whether the component is Analog, Digital or both.
  Family Describes the logic family. This can be one of UNDEF, TTL, CMOS or ECL.
Model
  Ferrite Indicates that the model for this pin is a ferrite.
<number>

## Slide 8: Examples
Example 1 [Component EMI] Voltage_range 1.625 2.375 Component_type Active Domain Digital Family ECL Cpd 6.4pF
Example 2 [Pin EMI] 1 shielded 4 type37 [Model EMI] type37 Model_emi_type Ferrite
<number>

## Slide 9: What’s next?
Prepare a more detailed specification
  Need to add more details as to why these parameters are important.
  How to measure, and where to find, the parameters.
Submit a Bird
  Currently in preparation.
<number>