## Slide 1: JEITA EDA Activity and Proposal
January 28, 2002
IBIS SUMMIT at Santa Clara
Atsuji Ito
Panasonic
pan00570@pas.mei.co.jp
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2
Today’s Presenter (JEITA/EDA WG member)
A.Ito Panasonic
Title：JEITA EDA activity and Proposal
T.Horigme SHINDENGEN
Title：To be model of Circuit Simulation
Y.Fujishiro TDK
Title：Proposal of Standardization of
Passive components model
Contents(A.Ito)
1. JEITA EDA Activity
2. IBIS in the Digital Consumer Appliance
3. Proposal for Joint Activity

## Slide 3
JEITA EDA Activity

## Slide 4
Promotion Organization
Board of Directors
ECALS Steering Committee
CALS/EC Promotion Office
Member: 85 companies
Organized 3 technical committees and 6 working groups
Technical Committee for Standardization
Technical Committee for
Utilization
Technical Committee for
Electronic Equipment CALS
Dictionary Standards WG
EDA Standards WG
Business Process WG
Data Exchange WG
Promotion WG
Data Set Standards WG
The Electronic Industries Association of Japan(EIAJ) and
Japan Electronic Industry Development Association (JEIDA)
merged effective November 1, 2000, to enter the 21 century as the
Japan Electronics and Information Technology Industries Association (JEITA).
Notes: 以上のような枠組みを決定し、推進している組織がＥＣＡＬＳ委員会であります。ごらんのようにＥＣＡＬＳ委員会の傘下に標準化と実用化の二つの専門委員会を設置しています。

## Slide 5: Issues and Needs in Catalog Data Distribution
■Semiconductors and Electronic Components
Issues
Needs
■Access to latest information and avoiding information access based on specified format
■Increase homepage access
■Minimize risks in providing own data
■Data request in specific format ,per need, such as design, procurement, etc.
■Limitations in homepage access
■Apprehensions over data use after access
Access to own company data and standardization
■Electronics equipment company
Issues
Needs
■Information access in vendor-specific format
■Burgeoning websites
■Data for viewing only; obsolete data
■Cost of data re-entry in own database
■Access to latest data on new components,
or discontinued parts, etc.
■Reduce re-entry steps in own database
■Computer-based automatic search, sharing
■Direct use of vendor data
Standardization and digitalization

## Slide 6
Standardization of dictionary for catalog data development
Standardization of data distribution
Promoting commercialization
Use of project achievements in commercialization
Promote business application
Companies to provide commercialization service to be recruited
from JEITA members
Elaborating on international standards for business applications
Development of content use guidelines for Internet distribution
Direction of Solution for ECALS

## Slide 7: Activities of the ECALS Steering Committee
Disclosure of ECALS Dictionary Version 1
Catalog content disclosure exceeds 246,000
■Version 1 of the IEC-compliant dictionary disclosure at website from April 2001.
■Terms for catalog data and content distribution based on ECALS standards
to be established. Contents disclosures: 246,000 (as of December 2001)
Future Plans
Expansion of standardization effort
■Expansion of ECALS dictionary and promote wider
■Expansion into EDA (electronic design automation)
■Greater coordination in standardization with overseas organizations
Commercialization activities
■Standardization of business processes and of corresponding data exchanges
■Promote wider use of ECALS catalog data
■Development and standardization of all B-to-B processes through
coordination with EDI Center

## Slide 8
JEITA Website
URL: http://www.e-parts.org
＊Opened in June 2000 to promote ECALS commercialization effort
URL: http://www.jeita.or.jp/

## Slide 9: EDA WG Activity
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
Investigation & Discussion on SI/EMI Simulation Models
EDA WG Activity
Term
April 2001 ~ March 2002
Applications
Digital Consumer Appliance
Activity
Members
Purpose
Discussion meeting between Users and Providers
for EDA Simulation model of Non-IC Components
Appliance & Components company Total:8
Matsushita, Mitsubishi , SHINDENGEN,TDK,Murata etc

## Slide 11
2. Efforts must be made to expedite format standardization
as well as to expand the range of application.(Included Board level )
Active together with EIA/IBIS Open forum
Not only semiconductor but also non- semiconductor devices
Conclusion of Discussion Meeting
ー Take a Step Forward ー
3. To be supported by EDA tools.
CAD and Simulation tools & Easy to use
1. Most important issue for users is to get new device models timely.
Any data format (IBIS,SPICE etc) is acceptable.
Just in time in design process & Create distribution channel

## Slide 12: IBIS in the Digital Consumer Appliance

## Slide 13
Digital Network Consumer Appliance
Digital Network Appliance
Pentium
Windows
Mobile , Game
Mobile Phone、PDA、PS2
DTV
DVD、VTR
P C
TV.VTR etc
Internet
Network
Digital Network
家電（ＡＶ機器）
Computer
Mobile
communication
Digital AV Equipment
Game
Internet TV
TV
PC・
Multi-Media Terminal
DIGITAL TV
Mobile Phone
etc
Broadcasting
Consumer Appliance
AV Equipment
Computer
Communication
From Now
Fusion Appliance : PC ＋ AV equipment ＋ Mobile
Simulation using EDA Model is important for Design.
Digital Appliance
Business world
Consumer electronics (AV Appliance)

## Slide 14: IBIS applications for digital consumer appliance in MEI
Current … SI simulation
  Clock line, memory bus(Rambus), LVDS, …
    Signal quality, timing, cross talk
    Evaluate dumping resistor value
    Make design rule
Future (or just start trial) … PI, EMC
  Power/GND bounce, SSO noise, optimize decoupling capacitors
  EMI noise

## Slide 15: Current issues concerning SI simulation (1)
IBIS availability
  ASIC, Gate Array: sometimes not available in early development stage
    Cannot use floor planning simulation
  Connector, filter, passive discrete components model: not IBIS (of course!)
    SI Simulation tools are not always support SPICE model or S-parameter itself. So we need some conversion or modification to such models, or use SPICE for SI simulation.
  File quality: sometimes has even syntax error.
    Monotonous I-V curves
    Inaccurate package model value
    Bad waveform data
Only post simulation
Use similar model

## Slide 16: Current issues concerning SI simulation (2)
Accuracy
  High density PCB’s Power/GND plane is not ideal
    Severe, unexpected condition for LSI operation ≠ IBIS model condition
    Typ/min/max condition in IBIS is not always suitable to real board
    Difficult to model the non-ideal plane
  Accuracy of IBIS file itself
    Monotonous I-V curves, bad package parameter, bad waveform
    Sometimes need modification to the files
  IBIS treatment in the simulators seems different
    Simulation results are sometimes different from simulator A and B

## Slide 17: IBIS Simulation (currently trying)
RDRAM data line
RDRAM receiver
Terminator →39Ω
RAC driver
Measured net
IBIS model is not optimized
(Just created from SPICE model)
Real Chip can change driver strength, but SPICE model can’t do it

## Slide 18: IBIS v.s. SPICE (1)
Test board conditions
  Driver & receiver: Philips 74ALVT16245
  Connector: AMP FH connector,(SPICE model is supplied by AMP)
  Transmission line: HSPICE W-element, SI tool X’s tline model (Power/GND is ideal)

## Slide 19: IBIS v.s. SPICE (2)
Test board schematics
W1 ・0.125mm ・l = 4.16mm
74ALVT16245
Driver
Dumping Resistor
82Ω
74ALVT16245Receiver
Connector
W2 ・0.125mm ・l = 76.36mm
W3 ・0.125mm ・l = 66.35mm
Probe model
Measurement point

## Slide 20: IBIS v.s. SPICE (3)
Simulation conditions
HSPICE model
IBIS model
HSPICE
SI tool X
Driver & Receiver
HSPICE
W-element
Tline model
Connector
SPICE model

## Slide 21: IBIS v.s. SPICE (4)
Results
  Not so serious difference, but …
t
IBIS accuracy?
IBIS treatment of each tools?

## Slide 22: Proposal to IBIS
Specify not only data description but also more kind of data conditions to increase accuracy
  Sometimes IBIS data conditions(R_fixture, R_load, …) are different from real application use
To obtain more high file quality
  Standard IBIS generation tool for the component manufacturer, or IBIS user(not only syntax check, but also data accuracy)
More challenge
  New data description or structure for PI/EMI simulation
Include passive component description into IBIS
  If all component models on the PCB become IBIS, simulators become more smart

## Slide 23
Proposal
for
Joint Activity

## Slide 24
Joint Activity
with
IBIS Open Forum and JEITA EDA-WG
1. High speed Digital board design is the most important for Digital network
appliance,DTV,DVD and Mobile etc.
LSI, Module,Connector, PKG and Passive components are on Board.
(System Board)
2．Board level simulation is necessary to reduce the design time&cost.
Device model standardization including Passive components are
necessary for it.
Suggestion:
We suggest you to cooperate together between IBIS Open forum and JEITA/EDA WG for IBIS-X or New IBIS standardization including Passive components.

## Slide 25
For New
IBIS Standard
Joint Activity

## Slide 26
IBIS: A national bird in Japan

## Slide 27
Thank you very much
for
your Attention
Japan Electronics and Information Technology Industries Association
and
Panasonic