## Slide 1: Signal Integrity Software, Inc.
Barry Katz
Daniel Nilsson

## Slide 3: The Bitter-Sweet Experiences of using IBIS Models

## Slide 4: High-Speed Design Challenges
On Board Data Rates
  Commonly 133MHz - 500MHz; moving to 1GHz+
Detailed Signal Integrity and Timing analysis required
  Must simulate over Process, Voltage, and Temperature
  Inter Symbol Interference
  Simultaneous Switching Output Noise and Crosstalk
  Pre-Layout Solution Space analysis
  Post-Layout Verification
Large number of simulations required

## Slide 5: IBIS Benefits
Performance
  10 -100x faster than transistor level models
Encapsulates large amount of information for
  Waveform analysis
  Timing Analysis
  System Verification
Can be as accurate as transistor level models
No proprietary transistor level information

## Slide 6: Generating good models is hard
Requires significant effort
  Correctly converting transistor level models to IBIS is a complicated process
  Simulate transistor level and IBIS models into representative topologies
  Review I-V and V-T data
  Check results in different process corners
  Various frequencies of operation
Good models result in good correlation

## Slide 7: Hspice vs. IBIS correlation

## Slide 8: However…
Effects not currently captured by IBIS models
  Frequency dependent delays
  Delay variation as a function of slew-rate
  Signal amplitude delay variations

## Slide 9: Delay Variations

## Slide 10: Delay Variations

## Slide 11: Delay Variations, slow process

## Slide 12: Steps to Design Success using IBIS models
I/O Characterization
  Understand I/O behavior over operating conditions
Model Qualification
IBIS results needs to be correlated to transistor level simulations

## Slide 13: Conclusions
Using IBIS models allows us to run a larger solution space analysis
Creating good IBIS models requires significant effort
Using IBIS for High-Speed Interfaces requires validated and correlated models
In many cases IBIS models can be used for designing 600+ MHz interfaces