## Slide 1: Progress and Issues in IBIS-X
Stephen Peters,
Intel Corp.

## Slide 2: Current Status
IBIS Macro Language Specification is now at revision 0.6
  Basic syntax, language rules and circuit elements are defined and documented.
  Added support for describing controlled sources using equations.
  T-lines syntax & usage are now formally documented (matrixes are being documented by the connector committee).
  Focus now is on describing IBIS 3.2 buffer in IBIS-ML, “complex” buffers and BIRDS for 4.0 (see issues list for details)
The IBIS-ML parser prototyping activity is on hold (no developer)
Based on current progress, expect to see revision 1.0 of the IBIS-ML specification end of this year.

## Slide 3: Current Issues
Support for [Model Spec] type keywords
  Does model itself contain the code that checks for signal violations as documented by the [Model spec] type keywords?
  If it does, what language support is required? Do we approach it with complex circuit elements (sample-holds, triggers, etc.) or do we create a full blown programming language (if-then-else, while loops, variables, etc.)
Is ‘driver’ element good enough for the first release?
  The ‘driver’ element is a black box containing a vendors IBIS 3.2 algorithm… has inputs for I/V and V/T tables.
  Advantage: shortcut to 1.0, quick adoption by industry
  Disadvantage: not expandable, still need to do basic work to insure that approach/definition is powerful enough to model differential, etc. buffers.
Still need method for adding package models into component

## Slide 4: Plans & activities (short and mid term)
Describe IBIS 3.2 in IBIS-ML without using ‘driver’ element
Describe complex I/O in IBIS-ML
  Differential drivers and receivers
  Drivers w/pre-emphasis (SCSI, 3GIO, etc.)
  Drivers with fallback
Describe proposed IBIS 4.0 birds.