## Slide 1: IBIS Version 4.0
Bob Ross
Mentor Graphics Corporation
DesignCon 2002 IBIS Summit Meeting
Santa Clara, California
January 28, 2002

## Slide 2: Version 4.0 - 10 More BIRDs
BIRD62.6 - Receiver Threshold spec extensions
  [Receiver Thresholds] -Vinh/l_ac/dc and differential thresholds offsets from Vth, Tslew, sensitivities
  [External Reference] - External voltage reference
BIRD64.4 - [Alternate Package Models]
BIRD65.2 - C_comp split to any four voltage references
BIRD66, BIRD71 [Model Spec] additions
  11 Timing test load subparameter extensions, PCI, PCI-X support (separate rising, falling loads)
BIRD67 - 1000 V-T lines

## Slide 3: BIRDs Continued
BIRD68.1 - Clarify V-T table rising and falling edges aligned
BIRD70.5 - Golden Waveforms
  [Test Data], [Test Load], and other keywords and subparameters to define golden waveforms (near, far, single-ended, differential, typ/min/max) and general test load circuit
BIRD72.3 - PMOS/NMOS series switch models
  Extends definition of series MOSFET to PMOS, NMOS and combinations - no syntax change
BIRD73.4 - Fall Back submodel
  Adds the Fall_back submodel for AVC technology
  Clarification and corrections to Bus_hold submodel

## Slide 4: Ratification Plan
Review copy uploaded under “Ver 4.0 Work In Progress” link of IBIS home page
Committee review/vote on Version 4.0 to stabilize syntax and resolve any interaction issues
Start ibischk4 parser project - another review and possible clarification BIRDs
Committee review/vote Version 4.1
Package and submit for EIA letter ballot
  3 months review
  Respond formally to comments
If successful, ratify as ANSI/EIA-656-B