## Slide 1
<number>
Tim Coyle
Applications Engineer
Network Interface Products
IBIS Modeling Experiences

## Slide 2: Modeling LVDS
Different methods available
  IBIS Modeling of LVDS Buffers, Hazem Hegazy and Mohammed Korany, Mentor Graphics
Not every method works for every LVDS device
  Different output structures
  Use method that best works for your circuit topology
Notes: Modeling differential technology such as LVDS can be challenging. However, there are many different methods available to achieve this. A good paper is ” IBIS Modeling of LVDS Buffers”, by Hazem Hegazy and Mohammed Korany. (http://www.mentor.com/pcb/tech_papers.cfm) This paper talks about how to create an IBIS file for an internally terminated LVDS driver. But it also shows different methods to model a LVDS driver with external termination and correlation results.
Another good source is “Creating Accurate LVDS IBIS Models”, by Adam Tambone. This paper describes one method (with correlation) used by the author to successfully create an LVDS IBIS file. (http://www.commsdesign.com/design_corner/OEG20020403S0018)
From my personal experiences, which method you use will ultimately come down to the circuit implementation. The output structures for an LVDS device will vary from part to part, and some methods work better than others, depending on the circuit topology. The best approach is to keep trying different methods until good correlation is achieved.

## Slide 3: IBIS Simulators
Different simulators can give different results
  Each simulator uses it’s own algorithm to process IBIS files
Some things supported in one tool, while not in another
  Internal termination
Notes: There are several IBIS simulators that are available. Each simulator uses it’s own algorithms to process IBIS files, which can lead to small (and sometimes big) differences. There can also be small differences between simulators in the manner that transmission lines are simulated. For example, internal field solvers between different simulators can give different (though normally only slightly) impedance values for a certain structure.
While most tools do a good job of supporting the latest IBIS specification, some IBIS features are not supported by all tools. Internal termination of a differential device is not currently supported by all IBIS simulators. Advanced package models are not supported by some simulators.
Most IBIS simulators are adequate for simulations. Certain tools have certain limitations, as is the case for all software tools.

## Slide 4: Differences Between Simulators
IBIS Simulator 1
IBIS Simulator 2
IBIS Simulator 3
Original SPICE
Notes: Different IBIS simulators can give different results. In this slide, a LVDS-LVDS repeater IBIS file was used with only a differential load resistor at 12.5 MHz. The same topology was used in three different IBIS simulators, and compared to the original SPICE model file. The slide shows a close-up of the Voh levels of one of the LVDS outputs. The IBIS file can vary as much as 10mV from the original SPICE model file. However, with a nominal VOD of 350mV this is less than a 3% error. The only difference is the simulators.
I have seen this occur with other LVDS IBIS files that I have created, and it could be due to my methods of creating an IBIS file. However, I did try two different IC vendor LVDS IBIS files and saw the same differences in the Voh and Vol levels between simulators.

## Slide 5: IBIS @ 2.5 Gbps
Notes: This is a SPICE to IBIS comparison of a 2.5 Gbps LVDS-LVDS Repeater. (Blue signal is IBIS, red signal is SPICE) The LVDS driver is driving a couple of inches of lossy microstrip with a 100 Ohm termination into a LVDS receiver. A K28.5 pattern was used as the input. The data rate was 2.5 Gbps (a bit width of 400psec). The SPICE simulator was HSPICE and the IBIS simulator was Signal Explorer. The eye opening and the jitter were almost the same for both the SPICE and IBIS simulation.
The question that always arises about IBIS is “ at up to what speed is IBIS valid?”
Some people would say 500 MHz, some people would say 1.5 GHz, and some people would say there are no limitations of IBIS.
IBIS should be adequate for multi-gigabit simulations, including complex topologies such as backplanes, to determine most signal integrity issues.
For issues such as ground bounce, IBIS may not be the best choice, due to that most IBIS simulators don’t handle (or even support) ground bounce simulations as well as other simulation tools.
Whether to model a high-speed device using IBIS should be based upon knowledge of circuit topology. Knowing the structure of the buffer, a model maker can decide if IBIS can adequately model the device or not.

## Slide 6: Some Issues of the Model Maker
Model works in one tool, but not in another one
The “feared” AC and DC mismatch warning
Simulation does not look the same as bench measurement
Notes: A model maker faces many challenges when supporting IBIS files.
One always difficult issue is when an IBIS file works as expected in one simulator, and does not work as expected in another simulator. Most of the time, this is due to simulator specific issues, such as having too long of a V-T window not working in a particular simulator.
The AC and DC endpoint mismatch is probably the most common IBIS warning or error. If an IBIS file created properly, then there should be no mismatch. However, a less than 2% difference should not impact your overall accuracy for most simulations.
Trying to correlate simulations to a customer’s bench setup is always challenging. A lot of detail about the bench setup is necessary in order to match the results. Often times components of the system are not modeled, such as the package. Other times the same values are not used in the simulation environment as the bench environment such as trace impedances. Always check the IBIS file, but remember other components in system as well.

## Slide 7: Packaging
Lumped RLC at 2.5 Gbps?
IBIS supports advance packaging
  Can include full RLC matrix w/coupling
Most IBIS simulators don’t support advance packaging
  Often have to create separate package model specific to simulation tool
Notes: As devices get faster, there is a need to pay more attention to packages. IBIS offers a way to include advance packages. Most simulators don’t support advance packages, so you have to create a separate package specific to a simulation tool.

## Slide 8: Accuracy
Working on providing Accuracy Report for every new IBIS file created
  Most model makers validate model before releasing, need to document and distribute
  Base on old Accuracy Specification and new Quality Group work
How do you validate a model that will be used in multiple tools?
  Pick a metric and go with it
  Goal of 90%, shoot for 95%
Notes: There is a need to provide documentation for IBIS files. The accuracy of the IBIS file and the logistics of testing the file need to be disclosed. However, it is difficult to come up with a solution with so many different simulators. Some simulators support some functions. There can also be a difference in results between simulators.

## Slide 9: VHDL-AMS
Is VHDL-AMS the future of IBIS?
Recently passed Bird will include use of external VHDL-AMS models
VHDL-AMS superset of VHDL that allows advanced behavioral modeling
  Ex. Use equations to describe buffer
Notes: VHDL-AMS allows analog mixed signal simulation. As circuit topologies increase in complexity, VHDL-AMS can offer an alternative way to model the circuit.

## Slide 10: National Semiconductor Modeling Resource Webpage
Coming Soon!
New webpage dedicated to IBIS and modeling issues
  www.national.com/appinfo/lvds/ibis_home
Notes: National Semiconductor has created a new IBIS and modeling webpage. Here IBIS files, as well as other simulator specific models such as Quad and DML, can be downloaded. Papers related to IBIS modeling available as well.