## Slide 1
IBIS Interconnect Specification (ICM):
Status and Proposed Changes
By
Kelly Green, Independent Contractor
Michael Mirmak, Intel Corporation
IBIS Summit at Design Con 2003
January 27, 2003

## Slide 2: Agenda
ICM Review
  Purpose
  History
  Structure
Need for Changes in Draft 1.0
Proposed Changes
Parser Overview & Status
Next Steps
  IBIS Futures Sub-committee Review
  Open Forum Review
Future Updates
  Potential technical improvements?
Backup: Example Model Text

## Slide 3: What is ICM?
ICM = IBIS Interconnect Specification
Purpose: to establish a human-readable standard format for exchanging interconnect modeling data
  “Interconnect” can be connector, cable, PCB traces or even an IC package
  Format is designed to be:
    Consistent & easily parsed by software
    Compatible with current means of representing data
      S-parameters
      R, L, G & C matrices
      “Swaths,” trees, node lists
    IBIS-like (keyword-driven)

## Slide 4: ICM History
Initial concept developed from 1995 - 1997
  Kellee Crisafulli, Hyperlynx
  Augusto (Gus) Panella, Molex
  Others through IBIS Connector Sub-committee
Revision 0.31 issued in Jan. 1999
  Outlined in Jan. 1999 IBIS Summit
  Shift from connectors to interconnects began
Revision 0.92 issued in Nov. 1999
Revisions 0.93 - 0.99901 issued 2000 - 2002
  Added “Argument,” Even & Odd Modes, etc.
  Revised Swath treatments
  Editorial changes
Draft 1.0 released Sept. 19, 2002

## Slide 5: ICM Structure
Header Information
  [Begin Header] & [End Header] keywords
  Spec. Version
  Filename & Revision
  Date
  Source, Notes, Disclaimer & Copyright
ICM Family
  Description of model “family” or group
  List of models in the “family”

## Slide 6: ICM Structure (continued)
ICM Model Description
  Type (SLM, S-parameter, MLM_*, etc.)
  Signal-to-ground ratio & (optionally) reference Z
  Tree Path Description
    Links groups of signals through cascaded “sections” of model data
    Intended to describe one-to-one connections between sections and ports or endpoints of the interconnect
    Allows “forks” with same number of conductors
  Nodal Path Description
    Links sections of model data through input & output nodes per section
    Connections need not be one-to-one
      Allows internal “dangling nodes”
  Note that Nodal and Tree Path Descriptions are mutually exclusive

## Slide 7: ICM Structure (continued)
Additional ICM Constructs
  ICM Pin Map
    Maps connector pins to Tree Path Descriptions
  ICM Node Map
    Maps connector pins to Nodal Path Descriptions
  ICM Section
    Data block for model sections
    Data is in RLGC matrix or s-parameter format
      Matrices include self-inductance, capacitance, conductance, loss, etc.
      Similar format to IBIS package models
    Each section is referenced by at least one Tree or Nodal Path Description

## Slide 8: ICM Structure (continued)
ICM Swath
  Allows minimal, economical description to be used for larger connectors or interconnects
    Smaller electrical parameter matrices can be repeatedly mapped over a larger structure
  Includes the [ICM Swath Description] and [ICM Swath Pin Numbers] keywords
Sample ICM model is included in Backup
  Data is taken from ICM specification examples

## Slide 9: Need for Changes in Draft 1.0
Draft 1.0 text needs improvement
  To increase readability & understanding
    Some small errors have survived revision process
    The writing style of several sections may produce confusion in readers
  To ease software parsing
    Several structures are defined in an ambiguous way and create a risk of conflicting “interpretations” by individual vendor software tools
    Some structures are not compliant with the Lex/YACC format used as the standard for creating compilers and parsers

## Slide 10: Summary of Proposed Changes
42 Proposed Changes in All
  18 Editorial Changes
    No impact to functionality of specification
    Examples
      Grammatical and spelling corrections
      Correction of keyword misuse in examples
      Inconsistent spelling: "Un-ordered“ vs. Un_ordered”
  24 Clarifications
    Provide stricter interpretation of content
    Examples
      Enforce consistent use of white space & tabs
      Enforce consistent use of “=“ with subparameters
      Allow use of non-one denominator in SGR
Technical changes to be considered only after Draft 1.0 approved by Open Forum

## Slide 11: Parser Overview & Status
ANSI C prototype in development
  Find issues with 1.0 specification EARLY
Exploiting widely available tools
  Lexical processor (FLEX) – COMPLETED
  Grammar (YACC/BISON) – IN PROGRESS
  Semantic analysis – NOT STARTED
Already operational at level of grammar
Schedule pending approval of proposed changes, but expect golden code by May
Unencumbered Open Source delivery
Realistic Test Models available?

## Slide 12: Short-Term Future
Changes to be presented to IBIS Futures Sub-committee
  Each change is numbered and can be considered and voted upon independently
  Next meeting likely in early February (shortly before IBIS Open Forum teleconference)
IBIS Open Forum Review
  New document, with changes, is presented
  Open Forum votes to approve or disapprove
  Next meetings: Feb. 14, March 7

## Slide 13: Future Improvements
Several technical issues may be considered after Draft 1.0 is approved
  Allow multiple types of data within a single [Begin ICM Model]/[End ICM Model] pair
    Example: Include S-parameter AND matrix data
  Include frequency-dependence in matrix data
    Example: Matrix parameters for 1 MHz, 100 MHz, etc.
  Allow mixed-mode S-parameters
    Example: SDC12 vs. S12 – coupled pair insertion loss is described in terms of common-mode excitation and differential response
Discussion point: on-die interconnect?

## Slide 14
Questions &
Free Discussion

## Slide 15
BACKUP

## Slide 16: ICM Example
[Begin Header]
[IBIS ICM Model Ver] 1.0
[File Name] iconm_hdi_202.icm
[File Rev] 1.0
[Date] January 20, 2003
[Source] Results from field simulation
[Notes] This is a test model only.
[Disclaimer] This information is for modeling purposes only, and is not guaranteed.
[Copyright] Copyright 2003, XYZ Corp.,
All Rights Reserved
[Support] http://www.VendorNameIbisModels.com
[Redistribution] Yes
[Redistribution Text] This file is freely redistributable.
[End Header]

## Slide 17: ICM Example (2)
[Begin ICM Family] High_Speed_Interconnect
[Manufacturer] XYZ Incorporated
[ICM Family Description]
High Density square pin connector for use on IEEE 99999 buses.
|====================================================================
[Begin ICM Model List]
| Name Mating Min_Slew_Time Image
|--------------------------------------------------------------------
HDI_202 Mated 100ps HDI_202_Mated.jpg
HDI_202_UnMatedA Unmated_side_A 100ps HDI_202_UnMatedA.jpg
HDI_202_SMT_to_Cable Mated 25ps HDI_TEST_202_Mated.jpg
HDI_202_SMT_to_ThruHole Mated 25ps HDI_202_Mated.jpg
|====================================================================

## Slide 18: ICM Example (3)
[Begin ICM Model Description]
High Density 0.1 center square pin with PCB effects
|====================================================================
[Begin ICM Model] MyModelExample3 | Has a stub fork!
ICM_Model_Type MLM
[Tree Path Description]
Model_PinMap MyModelPinMapA
Section Mult=1 SectionA
Fork
Section Mult=1 StubSection1
End_fork
Section Mult=1 SectionB
Model_PinMap MyModelPinMapB
| .
| .
[End ICM Model]

## Slide 19: ICM Example (4)
[ICM Pin Map] Baseboard_side
Pin_order = row_ordered
Num_of_columns = 4
Num_of_rows = 2
|Pin Type
A1 SIG
A2 SIG
A3 SIG
A4 SIG
B1 SIG
B2 SIG
B3 SIG
B4 SIG
[End ICM Family]

## Slide 20: ICM Example (5)
[Derivation Method] Lumped
|-----------------------------------------------------------
[Begin ICM Section] ExampleMatrix01
[Inductance Matrix] Full_matrix
[Row] 1
3.04859e-07 4.73185e-08 1.3428e-08 6.12191e-09
1.74022e-07 7.35469e-08 2.73201e-08 1.33807e-08
[Row] 2
3.04859e-07 4.73185e-08 1.3428e-08 7.35469e-08
1.74022e-07 7.35469e-08 2.73201e-08
|.
|.
|.

## Slide 21: ICM Example (6)
|The capacitance matrix has sparse coupling:
[Capacitance Matrix] Sparse_matrix
[Row] 1
1 2.48227e-10
2 -1.56651e-11
5 -9.54158e-11
6 -7.15684e-12
[Row] 2
2 2.51798e-10
3 -1.56552e-11
5 -6.85199e-12
6 -9.0486e-11
|.
|.
[End ICM Section] ExampleMatrix01
[End]